## Slide 1: Multi-STA Acknowledgment
Date: 2015-03-09
Name | Affiliation | Address | Phone | Email
Simone Merlin | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Santosh Abraham |  | 5775 Morehouse Dr. San Diego, CA, USA |  | sabraham@qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Cherian Gorge |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 1700 Technology Drive San Jose, CA 95110, USA |  | btian@qti.qualcomm.com
Menzo Wentink |  | 5775 Morehouse Dr. San Diego, CA, USA |  | mwentink@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Carlos Aldana |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | caldana@qca.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Tevfik Yucek |  | 5775 Morehouse Dr. San Diego, CA, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Tomo Adachi | Toshiba |  |  | tomo.adachi@toshiba.co.jp
Toshihisa Nabetani |  |  |  | 
Filippo Tosato |  |  |  | 
Narendar Madhavan |  |  |  | 

## Slide 2
Authors (continues):
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Mingguan Xu |  |  |  | mxu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Jie Huang |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Wookbong Lee | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | wookbong.lee@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Laurent cariou | Orange |  |  | Laurent.cariou@orange.com
Thomas Derham |  |  |  | thomas.derham@orange.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 8: Introduction
The following motion was approved at IEEE January meeting [1]
  Move to add to the TG Specification Framework document
    X.y.z The amendment shall define a mechanism for multiplexing DL acknowledgments sent in response to UL MU Transmissions
Presentation [2] proposed a basic frame exchange sequence for UL MU transmissions
In this presentation we propose a design for a ‘Multi-STAs’ Block ACK control frame to be used for acknowledging multiple STAs after UL MU PPDUs

## Slide 9: Acknowledgment options I
‘Legacy’ modes
  Immediate BA/BAR policy: STAs may use BAR to collect “single user” BAs
  Delayed BA policy: AP sends “single user” BAs to each STA sequentially. Each BA is acknowledged
Sequential BA
  AP sends a BA to each STA sequentially, without STAs’ ACK
All of the above methods cause a very large overhead
MU UL PPDU STA1-3
BA1
BAR
STA 2
BA 2
MU UL PPDU STA1-3
BA1
BA 2
ACK
BA 3
ACK
MU UL PPDU STA1-3
BA1
BA 2
BA 3
BAR
STA 3
BA 3

## Slide 10: Acknowledgment options II
BAs sent with DL OFDMA
  Overhead is reduced compared to previous options
  Duration is determined by the longest BA transmission time across users, which may be large if the BW/MCS allocated to one user is narrow/low.
  Requires the use of an HE PPDU, which has longer preamble than an 11a PPDU and is not legacy decodable (EIFS, NAV)
  Each BA includes certain redundant fields across users (TA, BA Control etc..) which could be compressed
BAs sent with DL MU MIMO
  Similar consideration as for DL OFDMA
  Only possible if CSI is available at AP. Gathering CSI from each STA just for BAs transmission would not be efficient. This mode is useful if CSI is already available (e.g. because already collected for DL MU MIMO Data transmission)
MU UL PPDU
DL OFDMA
BAs

## Slide 11: Proposed Multi-STA BA
Define a BA frame format that includes BA/ACK signaling for multiple STAs
  It can be sent in any PHY mode, including legacy 11a
    11a PPDU has a very short preamble for reduced overhead
    11a format enables NAV setting and correct EIFS behavior for legacy STAs
    11ac/ax formats can be used for higher rates/outdoor
  Amortizes the redundant fields across users
  Overhead analysis indicates this is a low overhead option (see appendix)
MU UL PPDU
M-BA

## Slide 12: Proposed Multi-STA BA frame format I
Define a multi-STA BA frame by re-using the Multi-TID BlockAck frame format with the following changes:
  Add an indication that the frame is a multi-STA BA (TBD)
  Each BA Information field can be addressed to different STAs
    B0-B10 of the Per TID Info field carry a (Partial) AID identifying the intended receiver of the BA Information field
B0-B10= AID

## Slide 13: Proposed Multi-STA BA frame format II
Allow ACK indication per STA (instead of BA)
  In a BA Info field, if B11 in the per-TID info field is set, then the BlockAck bitmap and the SC subfields are not present and this BA Info field indicates an ACK for the STA with AID indicated in the per-TID info field
B0-B10= AID
B11= ACK/BA

## Slide 14: References
[1] 802.11-15/0064r1 Consideration on UL-MU overheads
[2] 802.11-15/0365r0 UL MU procedure for 11ax system

## Slide 15: Straw Poll 1
Do you agree to add the following to the SFD:
The spec shall define a multi-STA BA frame by using the Multi-TID BlockAck frame format with the following changes:
  Add an indication that the frame is a multi-STA BA (TBD)
  Each BA Information field can be addressed to different STAs
    B0-B10 of the Per TID Info field carry a (Partial) AID identifying the intended receiver of the BA Information field
B0-B10= AID

## Slide 16: Straw Poll 2
Do you agree to add the following to the SFD:
The spec shall define a signaling in the Multi-STA BA frame that can indicate an ACK, as follows:
  If B11 in the per-TID info field is set, then the BlockAck bitmap and the SC subfields in the BA Info field are not present and this BA Info field indicates an ACK for the STA with AID indicated in the per-TID info field
  Instruction to the Editor: replace the Multi-STA BA figure from straw poll 1 with the following
B0-B10= AID
B11= ACK/BA

## Slide 17: Appendix - Overhead of BAs
Control rate per STA in SU mode [Mbps] (8 STAs) | DL FDMA BA exchange duration [us] (equal BW/Optimized split) | Multi-STA-BA duration [us]
[6 6 6 6 6 6 6 6] | 436 | 196
[6 6 6 6 24 24 24 24] | 436/228 | 196
[24 24 24 24 24 24 24 24] | 164 | 76
[6 6 6 6 48 48 48 48 ] | 436/164 | 196
[48 48 48 48 48 48 48 48] | 116 | 56
Muti-STA BA duration = SIFS + 11a preamble + (22 + N_STA*12) bytes sent at the minimum MCS across STAs
OFDMA BAs Duration = SIFS + OFDMA preamble [Assuming 52us] + (22 + 12) bytes sent at:
  Equal BW per STA: bytes transmitted at control rate / N_STAs
  Optimized: assume BW is allocated so that the rate = (min_su_rate + max_su_rate)/2 / N_STAs