## Slide 1: IEEE 802.11-IETF Liaison Report
Date: 2015-05-11
Authors:

## Slide 2: Abstract
This presentation contains the IEEE 802.11 – IETF liaison report for May 2015.

## Slide 3: IETF- IEEE 802 Liaison Activity
Joint meetings, agenda and presentations
  http://www.iab.org/activities/joint-activities/iab-ieee-coordination/
  2015-01-21 teleconference held; Next teleconference 18 June 2015
  No new 802.11 work items
  For information: https://tools.ietf.org/html/draft-baccelli-manet-multihop-communication-04 “This document describes characteristics of communication between interfaces in a multi-hop ad hoc wireless network, that protocol engineers and system analysts should be aware of when designing solutions for ad hoc networks at the IP layer”
RFC 7241, “The IEEE 802/IETF Relationship” has been published (RFC4441 update)
  https://datatracker.ietf.org/doc/rfc7241/
IEEE 802 Liaisons list is available
  http://ieee-sa.centraldesktop.com/802liaisondb/FrontPage
802 EC “IETF/IAB/IESG” 802 EC Standing Committee
  Formed March 2014, Pat Thaler as chair

## Slide 4: IETF Meetings
Meetings:
  July 19-24, 2015 – Prague
  November 1-6, 2015 – Yokahama
  April 3-8, 2016 – Buenos Aires
  July 17-22, 2016 - Berlin
http://www.ietf.org
  Newcomer training: https://www.ietf.org/edu/process-oriented-tutorials.html#newcomers
  Tutorials (process and technical); Wireless Tutorial (Donald Eastlake) : https://www.ietf.org/edu/tutorials.html

## Slide 5: Protocol to Access White Space database (paws) WG
Received request for IEEE 802.11 review of paws protocol draft document: https://datatracker.ietf.org/doc/draft-ietf-paws-protocol/
  Held IEEE 802.11 Call for Comments
  No comments received
Paws Charter and problem statement documents:
  Charter, see https://datatracker.ietf.org/wg/paws/charter/
  Problem Statement, see https://datatracker.ietf.org/doc/draft-patil-paws-problem-stmt/
  Use Cases and requirements, published as RFC 6953: https://datatracker.ietf.org/doc/rfc6953/
Update [May 2015]
  PAWS protocol document http://datatracker.ietf.org/doc/draft-ietf-paws-protocol/ sent for publication; in AUTH48 review

## Slide 6: RADEXT WG
See http://datatracker.ietf.org/wg/radext/
RADIUS Extensions
  The RADIUS Extensions Working Group will focus on extensions to the RADIUS protocol required to define extensions to the standard attribute space as well as to address cryptographic algorithm agility and use over new transports.
  In addition, RADEXT will work on RADIUS Design Guidelines and define new attributes for particular applications of authentication, authorization and accounting such as NAS management and local area network (LAN) usage.
Updates [May 2015]
  NAI document published as RFC7542, http://datatracker.ietf.org/doc/rfc7542/
  New version, submitted to IESG for publication: NAI-based Dynamic Peer Discovery for RADIUS/TLS and RADIUS/DTLS, see http://datatracker.ietf.org/doc/draft-ietf-radext-dynamic-discovery/
  RADIUS fragmentation draft, published as RFC7499, see http://datatracker.ietf.org/doc/rfc7499/
  New version of RADIUS extensions for IP Port Configuration and Reporting, see http://datatracker.ietf.org/doc/draft-ietf-radext-ip-port-radius-ext/ in WGLC

## Slide 7: Emergency Context Resolution with Internet Technologies (ECRIT)
Working Group website: http://www.ietf.org/dyn/wg/charter/ecrit-charter.html
Emergency Services
  Framework for Emergency Calling using Internet Multimedia, see http://datatracker.ietf.org/doc/rfc6443/
  Describing boundaries for Civic Addresses, see http://tools.ietf.org/id/draft-thomson-ecrit-civic-boundary-02.txt
Updates [May 2015]
  Updated: Routing Request extension for the HELD protocol, http://datatracker.ietf.org/doc/draft-ietf-ecrit-held-routing/
  Submitted to IESG for publication: Additional Data Related to an Emergency Call, see http://datatracker.ietf.org/doc/draft-ietf-ecrit-additional-data/
  Individual submission on Indoor Location Mechanisms for Emergency Services , see http://datatracker.ietf.org/doc/draft-marshall-ecrit-indoor-location/

## Slide 8: Home Networking (homenet) WG
See https://datatracker.ietf.org/wg/homenet/
This working group focuses on the evolving networking technology within and among relatively small "residential home" networks
  The task of the group is to produce an architecture document that outlines how to construct home networks involving multiple routers and subnets.
  This document is expected to apply the IPv6 addressing architecture, prefix delegation, global and ULA addresses, source address selection rules and other existing components of the IPv6 architecture, as appropriate.
  Home Networking Architecture for IPv6, Published as IPv6 Home Networking Architecture Principle: http://datatracker.ietf.org/doc/rfc7368/
Updates [May 2015] Documents of interest:
  New: Outsourcing Home Network Authoritative Naming Service , http://datatracker.ietf.org/doc/draft-ietf-homenet-front-end-naming-delegation/
  Updated: Prefix and Address Assignment in a Home Network: http://datatracker.ietf.org/doc/draft-ietf-homenet-prefix-assignment/
  Updated: Distributed Node Consensus Protocol, see http://datatracker.ietf.org/doc/draft-ietf-homenet-dncp/
  Home Networking Control Protocol: http://datatracker.ietf.org/doc/draft-ietf-homenet-hncp/

## Slide 9: Operations Area Working Group
http://datatracker.ietf.org/wg/opsawg/
  Area WG processes submissions related to Operations Area WGs that have closed
  Control and Provisioning of Wireless Access Points (CAPWAP) Working Group closed in 2009
Responded to requests from OPSAWG chairs for IEEE 802.11 review
  “Alternate Tunnel Encapsulation for Data Frames in CAPWAP” http://www.ietf.org/id/draft-zhang-opsawg-capwap-cds-02.txt , see Slide 5 in https://mentor.ieee.org/802.11/dcn/14/11-14-0368-01-0000-march-2014-liaison-to-ietf-report.pptx
  “IEEE 802.11 MAC Profile for CAPWAP” https://datatracker.ietf.org/doc/draft-ietf-opsawg-capwap-hybridmac/ , see https://mentor.ieee.org/802.11/dcn/14/11-14-0684-01-0000-capwap-hybridmac-liaison-response.docx
  “CAPWAP extension for 802.11n and Power/channel Autoconfiguration” http://datatracker.ietf.org/doc/draft-ietf-opsawg-capwap-extension/ , see https://mentor.ieee.org/802.11/dcn/14/11-14-0913-01-0000-liaison-response-opsawg-capwap-extension.docx
Updates [May 2015] Operations Area Working Group work group items
  CAPWAP Hybrid MAC published as RFC7494, http://datatracker.ietf.org/doc/rfc7494/
  Updated: http://datatracker.ietf.org/doc/draft-ietf-opsawg-capwap-alt-tunnel/
  Individual submission: CAPWAP Control and Data Channel Separation for Multi-provider Scenario, see http://datatracker.ietf.org/doc/draft-you-opsawg-capwap-separation-for-mp/
  (r5): http://datatracker.ietf.org/doc/draft-ietf-opsawg-capwap-extension/ No longer active
  Of interest: RFC6632, An Overview of the IETF Network Management Protocols, see https://tools.ietf.org/html/rfc6632

## Slide 10: Active Queue Management (AQM)
Active Queue Management and Packet Scheduling Working Group website: http://datatracker.ietf.org/wg/aqm/charter/
IETF Recommendations Regarding Active Queue Management to update https://datatracker.ietf.org/doc/rfc2309/
Updates [May 2015]
  In RFC Editor Queue: IETF Recommendations Regarding Active Queue Management, see http://datatracker.ietf.org/doc/draft-ietf-aqm-recommendation/
  Updated: AQM Characterization Guidelines, see http://datatracker.ietf.org/doc/draft-ietf-aqm-eval-guidelines/
  Updated: The Benefits and Pitfalls of using Explicit Congestion Notification (ECN), see http://datatracker.ietf.org/doc/draft-ietf-aqm-ecn-benefits/
  Updated: On Queuing, Marking, and Dropping, see http://datatracker.ietf.org/doc/draft-ietf-aqm-fq-implementation/
  Updated: Controlled Delay Active Queue Management, see http://datatracker.ietf.org/doc/draft-ietf-aqm-codel/

## Slide 11: Transport Layer Security (TLS)
Transport Layer Security Working Group website: http://datatracker.ietf.org/wg/tls/charter/
Work underway on a new version of TLS (used in EAP methods): Transport Layer Security Protocol Version 1.3
Updates [May 2015]
  RFC 7507 published, http://datatracker.ietf.org/doc/rfc7507/ TLS Fallback Signaling Cipher Suite Value (SCSV) for Preventing Protocol Downgrade Attacks
  New: TLS False Start, http://datatracker.ietf.org/doc/draft-ietf-tls-falsestart/
  Updated: Negotiated Finite Field Diffie-Hellman Ephemeral Parameters for TLS, see http://datatracker.ietf.org/doc/draft-ietf-tls-negotiated-ff-dhe/
  Updated: Deprecating Secure Sockets Layer Version 3.0, see http://datatracker.ietf.org/doc/draft-ietf-tls-sslv3-diediedie/
  TLS version 1.3 http://datatracker.ietf.org/doc/draft-ietf-tls-tls13/

## Slide 12: Extensions for Scalable DNS Service Discovery (dnssd)
Working Group website: http://datatracker.ietf.org/wg/dnssd/charter/
Charter: Develop scalable DNS-SD/mDNS Extension requirements and standard solutions to address problematic use of mDNS and DNS-SD in networks today
  mDNS discovery of services on other links is not possible
  Multicast transmissions over wireless are very expensive
  Addressed with different ad hoc technologies
Of interest to: Homenet, Zero configuration, Enterprise-grade vendors of 802.11 infrastructure, Multi-link mesh networking
Updates [May 2015]
  Updated version of Requirements document submitted to IESG for publication: http://datatracker.ietf.org/doc/draft-ietf-dnssd-requirements/
  Updated: Multicast DNS (mDNS) Threat Model and Security Consideration, see http://datatracker.ietf.org/doc/draft-rafiee-dnssd-mdns-threatmodel/
  On Interoperation of Labels Between mDNS and DNS, http://datatracker.ietf.org/doc/draft-ietf-dnssd-mdns-dns-interop/

## Slide 13: Of Interest to Smart Grid
6LOWPAN
  Working Group website: http://datatracker.ietf.org/wg/6lowpan/charter/
  Focus: IPv6 over Low Power PAN: Adaption of IPv6 protocol to operate on constrained nodes and link layers
ROLL
  Working Group website: http://datatracker.ietf.org/wg/roll/
  Focus: Routing over Low Power and Lossy Networks
CORE
  (Constrained RESTful Environments) Working Group website: http://datatracker.ietf.org/wg/core/
  Focus: framework for resource-oriented applications intended to run on constrained IP networks.

## Slide 14: Of Interest: Network-Based Mobility Extensions (NETEXT)
NETEXT: http://datatracker.ietf.org/wg/netext/charter/
Submitted to IESG for publication: Mapping PMIPv6 QoS Procedures with WLAN QoS Procedures, see http://datatracker.ietf.org/doc/draft-ietf-netext-pmip-qos-wifi/
Abstract: This document provides guidelines for achieving end to end Quality- of-Service (QoS) in a Proxy Mobile IPv6 (PMIPv6) domain where the access network is based on IEEE 802.11. RFC 7222 describes QoS negotiation between a Mobility Access Gateway (MAG) and Local Mobility Anchor (LMA) in a PMIPv6 mobility domain. The negotiated QoS parameters can be used for QoS policing and marking of packets to enforce QoS differentiation on the path between the MAG and LMA. IEEE 802.11, Wi-Fi Multimedia - Admission Control (WMM-AC) describes methods for QoS negotiation between a Wi-Fi Station (MN in PMIPv6 terminology) and an Access Point. This document provides a mapping between the above two sets of QoS procedures and the associated QoS parameters. This document is intended to be used as a companion document to RFC 7222 to enable implementation of end to end QoS.

## Slide 15: Potential Liaison: Protocol Independent Multicast (PIM) Re-charter
PIM: http://datatracker.ietf.org/wg/pim/charter/
  Group being re-chartered
  One contributor’s comment:
    IP Multicast over 802.11 is inefficient and unreliable. I would like to see at least one of the multicast working groups in the IETF have a chartered item to work with the IEEE coordinating a solution to this mess. Or at least a coordinated effort to state our dis-satisfaction with the current mess and make a formal request to provide high bandwidth, efficient multicast over 802.11 without sending unicast copies to each group member. After all, it is a radio and it is being broadcast???”

## Slide 16: References
RFC 4017 - IEEE 802.11 Requirements on EAP Methods
Jan 2012 report (PAWS, Homenet details), https://mentor.ieee.org/802.11/dcn/12/11-12-0122-01-0000-january-2012-liaison-to-ietf.ppt