## Slide 1
Pilot Design for 11ax
Date: 2015-05-10
Authors:

## Slide 2: Background
LTF-related decisions made in previous meetings [1]
  The HE PPDU shall support the following LTF modes:
    HE-LTF symbol duration of 6.4us excluding GI
      Equivalent to modulating every other tone in an OFDM symbol of 12.8 µs excluding GI, and then removing the second half of the OFDM symbol in time domain
    HE-LTF symbol duration of 12.8 µs excluding GI

## Slide 3: Pilots in LTF OFDM Symbols
Need for phase tracking in beamformed LTF (i.e. VHT-LTF) OFDM symbols was shown in [2].
Frequency drift compensation is also important in HE-LTF OFDM symbols.
  11ax will support even longer LTF OFDM symbol durations. This may result in further drift compared that with 11ac.
  XTAL and LO design used in 11ac is likely to re-used for 11ax.

## Slide 4: Pilots in 2xLTF
2xLTF limits the positions of pilots in certain data subcarriers.
  2xLTF and 4xLTF terminology barrowed from [3]. It refers to 6.4us and 12.8us DFT duration of LTF symbols.
Potentially, pilots positions designed and optimized for 4xLTF or just regular data subcarriers may result in some pilots missing in the 2xLTF OFDM symbol.
Having two different pilot designs for 2xLTF and 4xLTF case should be avoided as it adds implementation complexity.
…
…
…
…
2xLTF
OFDM Symbol
Data
OFDM Symbol
???

## Slide 5: Pilots in different OFDMA RUs
Most likely number of DC tones for 11ax is odd numbered, 1, 3, 5, or 7.
Some of the OFDMA resource units (RU) is likely to be mirror symmetric and have even number of subcarriers,
This combination results in following characteristics:
  some RUs of the same size are with position starting with odd numbered subcarrier
  some RUs of the same size are with position starting with even numbered subcarrier.
  different relative mapping of 2xLTF signals between RUs of the same size
  Different relative mapping of pilot tones between RUs of the same size
    Assuming that pilot tones are only mapped to tones with 2xLTF signals.
…
…
DC tones
-5 -4 -3 -2 -1 0 +1 +2 +3 +4 +5
…
…
+81 +82 +83 +84 +85
-85 -84 -83 -82 -81
Some Hypothetical Resource Boundary
Some Hypothetical Resource Boundary
Same RU size, but one starts with even subcarrier the other starts with odd subcarrier

## Slide 6: Conclusions
Pilot placement in LTF OFDM symbols and Data OFDM symbols in OFDMA requires some thought
  May have impact on the overall design and numerology itself.
To avoid loss in performance, pilot positions should be aligned with tones selected for 2xLTF transmission.
To avoid implementation complexity, pilot positions between the 4xLTF case and 2xLTF case should be identical.

## Slide 7: Straw Poll #1
Do you agree to the following concept
  Number of pilot tones in a LTF symbol, regardless of LTF symbol durations excluding GI, shall be identical to number of pilot tones in a data OFDM symbol for DL HE PPDU?

## Slide 8: References
[1] Robert Stacey, Specification Framework for TGax, 11-15/0132r3, March 2015.
[2] Youhan Kim, et. al., Phase Tracking During VHT-LTF, 11-10/0770r0, July 2010
[3] Hongyuan Zhan, et. al., HE-LTF Proposal, 11-15/0349r0, March 2015