## Slide 1: Multi Channel Availability for UL-OFDMA
Date: 2015-05-11
Authors:

## Slide 2: Introduction
In dense BSS environment, STAs in the same BSS might be influenced by transmissions from different OBSSs[1], [2]
Considering wider band operation, each STA might see channel (idle/busy) differently
UL-OFDMA procedure might suffer from the different channel availability between AP and UL-STAs

## Slide 3: Hidden node & Channel availability
STA1(CH1, 2) & STA4(CH3, 4) are transmitting data
  Since STA1 and STA4 is hidden from AP, AP sees channel 1 to 4 idle.
  STA2 sees CH1, 2 busy and (STA3-> CH3, 4)
STA1,2 and AP have different channel availability

## Slide 4: MU-UL motion in the previous meeting
The spec shall define the following mode of operation: An UL MU PPDU (MU-MIMO or OFDMA) is sent as an immediate response (IFS TBD) to a Trigger frame (format TBD) sent by the AP. [3]
UL STAs have to transmit UL data immediately after the trigger frame
  Every control information for UL data transmission must be delivered to UL-STAs within the trigger frame

## Slide 5: UL-OFDMA procedure
Considering UL-OFDMA with multiple channels
  AP must decide which STA to participate on which channel
  AP requires STAs’ buffer status and channel availability
  Buffer status information might be gathered periodically or implicitly within ongoing transmissions
  Channel availability cannot be obtained with the same manner
    Channel availability is much more sensitive to time
    Channel availability of past time is worthless
AP might assign (sub-)channels to UL-STAs with trigger frame
  There have been no considerations on channel availability yet
  AP will assign STAs to its available channels based on its discretion
    Simply using previous CSI or random assignment

## Slide 6: Necessity of channel availability on UL-OFDMA procedure (1)
4 channels are defined idle on AP side
AP may send trigger frame only on primary or each idle channel
AP assigns idle channels to STAs having UL data randomly or based on general CSI
Two nodes of different OBSSs, close to STA1 and STA4, were transmitting data

## Slide 7: Necessity of channel availability on UL-OFDMA procedure (2)
STA1 cannot transmit UL data as it couldn’t hear the trigger frame
  Assigned channel will be wasted
  Contention isolation gain and channel utility will decrease as the number of STAs who cannot transmit data increases
STA2 may receive the trigger frame directly from secondary 1 or from primary
  Assumption of full channel sensing is required (trigger frame from secondary 1)
  If STAs are supposed to sense the primary channel only, then STA2 should receive the trigger frame from the primary channel, and move to secondary 1 channel

## Slide 8: Necessity of channel availability on UL-OFDMA procedure (3)
STA4 could hear the trigger frame and transmit UL data
  In 802.11, It is generally assumed that STAs are sensing only primary channel before they transmit data
  STA4 will hear the trigger frame from the primary channel, unless AP informs, prior to the trigger frame, that which channels will be used
  Since STA4 is not possible to measure CCA within SIFS duration, it must transmit UL-data regardless of the channel availability
  UL data of STA4 might cause interference to ongoing transmissions of OBSS STAs

## Slide 9: Necessity of channel availability on UL-OFDMA procedure (4)
With increased xIFS (up to PIFS), it is possible for UL STAs to measure CCA before they transmit UL data
  Assigned STAs(STA4) may decide not to participate UL-transmission
  STA4 won’t make any interference to OBSS, but assigned channel will still be wasted
PIFS sensing for secondary channels may collide with existing PIFS based mechanism (e.g., beacon)

## Slide 10: Necessity of channel availability on UL-OFDMA procedure (5)
If AP could exploit channel availability of STAs
  Avoiding selecting inappropriate UL STAs
    STA1 and STA4 might interfere OBSS transmission or not transmit any UL data
  Assigning other STAs without channel availability issues
    STA5, STA6 don’t belong to OBSS interference range
  Assigning more channels to STA2, STA3
  Overall contention isolation gain or channel utility can be maintained

## Slide 11: Hidden node protection with existing RTS/CTS (1)
Using RTS/CTS for multiple STAs
  AP send RTS to UL-STAs one by one
  RTS can reserve and protect channel from OBSS STAs
  CTS can be regarded as channel availability feedback
Assuming channels are assigned with the trigger frame (1)
  RTS/CTS will be exchanged before the trigger frame on all AP’s idle channel

## Slide 12: Hidden node protection with existing RTS/CTS (2)
Channel will be over protected
  Secondary 1~3 didn’t have to be protected for STA1
  OBSS STAs of STA1 side have to defer for unused channels
For OBSS STAs only exposed to specific UL-STA, RTS/CTS duration could be seen idle
  OBSS STAs may start transmission during RTS/CTS period

## Slide 13: Hidden node protection with existing RTS/CTS (3)
Assuming the channel allocation is performed prior to the trigger
  RTS/CTS will be exchanged only on the assigned channel for each UL-STA
  Channel overprotection problem is no longer exist
  OBSS STAs may start transmission during RTS/CTS period still
  Overall UL-OFDMA procedure might become heavier due to channel allocation
Overhead of multiple STAs RTS/CTS is too large
  Advanced channel availability feedback or channel protection mechanism is required

## Slide 14: Conclusion
In dense BSS and STA environment, STAs in the same BSS might have different channel availability due to ongoing transmissions of OBSSs
Channel availability might not only reduce the channel utility and contention isolation gain of UL-OFDMA but also interfere ongoing transmissions of OBSSs
It is necessary to take the effect of channel availability into account for developing the procedure of UL-OFDMA
  Advanced sensing or channel reservation mechanism
  Channel availability feedback
  Relevant channel protection mechanism

## Slide 15: References
[1] 11-15-0091-01-00ax-ul-ofdma-procedure-in-ieee-802-11ax
[2] 11-15-0378-02-00ax-channel-sensing-in-ul-ofdma
[3] 11-15-0365-00-00ax-ul-mu-procedure

## Slide 16: Strawpoll
UL-OFDMA procedure should consider different channel availability between AP and UL STAs