## Slide 1: Channel Sounding for 802.11ay
Date: 2015-05-12
Authors:

## Slide 2: Abstract
In this presentation, we show the next options for 60 GHz channel sounding scenarios. For the next measurements we present 6 possible scenarios (living room, classroom/meeting, dinning hall, lecture hall, entrance hall, street canyon). We like to discuss the requirements of the measurement campaigns to make the results comparable and useful for channel modeling at 802.11ay.

## Slide 3: Outline
Motivation
Proposed measurement scenarios
Measurement requirement
Conclusion

## Slide 4: Motivation
ISM-band at 60 GHz
  Free and wide bandwidth available (up to 7 GHz)
  WLAN/WiGig (.11ad) and WPAN (.15.3.c)
Extension of IEEE 802.11ad regarding use cases and requirements/performance
  Requires extensive channel measurement of new scenarios/use cases
  Larger coverage, higher bandwidth, higher mobility/channel dynamic
Channel measurement should support advanced system concepts
  MIMO/Beam-forming  large spatial bandwidth
  Adaptive beam-forming /switching (to mitigate shadowing)
  Channel bonding to have large bandwidth
  …
Channel measurements requirements
  Ultra wide bandwidth
  Double directional measurements are needed to characterized the full channel
  Polarization is an important aspect
  High dynamic range are essential to measure the different propagation effects
  …

## Slide 5
Proposed measurement scenarios

## Slide 6: List of Proposed Scenarios
Living room
  HD entertainment centers, video games, etc
  Small Room
  Many Reflection
Class room / Meeting room scenario
  Provide access to students / users with tablets, notebooks, electronic devices, etc.
  Wireless office
Dinner Hall
  Provide video distribution
  Provide access to students / users with tablets, notebooks, electronic devices, etc
Entrance Hall
  Provide access to a large number users
  Modern buildings full of metal and glass
Lecture Hall
  Provide access to a large number users
  Provide access to users with tablets, notebooks, electronic devices, etc.
Street Canyon: Mobile Offloading and Fronthauling
  Transmissions are mostly LOS. Distance between far corners of the room are <100m
Notes:   5G systems at mm-wave require SNR optimisation  and this will be only done with dual polarisation

## Slide 7: Living Room
Dimensions:
4m x 5m x 3m
Charateristics:
HD entertainment centers, video games, etc
Small Room
Many Reflection

## Slide 8: Class room / Meeting room scenario
Dimensions:
4m x 12m x 3m
Part disguised wood
Charateristics:
Provide access to students / users with tablets, notebooks, electronic devices, etc.
Wireless office

## Slide 9: Dinning Hall
Dimensions:
9m x 20 m x 3m
Part disguised wood
Charateristics:
Provide video distribution
Provide access to students / users with tablets, notebooks, electronic devices, etc

## Slide 10: Entrance Hall
Dimensions:
7 x 25m x 9m
Glass and metal
3 different floors
Charatersitics:
Provide access to a large number users
Modern buildings full of metal and glass

## Slide 11: Lecture Hall
Dimensions:
22m x 36m x 7m
Chamfered
Part disguised wood
Charateristics:
Provide access to a large number users
Provide access to users with tablets, notebooks, electronic devices, etc.

## Slide 12: Street Canyon
Charateristics:
The height of the building is 13m-15m
Distances of more than 50 m possible
  Transmissions are mostly LOS. Distance between far corners of the room are <100m

## Slide 13: Mapping Use Cases and Scenarios
UC # | Indoor (I)/ Outdoor (O) | bne | Topology | Proposed Scenario's
 |  | LOS/ NLOS |  | 
1 Ultra Short Range (USR) Communications | I | <10cm | P2P | 
2 8K UHD Wireless Transfer at Smart Home | I | <5m | P2P | 
3 Augmented Reality and Virtual Reality | I | <10m | P2P | Living room
4 Data Center NG60 Inter-Rack Connectivity | I | <10m | P2P/P2MP | 
5 Video/Mass-Data Distribution/Video on Demand System | I | <100m | P2P/P2MP | Class room/ Meeting room; Dinning Hall; Lecture Hall; Entrance Hall;
6 Mobile Offloading and Multi-Band Operation (MBO) | I/O | <100m | P2P/P2MP | Street Canyon
7 Mobile Fronthauling | O | <200m | P2P/P2MP | Street Canyon
8 Wireless Backhauling with Single Hop | O | <1km | P2P/P2MP | Street Canyon
9 Wireless Backhauling with Multi-hop | O | <150m | P2P/P2MP | Street Canyon
*: Multi-hop will build up on the scope of the DMG Relay defined in IEEE 802.11ad

## Slide 14: Challenges in mm-Wave Channel Sounding for 802.11ay
3D analysis of indoor and outdoor scenarios
Full polarimetric propagation measurement
Analysis of time-variant scenarios
Multi–link channel analysis
Min. Bandwidth of 4 GHz for channel bonding at 802.11ay
The analysis of mm-Wave propagation need more than “bandwidth”
Notes: Multi–link channel analysis

## Slide 15: Dual Polarimetric Ultra-Wideband Channel Sounder (DP-UMCS)
7 GHz BW up to 10 GHz measurable bandwidth
Maximum excess delay of 585 ns (175m) in CS version 1 and 4.7 µs (1410m) CS version 2
Dual polarization measurement capability
Compact Size  the complete system can be attached to the positioner
Multiplier
X8
PA min. 27 dBm
7 GHz
Oscillator
Multiplier
X8
LNA
Gain : 40 dB
UWB Sounder RX
0 – 3.5 GHz
3.5 GHz - 10.5 GHz
H Pol.
V Pol.
CH 1
CH 2
H Pol.
V Pol.
Switch
TX Module
RX Module
56 - 66 GHz
56 - 66 GHz
PA min.
27 dBm
Step
Attenuator
LNA
Gain : 40 dB
UWB Sounder TX
0 – 3.5 GHz
3.5 GHz - 10.5 GHz
Optical link
Optical link
Step
Attenuator
High instantaneous dynamic range: up to 75 dB
Multi-Link and Massive MIMO capabilities
Double directional measurements (with 1 TX and 2 RX) feasible

## Slide 16: Measurement Setup of the DP-UMCS
7 GHz
Oscillator
and
Optical TX
UWB Sounder RX
0 – 3.5 GHz
3.5 GHz - 10.5 GHz
H Pol.
V Pol.
CH 1
CH 2
H Pol.
V Pol.
UWB Sounder RX
0 – 3.5 GHz
3.5 GHz - 10.5 GHz
Optical link
Optical link
mmWave
TX Module
mmWave
RX Module
UWB Sounder RX
0 – 3.5 GHz
3.5 GHz - 10.5 GHz
H Pol.
V Pol.
CH 1
CH 2
mmWave
RX Module
Optical link
Optical RX
Optical RX
Optical RX
Control PC
Control PC
Control PC
Controlling per Ethernet or Wlan

## Slide 17: Conclusion/Discussion
We present 6 scenarios as options for different usage cases
  Living room, classroom/meeting, dinning hall, lecture hall, entrance hall, street canyon
  Which are useful scenarios for the 802.11ay group?
  How many measurement points are required/meaningful?  measuring time
  Which resolution for the azimuth and elevation scan? measuring time
  Which range for the azimuth and elevation for the different scenarios are useful?  measuring time
We revise the current 60 GHz Channel Sounder
  Measurement bandwidth of 7 GHz  analysis of channel bonding possible
  The capability of MIMO measurements
  End of 2015: A fast measurement CS system with the capability of 10000 CIR/s per RX channel  Doppler resolution of around 40 km/h
Notes:   5G systems at mm-wave require SNR optimisation  and this will be only done with dual polarisation