## Slide 1: Experimental Measurements for Short Range LOS SU-MIMO
Date: 2015-05-11
Authors:

## Slide 2: Abstract
This contribution presents the results of experimental measurements for the LOS short range 2x2 SU-MIMO system, [1].
As it was shown in [2] for particular example of 2x2 LOS MIMO configuration the Shannon capacity depends on the phase difference between channel coefficients and attenuation factor of the cross links.
However it was shown that the dependence on phase difference is not prominent if the power of cross links is small enough comparing to the power of the direct links.
In this work the results of non-coherent channel measurements are provided. In particular the power of the direct and cross links is measured and the impact of spatial antennas separation and antennas cross polarization is investigated.
The previous channel measurement results (IEEE 802.11ad) obtained for the larger distances and reflected paths can be found in references [3], [4].

## Slide 3: Usage Models Description
The LOS SU-MIMO is proposed to be used for different usage models scenarios, [5], [6]:
  Sync-and-go kiosk, digital content downloading;
  Device-to-device (D2D) short range communication, tablet to laptop, handheld to laptop, laptop to laptop;
  Wireless docking, connection of the laptop to external monitor and other peripherals.
The distance of interest can be from ~10 - 20 cm and up to ~2 m;
Sync-and-go kiosk
D2D communication
Wireless docking

## Slide 4: LOS MIMO Configurations
Figure below shows two LOS MIMO configurations investigated in the experiment.
Configuration #1:
  Both devices have two Phased Antenna Array (PAAs), which can be separated by d = 10 – 30 cm and have vertical polarizations (V). It is assumed that antennas are mounted in the corners of the laptop’s lid or in the corners of the tablet device.
Configuration #2:
  Both devices have single PAA, but it is divided into two subarrays whose elements have different polarization types, i.e. vertical (V) or horizontal (H). This configuration may be viable for small factor handheld devices where spatial separation of antennas is not possible.

## Slide 5: Measurement Setup Description
Configuration #1 – antennas spatial separation:
  Measurements were done in the conference room, TX and RX devices are placed on the table.
  Both TX Phased Antenna Arrays (PAAs) and RX PAAs have vertical polarization and the same geometry of 2 x 8 elements. PAAs are placed at the height of 18 cm above the table.
  Distance between the geometrical centers of TX/RX PAAs: d = 10, 20, and 30 cm.
  Distance between TX and RX devices: D = 20 – 200 cm, with discrete step = 20 cm.
  Measurements were done after application of TXSS beamforming, assuming that TX PAA 1 makes beamforming with RX PAA 1 and TX PAA 2 makes beamforming with RX PAA 2.
  Both links are trained independently.

## Slide 6: Measurement Setup Description (Cont’d)
Configuration #2 – cross polarization:
  The TX PAA uses for transmission subarray of 4 elements and RX PAA uses for reception only 1 omni element of the array. PAAs are placed at the height of 18 cm above the table.
  The TX PAA has vertical (V) polarization and RX PAA omni element can have vertical (V) or horizontal (H) polarization, distance between TX and RX devices can be D = 20 – 200 cm, with step = 20 cm;

## Slide 7: Measured Signal Characteristics
To set up directional link Transmit Sector Sweep (TXSS) beamforming protocol was applied.
The following signal characteristics were measured:
  Received Signal Strength Indicator (RSSI), which is actually a received power in the 2.16 GHz signal bandwidth, mean RSSI was estimated over 105 packet transmissions.
  Channel impulse response @ 2.64 GHz sample rate for channel coefficients in the direct H11 and interfered link H21.
Channel measurements were done non-coherently, i.e. first channel impulse response was measured for link H11 and then for H21 (not simultaneously).

## Slide 8: Antennas Spatial Separation
Figure shows measured Radiation Pattern (RP) for broadside direction (blue line) for 2x8 array and its comparison to the theoretical one (red line) calculated for array with λ/2 elements spacing.
Both curves are plotted for elevation angle equal to 00.
Half Power Beamwidth (HPBW) is equal to ~ 14.00.
First null corresponds to the ~0.25 rad or ~14.30.
Theoretical RP is defined by the following equation:
Comparison of measured and theoretical radiation patterns for 2x8 λ/2 array
where Nx = 8, dx = λ/2, φ – azimuth angle.

## Slide 9: Antennas Spatial Separation (Cont’d)
The received power for the direct link H11 can be theoretically predicted applying Friis equation:
where G(φ) is PAA gain introduced at the previous slide, d is the PAAs separation distance, D is the distance between devices.
The received power of the interfered link H21 can be theoretically calculated as follows:

## Slide 10: Antennas Spatial Separation (Cont’d)
Figure shows dependence of measured mean RSSI vs. distance D (solid lines) for direct link H11 and interfered link H21 for different antennas spatial separation equal to 10, 20, and 30 cm.
RSSI is plotted in dB scale relatively to the point with maximum power corresponding to the direct link and D = 20 cm. This reference level is applied to be equal to 0 dB.
As it can be seen from the graph, antennas separation by d = 30 cm (pink curve) creates the power difference for direct H11 and interfered link H21 ≥ 15.0 dB for the distances up to 2 m.
Dashed lines correspond to the theoretical dependences P11(D) and P21(D,d) introduced at the previous slides.
RSSI Measurements

## Slide 11: Antennas Cross Polarization
Figure shows measured dependence of mean RSSI vs. distance D for TX V – RX V and TX V – RX H polarization configurations.
RSSI is plotted in dB scale relatively to the reference point (assigned to 0 dB) with maximum power corresponding to the direct link and D = 20 cm.
The cross polarization factor (X-pol) does not depend on the distance and is equal to 23.0 – 24.0 dB.
RSSI Measurements

## Slide 12: Conclusions
This work presents the results of non-coherent channel measurements for the LOS short range SU-MIMO system.
Two practical configurations for 2x2 MIMO scheme exploiting antennas spatial separation and polarization discrimination were experimentally investigated.
It was shown that antennas spatial separation by 30 cm creates the difference in the direct and interfered links more than 15.0 dB for the distances up to 2 m.
Cross polarization factor and therefore links separation for the perfect matching of the TX and RX antennas can achieve ~23.0 – 24.0 dB.
Channel impulse responses measured @ 2.64 GHz sample rate for both direct and interfered links in the LOS conference room environment include one main tap and do not contain any significant reflection taps.

## Slide 13: References
A. Maltsev et al., “mmWave MIMO Link Budget Estimation for Indoor Environment,” IEEE doc. 11-15/0113r1.
A. Tarighat et al., “A Framework for MIMO Operation over mmWave Links,” IEEE doc. 11-15/0334r0.
A. Maltsev et al., “Experimental Investigation of 60 GHz WLAN Systems in Office Environment,” Journal on Selected Areas in Communications, vol. 27, pp. 1488 - 1499, 2009.
A. Maltsev et al., “Impact of Polarization Characteristics on 60 GHz Indoor Radio Communication Systems,” Antennas and Wireless Propagation Letters, vol. 9, pp. 413 - 416, 2010.
C. Cordeiro et al., “Next Generation 802.11ad: 30+ Gbps WLAN,” IEEE doc. 11-14/0606r0.
R. Sun et al., “NG 60 Use Cases,” IEEE doc. 11-15/0328r4.