## Slide 1: Simulation Results for Box5
Date: 2015-05-09
Authors:
Name | Affiliation | Address | Email
Zhiqiang Han | ZTE |  | han.zhiqiang1@zte.com.cn
Ruimei Li | ZTE |  | li.ruimei@zte.com.cn
Bo Sun | ZTE |  | Sun.bo1@zte.com.cn
Yonggang Fang | ZTE |  | yfang@ztetx.com
Jiadong Du | CATR |  | dujiadong@catr.cn

## Slide 2: Abstract
  The submission provides updated simulation results for Box-5 calibration.
  Applying the assumptions about preamble detection and other issues like receiving procedure in [2].
  Some further details in our simulation are listed in the following slides.
  There are some difficulty in the complex scenario calibration，we provide some calibration result in the simple scenario.

## Slide 3: Box5 Calibration Scenario
11ac SS6 – OBSS Enterprise [1]
AP C | (-40,-20)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
AP A | (0,0)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)
Fixed Location and Association
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
AP B | (40,20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)

## Slide 4: Box-5 PHY Details
PHY parameters | 
BW | All BSSs at 5GHz [80 MHz, no dynamic bandwidth]
Channel model | TGac D NLOS per link
Shadow fading | 0
Data Preamble Type | [5GHz, 11ac], always decoded correctly after successful reception, duration is considered.
STA TX Power | 15 dBm per antenna
AP TX Power | 20 dBm per antenna
AP number of TX/RX antennas | 1/1
STA number of TX /RX antennas | 1/1
Capture Window | [0 ns 800ns]
preemption window | [0 ns]
AP antenna gain | 0 dBi
STA antenna gain | -2 dBi
Noise Figure | 7dB
CCA threshold ( CCA-SD) | -76dBm (measured across the entire bandwidth after large-scale fading)
ED threshold (CCA-ED) | -56dBm
Link Adaption | Fixed MCS =5 （234Mbps)
Channel estimation | ideal
PHY abstraction | RBIR, BCC [1, 5]
Channel correlation | Independent or time-correlated channel per packet

## Slide 5: MAC Parameters
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3]
Queue length | 2000 packets length multiplied by the STA number inside AP; 2000 packets length inside STA
Traffic type | UDP CBR with rate 10^8bps. The same traffic is attached to each STA or AP.
MPDU size | 1530 Bytes (1472 MSDU + 36 UDP、IP、LLC header + 30 MAC header)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU with immediate BA], Max aggregation: 64 MPDUs with 4-byte MPDU delimiter (with 2 bytes padding)
Max number of retries | 10
Beacon | Disabled
RTS/CTS | OFF
Traffic direction | DL only,
Throughput metric | CDF or Histogram of per non-AP STA throughput (received bits/overall simulation time)

## Slide 6: Sim. Result of DL only for BSS B
 |  | Throughput（Mbps）
5 STAs | STA3 | 51.98
 | STA9 | 52.03
 | STA15 | 52.16
 | STA21 | 52.21
 | STA 27 | 51.86

## Slide 7: Single BSS Operation Result - DL
Chart: 
| 3 | 9 | 15 | 21 | 27
Huawei | 51.09 | 51.55 | 51.05 | 51.42 | 51.37
LG | 51.05 | 50.97 | 51.11 | 50.7 | 51.1
MRVL | 52 | 52.68 | 52.68 | 52.51 | 52.81
NTT | 49.92 | 50.08 | 49.95 | 50.04 | 50.24
ZTE | 51.98 | 52.03 | 52.16 | 52.21 | 51.86
1-BSS DL-only results from five companies show similar trend.

## Slide 8: Sim. Result of UL only for BSS B
 |  | Throughput（Mbps）
2 STAs | STA3 ，STA9 | STA3：98.27: STA9：98.00
 | STA3 ，STA27 | STA3：98.13 STA27：96.73
 | STA3 ，STA15 | STA3：98.10 STA15：98.38
3 STAs | STA3 ，STA9，STA27 | STA3：67.81 STA9：68.37 STA27：69.26
 | STA3 ，STA9，STA15 | STA3：67.80 STA9：69.17 STA15：67.09

## Slide 9: Single BSS Operation Result - UL
Chart: 
| 3 | 9
WILUS | 98.02 | 98.3
NEWRACOM | 97.8 | 99.28
Huawei | 98.59 | 98.37
NTT | 98.16 | 98.15
LG | 98.33 | 97.83
ZTE | 98.27 | 98
Chart: 
| 3 | 27
WILUS | 97.28 | 97.31
NEWRACOM | 95.29 | 97.11
Huawei | 99.76 | 96.94
NTT | 97.01 | 97.58
LG | 89.01 | 98.77
ZTE | 98.13 | 96.73
Chart: 
| 3 | 15
WILUS | 97.21 | 98.26
NEWRACOM | 95.02 | 97.84
Huawei | 99.74 | 97.36
NTT | 97.44 | 99.23
LG | 96.04 | 99.24
ZTE | 98.1 | 98.38
Chart: 
| 3 | 9 | 27
WILUS | 63.51 | 67 | 61.77
NEWRACOM | 55.7 | 61.07 | 62.26
Huawei | 64.66 | 63.61 | 59.54
NTT | 61.82 | 62.18 | 61.52
LG | 70.09 | 65.07 | 52.15
ZTE | 67.81 | 68.37 | 69.26
Chart: 
| 3 | 9 | 15
WILUS | 65.56 | 61.92 | 62.98
NEWRACOM | 57.57 | 66.6 | 59.08
Huawei | 70.07 | 56.66 | 62.54
NTT | 60.75 | 61.63 | 63.79
LG | 63.01 | 60.75 | 64.51
ZTE | 67.8 | 69.17 | 67.09

## Slide 10: Summary
Provide Box-5 simulation result in the simple scenario for further calibration.

## Slide 11: References
[1] 11-15-0053-00-00ax-box5-results-of-11ac-ss6.