## Slide 1: Control PHY Design for 40-50GHz Millimeter Wave Communication Systems.pptx
Authors:

## Slide 2: Introduction
Link budget analysis shows that beamforming is needed to support 10m NLOS
Discovery and beamforming training needs control PHY that works in low SNR regime
This proposal designs a Control PHY with low implementation complexity and good performance

## Slide 3: Link Budget for NLOS case
Extra gain needed
  SNR requirement is 1.0 dB for BPSK, ½ rate code
  Extra Gain Needed: 20*log10(d)-(Rx_SNR-required_SNR)=16dB
Tx power (dBm) |  | 10
Tx Antenna Gain |  | 0
Center Frequency (GHz) |  | 45
Propogation Loss at 1m (dB) |  | 65.56425
Shawdowing+link margin |  | 10
RX antenna Gain |  | 0
Receiver Signal Strength |  | -65.5643
Rx Noise Figure (dB) |  | 10
Immeplentaion loss (dB) |  | 2
BW (GHz) |  | 1
Noise Floor |  | -84
RX SNR (dB) |  | 6.43575
SNR BPSK, LDPC 1/2 |  | 1.0
Distance (m) |  | 1.573213
extra gain needed for 10m NLOS (dB) |  | 16.06425

## Slide 4: Design Requirements on Control PHY[1]
One side beamforming gain can be provided by sector level sweep
  Gain is about 10*log10(N), N it the number of antenna, for example, using 8 antennas can get 6-9 dB
  Note that receive antenna gain does not count Tx power increase.
Assume 8dB Gain is provided by one side beamforming, than extra gain 8dB is needed for BPSK and LDPC ½ rate code.
We need a low rate PHY that can operate at SNR:
  -8+1.0=-7 dB.

## Slide 5: Control PHY Design
  Control PHY Preamble still uses ZCZ sequences
    Easier for implementation since common preamble sequences for SC PHY and OFDM PHY [2]
  Control PHY is only transmitted in 540MHz channel
    To get extra range and reduce the complexity
  Control PHY Header and Data portion
    Modulation: BPSK with LDPC encoded
    Single Carrier (SC) with Spreading
    Spreading factor is changeable for flexible designs and different spectrum efficiency.

## Slide 6: Spreading with Barker Sequences
Spreading using Barker Sequences
  Barker sequence is a finite sequence of N values of +1 and −1 with ideal correlation property
The chosen spreading sequences are in read and filled with blue color.
  Barker Sequence has the lowest sidelobe level ratio among all binary sequences
  reading with factor 13 provides 11dB SNR enhancement
Length | Codes |  | Sidelobe level ratio | SNR Gain
2 | +1 −1 | +1 +1 | −6 dB | 3dB
3 | +1 +1 −1 |  | −9.5 dB | 4.7dB
4 | +1 +1 −1 +1 | +1 +1 +1 −1 | −12 dB | 6dB
5 | +1 +1 +1 −1 +1 |  | −14 dB | 7dB
7 | +1 +1 +1 −1 −1 +1 −1 |  | −16.9 dB | 8.4dB
11 | +1 +1 +1 −1 −1 −1 +1 −1 −1 +1 −1 |  | −20.8 dB | 10.4dB
13 | +1 +1 +1 +1 +1 −1 −1 +1 +1 −1 +1 −1 +1 |  | −22.3 dB | 11.1dB

## Slide 7: Signaling on spreading factor
Spreading factor signaling information can be conveyed using a field control PHY header
  PHY header is spread with barker sequence 13 and with fixed encoding schemes.
Field name | Number of Bits | Starting Bit | Description
Reserved | 1 | 0 | Set to 0 (differential detector initialization).
Scrambler Initialization | 4 | 1 | Bits of the initial scrambler state
Length | 10 | 5 | Number of data octets in the PSDU. Range 14-1023.
Packet Type | 1 | 15 | TRN packet type
Training Length | 5 | 16 | Length of the training field.
Turnaround | 1 | 21 | Set to 1 if the STA is transmitting a packet during an SP or TXOP.
Spreading Factor | 2 | 22 | Set to 0: spreading by 13 Set to 1: spreading by 7 Set to 2: spreading by 4 Set to 3: no spreading
HCS | 16 | 24 | Header Check sequence.

## Slide 8: Simulation Settings
LDPC code rate ½
BPSK modulation
Spreading factor 4, 5, 7, 11, 13
Packet size 42 bytes (336 bits)
Real Channel Estimation based on Channel Estimation Sequences using ZCZ 256 sequences
AWGN, Exp 4ns, Exp 10 ns, Exp 20 ns channels

## Slide 9: PER in AWGN Channels
With Spreading 13, system can work at SNR less than -11dB, which is good enough for an AP with 4 TX antennas.
SF | SNR (dB) @10-1 PER
13 | -11.2
11 | -10.6
7 | -9.1
5 | -7.9
4 | -7.0
PER

## Slide 10: BLER in Exp 4ns Channels
SF | SNR (dB) @10-1 PER
13 | -10.6
11 | -9.9
7 | -8.2
5 | -6.7
4 | -5.2
PER

## Slide 11: BLER in Exp 10ns Channels
SF | SNR (dB) @10-1 PER
13 | -9.7
11 | -9.2
7 | -7.3
5 | -5.3
4 | -3.2
PER

## Slide 12: BLER in Exp 20ns Channels
SF | SNR (dB) @10-1 PER
13 | -8.1
11 | -7.5
7 | -5.6
5 | -3.1
4 | -0.2
PER

## Slide 13: Performance Summary
SNR @ 10-1 PER
SF | AWGN | Exp 4ns | Exp 10 ns | Exp 20ns
13 | -11.2 | -10.6 | -9.7 | -8.1
11 | -10.6 | -9.9 | -9.2 | -7.5
7 | -9.1 | -8.2 | -7.3 | -5.6
5 | -7.9 | -6.7 | -5.3 | -3.1
4 | -7.0 | -5.2 | -3.2 | -0.2

## Slide 14: Summary
Link Budget analysis shows that a control PHY that works in low SNR regime is required.
We propose a control PHY design with low implementation cost and good PER performance.

## Slide 15: References
[1] WPAN-PG4-T-14-036-00 Mediatek Introduction to Beamforming Protocols for 40-50GHz
[2] Complete-specification-proposal-IEEE-802.11aj(45GHz)_v0.1.1