## Slide 1: Pilot Design for Data Section
Date: 2015-07-13
Authors:
Name | Company | Address | Phone | Email
Sameer Vermani | Qualcomm | 5775 Morehouse Dr San Diego, CA |  | svverman@qti.qualcomm.com
Alice Li | Qualcomm |  |  | 
Lin Yang | Qualcomm |  |  | 
Bin Tian | Qualcomm |  |  | 
Tao Tian | Qualcomm |  |  | 
Arjun Bharadwaj | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
Richard Van Nee | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | 
Allert Van Zelst | Qualcomm |  |  | 
Youhan Kim | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | 
VK Jones | Qualcomm |  |  | 

## Slide 2
Name | Affiliation | Address | Phone | Email
Qinghua Li | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-408-765-9698 | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | +408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Authors (continued)

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Sudhir Srinivasa | Marvell (Cont’d) | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Eric Wong | Apple | Cupertino, CA | +1-408-9745967 | ericwong@apple.com
Chris Hartman |  |  |  | 
Aon Mujtaba |  |  |  | 
Joonsuk Kim |  |  |  | joonsuk@apple.com
Guoqing Li |  |  | +1-408-974-9164 | guoqing_li@apple.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Weimin Xing | ZTE Corp. |  |  | Xing.weimin@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Ke Yao |  |  |  | Yao.ke@zte.com.cn
Bo Sun |  |  |  | Sun.bo1@zte.com.cn
Yonggang Fang | ZTE TX |  |  | yfang@ztetx.com

## Slide 9
Introduction
In these slides, we try to reach consensus on high level pilot design for data section of 11ax PPDUs
  Focus on key decision of choosing between following 2 designs:
    Single stream pilots (as used in 11ac)
    MIMO pilots (as used in 11n)
Data section pilot design can be categorized into following cases
  SU, DL OFDMA, UL OFDMA PPDUs
    Need to track only one phase on the assigned frequency resource
  UL MU-MIMO PPDUs
    Need to track multiple phases (one per user) over the same frequency resource
Based on analysis shown in these slides, propose transmission of single stream pilots in data section of all PPDUs in 11ax

## Slide 10: Pilots in 802.11: Historical Perspective
Two kinds of pilot mappings exist in 802.11 standards
  MIMO pilots
    Used in 11n, different stream uses different pilot sequence
    Orthogonal space-frequency and space-time mapping
      More robust performance for highly correlated channels by providing diversity and avoiding undesired BF
  Single stream pilots (SSP)
    Used in 11ac, different streams use exactly the same pilot sequence
    Used for both SU and DL MU-MIMO

## Slide 11: Pilot design in 802.11ax
For SU and DL/UL OFDMA, reusing 11ac single-stream pilots (SSP) becomes natural choice
  Similar to 11ac, just one common phase offset needs to be tracked
    On the entire band (SU) or on each user’s frequency assignment (OFDMA)
The key question is for UL MU MIMO: Do MIMO pilots bring any performance benefit?
  In UL MU-MIMO, AP needs to do per user phase tracking and correction
  If there is no performance benefit of MIMO pilots, adopt SSP
    Leads to unified pilot structure for all Tx modes
Next 2 slides compare MIMO pilots vs SSP for UL MU-MIMO

## Slide 12: Suitability of the two pilot options for 11ax UL MU-MIMO
MIMO pilots
  Similar to 11n, different streams would use different pilot sequence
    Pilot sequence decided based on stream index in the UL
    Space time and space frequency orthogonal mapping
  Orthogonality provided in the MIMO pilots may not be that useful for UL MU-MIMO
    Space-frequency orthogonality to avoid undesired beamforming (over all pilot tones together)
      Channels from different users/streams are most likely uncorrelated
      Large timing offsets and CSDs further help destroy the flatness in fading, so undesired BF unlikely to happen on all pilot tones together
    Space-time orthogonality to get better diversity
      Averaging over time is needed to use this for pilot tracking
      Reduces phase tracking loop BW admitting more phase noise
        Phase tracking loop BW situation is already exacerbated by 4x symbols
Single stream pilots with same pilot sequence for every user
  All streams/users transmit the same pilot sequence
    Similar to 802.11ac
  Unifies pilot design with other modes
  Need to check if phase tracking performance is comparable to MIMO pilots

## Slide 13: Performance comparison of the two pilot options for UL MU-MIMO
  AP with 4 Rx antennas, 4 STAs with each having 1 Tx antenna transmitting 1 spatial stream each
Two Scenarios
  Independently located STAs
  Co-located STAs
    Assign antennas of an SU-MIMO channel to a different users
Channels
  DNLoS channel
  DLoS channel with Rician factor K_Rice_dB = [0, 6, 10]dB
Impairments modeled
  Non-linear PA
  IQ imbalance
  Phase noise (PN)
  CFO: [-CFO -CFO +CFO +CFO]/2 for 4 STAs
For all the scenarios listed above, we found negligible difference (<0.2
dB) in the performance of MIMO pilots and SSP
  Tested MCS3 and MCS8

## Slide 14: Summary on pilot design
Natural to use 802.11ac single stream pilots for SU and DL/UL OFDMA PPDUs
  Just one phase to track like 802.11ac
We found that even for UL MU-MIMO, the performance benefit of MIMO pilots over SSP is fairly minimal
  Performance is very close even in co-located, highly correlated cases
Recommend using Single stream pilots (as in 11ac) in data section for all transmission modes of 802.11ax
  Unified pilot design across all modes
  All streams transmit the same pilot sequence for UL MU-MIMO

## Slide 15: Straw-poll 1
Do you agree to add the following text to the TGax spec framework document:
  “All 802.11ax PPDUs shall have single stream pilots in the data section
    All streams use the same pilot sequence even in UL MU-MIMO”
  Y
  N
  A

## Slide 16: Motion 1
Move to add the following text to the TGax spec framework document:
  “All 802.11ax PPDUs shall have single stream pilots in the data section
    All streams use the same pilot sequence even in UL MU-MIMO”
  Y
  N
  A