## Slide 1: CP Indication for UL MU Transmission
Date: 2015-07-13
Authors:
Name | Affiliation | Address | Phone | Email
Zhigang Rong | Huawei | 10180 Telesis Court, Suite 365, San Diego, CA 92121, USA |  | zhigang.rong@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121, USA |  | yangyunsong@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Bo Yu |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hyeyoung Choi | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hy0117.choi@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 8: Introduction
In [1], the following has been specified
  “Data symbols in an HE PPDU shall support guard interval durations of 0.8 µs, 1.6 µs and 3.2 µs.”
For UL MU (i.e., UL OFDMA and UL MU-MIMO) transmission, it is required that signals from multiple STAs to be time-aligned at the AP
  Otherwise, significant interference among STAs will occur
Therefore, it is required that all the STAs involve in UL MU transmission should use the same CP length
  Different CP for different STA will cause signals from different STA misaligned at the AP
  Signals arriving at the AP should be within the CP window
Due to the difference on UL and DL, the CP length required for UL and DL MU transmission could be different
  UL transmission are from multiple transmitters (i.e., STAs) while DL transmission are from a single transmitter (i.e., AP)
  CP for UL MU transmission needs to accommodate round trip delay difference and timing inaccuracy among STAs while CP for DL MU does not need to

## Slide 9: Possible CP Length for UL MU
Option 1: a single CP length for UL MU transmission
  This CP length should be large enough to accommodate the maximum round trip delay, timing inaccuracy among STAs, and channel delay spread
  Possible value could be 1.6 us or 3.2 us
Option 2: multiple possible CP lengths for UL MU transmission
  AP can select one out of multiple CP lengths and assign it to multiple STAs for UL MU transmission
  Possible values could be 0.8 us, 1.6 us and 3.2 us

## Slide 10: CP Indication for UL MU Transmission
Alt. 1: CP length is implicitly indicated by the usage of UL MU
  STA can read the UL scheduling information in Trigger frame and decide if the following UL transmission will be UL MU
  If the UL transmission is for UL MU, the STA will use a default CP length for its UL MU transmission
  Suitable for Option 1: a single CP length for UL MU transmission
Alt. 2: CP length is explicitly indicated
  CP length can be indicated by a “GI Length” field in a common part of UL scheduling information in a Trigger frame
  Suitable for Option 2: multiple possible CP lengths for UL MU transmission

## Slide 11: Comparison of Alt.1 and Alt. 2
 | Alt. 1 (Implicit) | Alt. 2 (Explicit)
Signaling Overhead | No | Yes
Flexibility | Low | High
Support CP Length Option | Option 1 | Options 1 and 2

## Slide 12: Conclusions
We presented two alternatives to indicate CP length for UL MU transmission
Alt. 1 incurs no additional signaling overhead but can only support a single CP length
Alt. 2 requires additional signaling overhead but is more flexible to support multiple possible CP lengths
Our preference is Alt. 2

## Slide 13: Straw Poll
Do you agree to add the following text into 11ax SFD?
  3.y.z CP length of UL OFDMA/MU-MIMO transmission shall be explicitly indicated by AP in the Trigger frame that allocates resources for the UL OFDMA/MU-MIMO transmission. The value of CP length for all users addressed by the Trigger frame shall be the same.

## Slide 14: References
[1] 11-15/0132r6 Specification Framework for TGax