## Slide 1: P Matrix for HE-LTF
Date: 2015-07-12
Authors:
Name | Affiliation | Address | Phone | Email
Yakun Sun | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | yakunsun@marvell.com
Hongyuan Zhang |  |  |  | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvell..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 2
Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com

## Slide 3
Authors (continued)
Name | Affiliation | Address | Phone | Email
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Hyeyoung Choi |  |  |  | hy0117.choi@lge.com
Jinmin Kim |  |  |  | Jinmin1230.kim@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 4
Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 5
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Authors (continued)

## Slide 6
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Alice Chen |  |  |  | 
Lin Yang |  |  |  | 
Authors (continued)

## Slide 7
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Bo Sun | ZTE | #9 Wuxing duan, Xifeng Rd, Xi’an, China |  | Sub.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | Yao.ke5@zte.com.cn
Weimin Xing |  |  |  | Xing.weimin@zte.com.cn
Authors (continued)

## Slide 8: Overview
HE-LTF has been agreed such that [1]:
  “The HE-LTF shall adopt a structure of using P matrix in the data tones as in 11ac. In the data tones, every space-time stream is spread over all HE-LTF symbols by one row of the P matrix as defined in 11ac. Different space-time streams use different rows in P matrix…”
  “In an HE PPDU, the HE-LTF section shall start at the same point of time and end at the same point of time across all users…”
Focus of these slides: How to align HE-LTF if different resource units have different number of spatial streams

## Slide 9: Example of HE-LTF
Suppose HELTF have NHELTF symbols, per the maximum number of Nsts across users.
AP can also intentionally signal a longer HE-LTF to boost channel estimation performance.
If a user chooses P matrix by its Nsts, it is a problem how to fill up to NHELTF symbols.
Legacy Preamble
Full-20MHz HE Preamble
(RLSIG, HESIGA, HESIGB)
HE-STF
HE-STF
HE-STF
HE-STF
HE-LTF
HE-LTF
HE-LTF
HE-LTF
OFDMA-User-1 (Nsts_1)
OFDMA-User-2 (Nsts_2)
OFDMA-User-3 (Nsts_3)
OFDMA-User-4 (Nsts_4)
N_HELTF symbols
?

## Slide 10: Option 1: Repeating
Each user selects an 11ac Nsts × NVHTLTF P matrix and generates HE-LTF symbols in its scheduled tones.
Then circularly repeat the generated HE-LTF symbols till all NHELTF HE-LTF symbols are filled.
Legacy Preamble
1x HE Preamble
HE-STF
HE-STF
HE-STF
HE-STF
HE-LTF
PNsts1 x N_VHTLTF1
HE-LTF
HE-LTF
HE-LTF
OFDMA-User-1 (Nsts_1)
OFDMA-User-2 (Nsts_2)
OFDMA-User-3 (Nsts_3)
OFDMA-User-4 (Nsts_4)

## Slide 11: Option 2: Uniform Spreading
Each user(s) applies the first Nsts rows of a “super” P matrix.
  “Super” P matrix is determined in 11ac style by assuming size of NHELTF × NHELTF.
  So P matrix is Nsts × NHELTF.
Legacy Preamble
1x HE Preamble
HE-STF
HE-STF
HE-STF
HE-STF
HE-LTF
PNsts1 x N_HELTF
HE-LTF
HE-LTF
HE-LTF
OFDMA-User-1 (Nsts_1)
OFDMA-User-2 (Nsts_2)
OFDMA-User-3 (Nsts_3)
OFDMA-User-4 (Nsts_4)

## Slide 12: Examples of Option 2
Suppose NHELTF = 6.
All users chooses the super P matrix as 11ac P6x6.
P for
Nsts=1
P for
Nsts=3
P for
Nsts=5
Reuse 11ac P matrices. No need to define new orthogonal matrices.

## Slide 13: HE-LTF P Matrix
Option 1:
Option 2:

## Slide 14: Comparison of Option 1 & 2
Option 1 and 2 are not equivalent only when N_VHTLTF cannot divide N_HELTF. Namely:
  N_HELTF = 6 and Nss = 3 or 4 (N_VHTLTF = 4)
  N_HELTF = 8 and Nss = 5 or 6 (N_VHTLTF = 6)
A unified P matrix generation at transmitter for option 2.
  Apply a single P matrix for each RU (up to different numbers of rows)
Noise suppression:
  Option 1 is not optimal in term of noise suppression, and the residual channel estimation error are colored across streams, due to the non-orthogonal P matrix.
  Option 2 always maximizes noise suppression (minimizes ChanEst MSE).

## Slide 15: Simulations
4x4 with TxBF, BCC
20MHz, D_NLOS channel
Actual channel estimation, no other impairment
4x HELTF symbols:
  Option 1: 6 HELTF symbols with a 4x4 P matrix and a circular repetition from 4 HELTF symbols
  Option 2: 6 HELTF symbols with a 4x6 P matrix
  Option 3: 4 HELTF symbols as a comparison
    This is to model another option of padding garbage for the last two HELTF symbols.
    This can also model a simple receiver ignoring the 2 circularly repeated HELTF symbols.

## Slide 16: Simulations (2)
Option 3 (4 HELTF symbols) have more than 1dB loss.
Option 2 has 0.5dB gain over option 1 for lower MCS and smaller gain in higher MCS.

## Slide 17: Conclusions
Two options of generating P matrix for OFDMA HE-LTF are discussed.
Using a uniform “super” P matrix has the benefits of noise suppression and simpler signaling.

## Slide 18: References
[1] 11-15-0132-06-00ax-spec-framework

## Slide 19: Straw Poll #1
Do you support that in an OFDMA PPDU, using N HE-LTF symbols, an RU with Nsts,total shall use the first Nsts,total rows of the N × N P matrix?