## Slide 1: Preamble Design and Auto-Detection for 11ax
Date: 2015-09-14
Authors:

## Slide 2: Abstract
In the same platform, the previously proposed repeated L-SIG[1] and signature symbol schemes[2] are evaluated
The repeated L-SIG scheme needs optimization efforts for repetition threshold considering a trade-off between false detection and mis-detection probabilities
The signature symbol scheme shows reasonable performance in both mis-detection and false detection
For a simple implementation and future extension, the signature symbol scheme is more preferred than the repeated L-SIG scheme

## Slide 3: Introduction
Repeated L-SIG (RL-SIG) [1]
  Modulating the RL-SIG (L-SIG repetition ) symbol with BPSK and rate ½ BCC.
  Detection from both a repetition check and an L-SIG validity check
Signature symbol (SS) [2]
  One symbol, MCS 0, separately encoded
    Signature of 10~12 fixed bits
    Additional info. of 6~8 bits
  Detect from checking a known signature after decoding
L-SIG 4us
HE-SIGA
R-LSIG 4us
BPSK
BPSK
BPSK
L-SIG 4us
HE-SIGA
Signature
4us
BPSK
BPSK
BPSK
…
…

## Slide 4: Simulation Environments
Bandwidth : 20MHz
Multi-antenna transmission with CSD: 1x1, 2x1, and 4x1
Wireless channel: TGac D and UMi
Carrier frequency offset (CFO): fixed at 40 ppm (@ 5GHz)
Phase noise (both at Tx/Rx): -41dBc
Real timing estimation & synchronization
Signature symbol configuration [2]
  12 bits for signature, 6 bits for tail, and 6 bits for random information
11ax detection algorithms
  Explain in the following pages
SIG-A assumption: 34 payload + 6 tail + 8 CRC bits (2 OFDM symbol)

## Slide 5: Detection Algorithm for 11ax : Repeated L-SIG (RL-SIG)
Timing/CFO compensation
Equalization
L-STF
L-LTF
Repetition Threshold > α
Legacy
Detection
MRC & L-SIG Validity Check
Y
N
N
t
L-SIG
RL-SIG
Y
11ax detect
11n
11ac
11a
The same detection algorithm in [1]
Repetition threshold, α
  Cross-correlation value btw. L-SIG and RL-SIG
L-SIG validity check
  Parity = OK
  L-Rate = 6Mbps
  L-Length (mod 3) = 0

## Slide 6: Detection Algorithm for 11ax : Signature Symbol (SS)
The same detection algorithm in [2]
Signature check
  After decoding with the tail bits, the 12 bits are matched with the known signature
Timing/CFO compensation
Equalization
L-STF
L-LTF
Signature Check
Legacy
Detection
Y
N
t
L-SIG
11ax detect
11n
11ac
11a
SIGNATURE

## Slide 7: Mis-Detection & False Detection
Mis-detection in the 11ax receiver
  When an 11ax PPDU is transmitted, an 11ax device detects it as other types of PPDUs
Two types of false detections
  Type 1 (to see impacts to legacy devices): When an 11ax PPDU is transmitted, a probability that an 11ac (or 11n) device detects it as an 11ac (or 11n) PPDU
    It should be checked if a new 11ax PPDU has unusual modulations in the position of 11n/11ac SIG-A symbols
  Type 2 (to see impacts from legacy PPDUs): When an 11ac (or 11n or 11a) PPDU is transmitted, a probability that an 11ax device detects it as an 11ax PPDU
In this contribution, the type 2 false detection is considered.
  Type 1 false detection has minimal system impact

## Slide 8: Mis-Detection Performance
The RL-SIG shows 1.0~1.5 dB gain compared to the SS scheme due to MRC combining of two L-SIG symbols
  The both schemes shows similar mis-detection curves to each of L-SIG errors
  L-SIG and mis-detection of SS
  L-SIG and mis-detection of RL-SIG
  1.0 dB
  Both schemes show error floors in UMi
  1.5 dB

## Slide 9: Mis-Detection Performance (cont’d)
Both schemes show no serious degradation or other noticeable aspects in multi-antenna transmissions
  Compared to 1x1 in TGac D, the 2x1 has approximately 1.0 dB gain @ 10-1
  Compared to 1x1 in UMi, the 4x1 has approximately 1.7dB gain @ 10-1
  1.0 dB
  1.7 dB

## Slide 10: False Detection for RL-SIG
The false detection increases as SNR increases for 11ac/11a PPDUs
Even at a high SNR, over 4% of 11ac PPDUs are detected as 11ax PPDU due to the high false detection
  The same trend is verified in AWGN (Appendix A)
Most of 11n PPDUs can be filtered out in the repetition check since it has QBPSK symbol
L-SIG
(BPSK)
SIG-A1
(BPSK)
11ac PPDU
L-SIG
(BPSK)
SIG-A1
(QBPSK)
11n PPDU
L-SIG
(BPSK)
Data
(QAM)
11a PPDU
11ax Receiver
Falsely Detected
as 11ax
Correctly Detected
as others
…
…
…
…
…
…
About 4%
false detection

## Slide 11: False Detection for RL-SIG (cont’d)
  In high SNR, 11a/11ac PPDUs are falsely detected as 11ax
  L-SIG validity check does not work properly in high SNR
  HE STA combines 11ac L-SIG and VHT-SIG-A1 (in MRC) for decoding
  If cross-correlation is high enough (according to our simulations, above 0), combined L-SIG + VHT-SIG-A1 successfully decodes as L-SIG.
    VHT-SIG-A1 is not trellis terminated and acts as interference to L-SIG.
    If combined second OFDM symbol (e.g. VHT-SIG-A1) is self-decodable (i.e. trellis terminated), the combined signal can be decoded either as L-SIG or the second OFDM symbol. (Appendix B)
    L-SIG at 0dB (AWGN) can be decoded with 99.7% probability (Appendix C)

## Slide 12: False Detection for RL-SIG (cont’d)
False detection and mis-detection probabilities trade-off
  With a large repetition threshold α (= tight repetition check), the false detection is reduced
  But the mis-detection increases (more 11ax PPDUs are filtered out in the repetition check stage)
False detection
decreases with α
Mis-detection
increases with α
Mis-detection is worse than Non-Combined L-SIG PER
Increase with SNR

## Slide 13: False Detection in the Signature Symbol
Good false detection probabilities in both indoor and outdoor channels
  Always lower than 10-3 (regardless of SNR and PPDU types)
  False detection that also checks SIG-A CRC is below 10-4
  Not seen above 10-4 when SIG-A CRC is checked
  Not seen above 10-4 when SIG-A CRC is checked

## Slide 14: Additional Simulations for RL-SIG: Repetition Detection with Pre-Equalized Symbols
Checking L-SIG repetition using pre-equalized (i.e. before channel equalization) has similar performance.
  The increases of the false detection is come from the validity check fail, not from the repetition check
Still increase with SNR
high mis-detection to keep the false detection low

## Slide 15: Additional Simulations in RL-SIG: L-SIG Length Modification in 11ax
11ax transmitter can set the L-Length field which has a modulo-3 of 1 or 2 instead of 0, and 11ax receiver can check it for L-SIG validity
  It can significantly reduce the false detection probability of 11ac PPDUs
The α of 0.3 or larger can keep the false detection lower than 10-3
The α of 0.3 or larger can keep the mis-detection lower

## Slide 16: Additional Simulations in RL-SIG: L-SIG Length Modification in 11ax (cont’d)
However, it has still a problem with falsely detecting of 11a as 11ax PPDU. 11a PPDU can be sent with modulo-3 payload length of 1 or 2 and MCS 0
  For example) RTS, CTS, and ACK has 20, 14, and 14 bytes which are modulo-3 of 2
  Beacon frames will have a modulo-3 of 1 or 2 with a probability of 2/3
Legacy frames of MCS 0 which may be management frames may face detection issue 11ax devices
The modulo length changes to L-SIG Length is NOT a fool-spoof solution

## Slide 17: Additional Simulations in RL-SIG: Coverage Gain of RL-SIG
After applying an advanced detection algorithm+ for RL-SIG, the false detection can be kept lower than 10-3, but the actual coverage improvement for data frames is non-existent
Both RL-SIG and SS have similar performance in Beacon of 150 byte, which is the smallest estimated size*
  *Note: the conventional (measured) size of Beacon frame is about 300 byte including some optional and vendor-specific features and both schemes has no difference in PER with 300 byte Beacon as well
Advanced detection algorithm can make the false detection low at all SNRs
+Note: based on simplified GLRT detection
Beacon
Mis-Detection
False-Detection

## Slide 18: Potential Issues in the RL-SIG
The false detection probability increases with SNR
  Worst case: 11ac PPDU or 11a PPDU with BPSK data (e.g. management or control packet)
  False detection results in loss of 11ac or 11a packet entirely
False detection can be mitigated with HE-SIG-A CRC check
  Results in more complex receiver architecture (due to potential 11n/11ac AGC symbol)
  Benefits of early detection (right after L-SIG) lost
L-SIG Length modification in 11ax can not be a complete solution of the false detection problem
  L-Length field in 11a PPDUs can have a modulo-3 of 2 especially in RTS, CTS, and ACK
Complex receiver architecture & optimization
  In order to get any MRC gains (from duplication), complex adaptive cross-correlation detection algorithms is needed.
  Implementation margin is likely to eat up any MRC gain.

## Slide 19: Conclusion
Repeated L-SIG scheme, has high false detection probability for 11ac PPDUs and 11a BPSK PPDUs.
  Extension of repeated L-SIG will be limited and may cause even more miss-detection/false detection issues.
  With the L-Length modification, most of essential 11a management frames can have the false detection issue
1 dB MRC gain of L-SIG is washed away when taking into account false detection issues.
  With wrong parameter configuration, even worst performance than single L-SIG decoding
  Even with use of advanced detection algorithms, coverage gain in data is non-existent
  Additional one symbol for pure repetition (i.e. RL-SIG) is wasteful
Signature symbol scheme is preferred
  Simple implementation (no additional optimization needed, no additional detection algorithm needed)
  Robust performance under any scenario
  Great future extension ability (additional 6~8 bits for 11ax and future use)

## Slide 20: Straw Poll
Do you support the following?
  HE PPDU is with a separately encoded signature symbol immediately after L-SIG. The bitwidth of the signature in the signature symbol is TBD.

## Slide 21: References
[1] 11-15-0579r3, Preamble Design and Autodetection
[2] 11-15-0643r0, Autodetection with Signature Symbol

## Slide 22: Appendix A: Verification in AWGN
Repetition Threshold > α
MRC & L-SIG Validity Check
Y
Y
N
N
L-SIG(1:24)
SIG-A(1:48)
Encoding
Encoding
AWGN
AWGN
(1:48 )
(1:48)
A
B
C
False detection prob. (= C/A)
  As SNR increases, the increase in the false detection can be seen as well in AWGN
  This increase comes from the L-SIG validity check (See the ratio C/B the next page)
Simple bit-level realization of 11ac PPDUs
take the first 48 modulated symbol
Combine two symbols

## Slide 23: Appendix A: Verification in AWGN (cont’d)
Validity check pass ratio = C/B
  For all SNRs, it has over 80% pass ratio and increases with an increase in α value
Repetition check pass ratio = B/A
  It is mostly independent to SNR and varies significantly with α value

## Slide 24: Appendix B: Effect from SIG-A Encoding
Assuming the interfered symbol (SIG-A1) is a self-decodable (i.e. trellis terminated within the symbol) (Blue curve),
  With some chances, the decoding Trellis of the combined signal (L-SIG + SIG-A1) can follow SIG-A1’s because it is also self-decodable
However, the current 11a/11ac/11n SIG-A1 is a portion of longer encoded information (Red curve),
  SIG-A1 is not self-decodable
  Therefore, highly likely to be decoded as L-SIG and pass the L-SIG validity check
Therefore, the L-SIG content check of the combined L-SIG is not useful
  50% chance of L-SIG validity check pass

## Slide 25: Appendix C: L-SIG PER in AWGN
Approximately 99.7% of L-SIG symbols can be decoded correctly even at 0 dB
  The 0 dB is almost equivalent to the condition combining an L-SIG symbol with the same powered random symbol without noise