## Slide 1: UL MU Random Access Analysis
Date: 2015-07-13
Authors:
Name | Affiliation | Address | Email
Yonggang Fang | ZTE |  | 
Bo Sun | ZTE |  | 
Kaiying Lv | ZTE |  | 
Weiming Xing | ZTE |  | 
Ke Yao | ZTE |  | 
He Huang | ZTE |  | 

## Slide 2: Abstract
802.11ax SFD specifies OFDMA to be supported.
UL MU transmissions can be
  scheduled by AP’s trigger frame if AP has knowledge about STA’s buffered data for UL transmissions, or
  triggered by AP to allow multiple STAs to perform UL MU random access to acquire TXOP for UL transmissions.
In this contribution, we will
  analyze the OFDMA based UL MU random access performance and related issues.

## Slide 3: Requirements in SFD
PHY
  Legacy Preamble
    An HE PPDU shall include the legacy preamble (L-STF, L-LTF and L-SIG), duplicated on each 20 MHz, for backward compatibility with legacy devices.
  HE Preamble
    HE-SIG-A (using a DFT period of 3.2 µs and subcarrier spacing of 312.5 kHz) is duplicated on each 20 MHz after the legacy preamble to indicate common control information
    Downlink HE MU PPDU shall include HE-SIG-B field, and the number of OFDM symbols of HE-SIG-B field is variable
    HE-STF of a non-trigger-based PPDU has a periodicity of 0.8 µs with 5 periods.
    The HE-STF of a trigger-based PPDU has a periodicity of 1.6 µs with 5 periods.
      A trigger-based PPDU is an UL PPDU sent in response to a trigger frame
    The HE-LTF shall adopt a structure of using P matrix in the data tones as in 11ac.

## Slide 4: Requirements in SFD
UL MU OFDMA
  An UL MU PPDU (MU-MIMO or OFDMA) is sent as an immediate response (IFS TBD) to a Trigger frame (format TBD) sent by the AP.
  HE-PPDU for UL-OFDMA shall support UL data transmission below 20 MHz for an HE STA.
  The amendment shall include a mechanism to multiplex BA/ACK responses to DL MU transmission.

## Slide 5: UL MU Access Procedure
    Basic UL MU Access Procedure (example)
      HE UL MU random access
      HE UL MU transmissions
      HE UL Re-transmission
AP
HE Trigger for UL MU RA
Response
by STA1
Response
by STA2
Response
by STA3
Response
by STA4
MU STAs
AP
MU BA
MU BA
MU BA
MU BA
MU STAs
HE UL MU RA
PPDU from STA1
PPDU from STA2
PPDU from STA3
PPDU from STA4
HE UL MU Transmission
AP
HE Resource Allocation.
PPDU from STA3
HE UL MU Re-Transmission
MU BA
MU STAs
AP

## Slide 6: UL MU Random Access
    Requirements of Trigger Frame for RA
      Indication of UL MU procedure commence
      TXOP protection
        Protect other STAs including legacy STAs to content the medium in the TXOP
      Synchronizations
        Trigger MU STAs to perform frequency and timing synchronization with the AP so that the following UL MU transmissions from MU STAs could be aligned up at AP receiver.
      Polling Function
        Poll a list of STAs to allow them to transmit UL buffered data information
      Access Category
        Have higher priority over other frames to acquire the medium.
      Resource Allocation
        AP needs to schedule RBs for MU transmissions
        Power control level
        Allowed MCS rate

## Slide 7: UL MU Random Access Analysis
    KPIs for OFDMA Random Access
      Trigger frame
        Overhead
        Random access latency
      Trigger based OFDMA response
        Success rate
        Overhead
        Padding Efficiency

## Slide 8: Trigger Frame Overhead
    Trigger Frame Format
      Trigger frame is a special management/control frame to control RA TXOP or resource allocation for UL transmission. It has not decided yet how to define trigger frame, but some or more content should be considered in the trigger frame. For example:
      Common field:
        Min Access Category
        Length of STA Info
      STA Info
        AID or Temp AID
        Resource Block
L-Preamble
HE SIG
MPDU
FC
Duration
TA
…
STA n
Info
FCS
Common
Info Field
STA 1
Info
2B
2B
6B
2B
4B
Min AC
Length
AID
RB
2B
2B
2B

## Slide 9: Trigger Frame Overhead
    Overhead in Single BSS
      Assumptions
        Preambles size
          11ax preamble = L-Preamble + HE-Preamble (TBD) = 40us (same as 11ac)
        Transmission rates
          Use reliable MCS rate for legacy protection: 6Mbps
      Trigger Frame Overhead
        For polling 9 STAs for OFDMA based contentions
          80us + 2* xSIFS = 112 us
        For polling 20 STAs for OFDMA based contention
          109us + 2* xSIFS = 141 us

## Slide 10: Trigger Frame Overhead
    Overhead in Multi-BSS
      Assumption
        Deployment case based on Scenario 3 of 802.11ax Simulation Scenario [5]
          19 cells with cell radius R = 10m,
          reuse factor = 3.
          10+ APs could be seen in OBSS [2]
        Trigger Transmission: is sent every 10ms
      Total Trigger Frame Overhead
        Trigger frame transmission by 10+AP will cause 1.4 ms overhead in 10ms period, which is about 14% air time used for trigger frames.
        If using RTS/CTS to protect trigger frame transmission, overhead would be even higher.

## Slide 11: Trigger Based Random Access Latency
    OFDMA RA
      If a trigger frame is used to trigger the random access procedure, it needs to be transmitted as often as possible. Otherwise, it would cause more random access latency comparing to CSMA/CA.
      Assumptions
        Assume the trigger frame is transmitted every 10ms.
        40 STAs per BSS, and 50% STAs have buffered data for UL transmissions
      Access delay
        If only 9 STAs are allowed to perform contention per trigger frame (for reduce collision probability), the probability that buffered STAs get a chance to contend is 22%, and half of them may transmit.
        If the STA depends on trigger frame (sent every 10 ms) to perform random access, the the average random access delay is > 5ms.

## Slide 12: Trigger Based OFDMA RA Response
    Success Rate and Collision Probability
      If the allocated RB for RA and STA is not 1-to-1 mapping, there exists collision probability for two STAs to contend the same RB. To control collisions, AP may need to limit the number of STAs for RA.
      Assume that AP allows N of STAs to perform RA after trigger frame, which can randomly transmit trigger response in UL MU PPDU format, if they have buffered data.
MU Spatial / Frequency Domain
AP
HE Trigger for UL MU RA
MU STAs
AP
HE Trigger for Resource Allocation.
Response by STA3
Response by STA6
Response by STA7
Response by STA1
      The maximum success transmission probability is 37% (slotted aloha model), which means at least 63% spectrum are wasted in OFDMA based random access. The more time the OFDMA RA trigger responses take, the less spectrum efficiency.

## Slide 13: Trigger Based OFDMA RA Response
    OFDMA PHY Overhead
      Assume HE PHY use following format
        Legacy and HE-SIG-A shall be same as they are transmitting over 20MHz.
          L-Preamble = 20us;
          HE-SIG-A = 2 x (3.2 + 0.8) = 8us
        HE-STF and HE-LTF may need to transmit over the allocated sub-channel.
          HE-STF = 1.6us x 5 = 9us
          HE-LTF = 6.4 (or 12.8)us + 0.8 (or1.6 or3.2)us <= 16us
        Total PHY header <= 53us
L-STF
L-LTF
L-SIG
HE- SIG-A
HE-STF
HE-LTF
Data

## Slide 14: Trigger Based OFDMA RA Response
    UL OFDMA MAC Overhead
      Assume HE payload is used to get bandwidth request. Therefore it could use same frame format.
        Total MAC size = 15B
          MAC Header = 10B
          Buffer Info = 1B
          FCS = 4B
        If using lowest MCS to transmit over one RB, the data rate would be 26/16us = 1.6Mbps. It takes 15 *8 / 1.6 = 75us
      The total OFDMA trigger response time (PHY + MAC): 75us + 53us = 128us
      If each STA would transmit individual payload with different size, it would take longer time and have deficiency issue of OFDMA padding
FC
Duration
TA
FCS
Buffer Info
2B
2B
6B
1B
4B

## Slide 15: Trigger Based OFDMA RA Response
    UL OFDMA Gain
      [4] analyzed MAC overhead on the impact of UL MU gain vs SU and provided the simulation results
      For 20MHz bandwidth,
        The gain of UL MU decreases as the data size increases since the overhead in UL SU transmissions would decreases.
        The control exchange overhead for UL MU should be less than a certain time in order to gain UL MU transmission.
        With the similar constrain of maximum control frame exchange, more STAs allowed for MU would provide higher gain.
 | 4 STAs | 8 STAs | 
Gain of UL MU vs SU for 20 OFDM symbols payload | 1.5x | 1.5x | 2.5x
Max overhead for control frame exchange | 178us | 633us | 184us

## Slide 16: Trigger Based OFDMA RA Response
    Gain of UL MU vs SU
      If the trigger frame size takes 80+ us for example, it only leases 523us for the trigger responses based on the maximum time limit for control frame exchange (1.5x gain).
      Therefore it needs to design an efficiency way for UL MU random access procedure.
MU Spatial / Frequency Domain
AP
HE Trigger for UL MU Random Access
Response
by STA1
Response
by STA2
Response
by STA3
Response
by STA4
MU STAs
UL MU Control Frame Exchange
AP
HE Resource Allocation.
SIFS
SIFS
80+us
???
 | 8 STAs | 
Gain of UL MU vs SU for 20 OFDM symbols payload | 1.5x | 2.5x
Max overhead for control frame exchange | 633us | 184us
Trigger + 2 * SIFS | 110us | 110us
Max Trigger Response Time | 523us | 74us

## Slide 17: Trigger Based OFDMA RA Response
    OFDMA Padding Deficiency
      [3] provides analysis and simulation results for the OFDMA based transmission efficiency.
      Due to longer symbol duration, OFDMA would cause excessive padding in OFDMA transmissions. Especially when sending short packets in wide bandwidth, transmission efficiency drops significantly due to padding issue.
 | 40 +44bytes1 | 576+44bytes2 | 1500+44bytes3
MCS0 (80MHz, NSTS = 1) | 45.8% | 8.67% | 3.14%
MCS1 (80MHz, NSTS = 1) | 45.8% | 18.6% | 3.14%
MCS2 (80MHz, NSTS = 1) | 119% | 18.6% | 7.11%
MCS3 (80MHz, NSTS = 1) | 192% | 18.6% | 11.1%
MCS4 (80MHz, NSTS = 1) | 338% | 18.6% | 19.0%
MCS5 (80MHz, NSTS = 1) | 483% | 58.1% | 26.9%
MCS6 (80MHz, NSTS = 1) | 556% | 77.8% | 7.11%
MCS7 (80MHz, NSTS = 1) | 629% | 97.6% | 19.0%
MCS8 (80MHz, NSTS = 1) | 775% | 18.6% | 42.8%

## Slide 18: Code Based Contention
    OFDMA Padding Deficiency
      If each STA is allowed to transmit any size payload in OFDMA random access TXOP, it has more severe issue of padding and would cause more waste.
        Since AP does not know STA’s buffered data information, it cannot give accurate random access duration in the trigger frame.
        As a STA does not know size of PPDU of other STA’s OFDMA transmissions, it has to pad the empty payload till the end of the random access duration.
MU Spatial / Frequency Domain
AP
HE Trigger for UL MU RA
MU STAs
AP
HE Trigger for Resource Allocation.
Response by STA3
Response by STA6
Response by STA1
      The better way to avoid padding issue is to keep same length of transmissions in UL MU OFDMA.

## Slide 19: Summary
    Conclusion
      Trigger frame used to for random access might have some issues that impacts on user experience
        Longer random access latency
        Less transmission efficiency (time waste v.s. retransmission due to collision)
        Higher overhead.
      Trigger response efficiency decreasing due to
        Padding caused by UL MU OFDMA
        Overhead caused by extra frame exchange.
      We need some mechanism
        Reducing trigger frame overhead
        Improving trigger response efficiency
        Reduce the random access latency

## Slide 20: References
11-15-0132-05-00ax-spec-framework
11-15-0362-00-00ax-beacon-issues-2
11-15-0572-00-00ax-phy-inefficiency-of-256-fft-per-20mhz
11-15-0336-01-00ax-mac-overhead-analysis-of-mu-transmissions
11-14-0980-12-00ax-simulation-scenarios