## Slide 1: LTF Design for Uplink MU-MIMO
Date: 2015-07-13
Authors:

## Slide 2: LTF Sequence for Uplink MU-MIMO
LTF Sequence masking with orthogonal codes was proposed for Uplink MU-MIMO operation [1].
The idea is to allow full channel estimation within a symbol to allow phase/frequency offset tracking.
There are two issues with the proposal
  Orthogonal code masking does not create orthogonal codes due to CSD application in different spatial streams.
    May require complex receivers for tracking frequency/phase
  Code masking to the entire LTF sequence results in very high PAPR sequence.

## Slide 3: Non-Orthogonality of P matrix Masking
L1
L2
L3
L4
L5
L6
L7
L8
[ 1 -1 1 1 ][ 1 -1 1 1 ]
Row 1 of P matrix
x
x
[ 1 1 1 1 1 1 1 1 ]
CSD for SS#1
L1
L2
L3
L4
L5
L6
L7
L8
[ 1 1 -1 1 ][ 1 1 -1 1 ]
Row 2 of P matrix
x
x
[ 1 ej2πθ ej2π2θ ej2π3θ ej2π4θ ej2π5θ ej2π6θ ej2π7θ ]
CSD for SS#2
HE LTF Sequence 1
HE LTF Sequence 2
L1
–L2
L3
L4
L5
– L6
L7
L8
L1
ωL2
-ω2L3
ω3L4
ω4L5
ω5L6
-ω6L7
ω7L8
NOT ORTHOGONAL

## Slide 4: Cross Correlation between LTF Spatial Streams
To quantify the non-orthogonality between different LTF spatial streams, we have computed cross correlation between them.
  When spatial stream are completely orthogonal cross correlation terms would be zero.
  Not all LTF spatial streams are equal, some stream pair have worse interference between each other than other stream pairs.
 | SS #1 | SS #2 | SS #3 | SS #4 | SS #5 | SS #6 | SS #7 | SS #8
SS #1 |  | 0.002406 | 0.049069 | 0.29361 | 0.343407 | 0.000507 | 0.000301 | 0.033816
SS #2 |  |  | 0.098141 | 0.049069 | 2.31E-07 | 0.245362 | 0.00542 | 0.003688
SS #3 |  |  |  | 0.002406 | 0.000678 | 0.01219 | 0.09817 | 0.000307
SS #4 |  |  |  |  | 0.003764 | 7.53E-05 | 0.000231 | 0.147246
SS #5 |  |  |  |  |  | 0.001354 | 0.061323 | 0.196079
SS #6 |  |  |  |  |  |  | 0.269276 | 0.024541
SS #7 |  |  |  |  |  |  |  | 0.00634
SS #8 |  |  |  |  |  |  |  | 

## Slide 5: Residual Frequency/Phase Offset Compensation with P matrix masked LTF symbols
perform de-spreading per stream
Received LTF symbols (freq-domain)
D
estimate residual
frequency/phase offset
Compensated LTF symbols for time domain de-spreading processing
‘K’ de-spreaded tones used for residual frequency/phase offset
Nss x 242
Nss x K
Nss x K
fo &θ per STA
Nss x 242
Note:
We have performed tests with various K.
Obviously high K values means higher complexity at the AP receiver.
(The chosen tones were evenly spaced across frequency for diversity effects)

## Slide 6: P-Matrix De-spreading
L1 ejθ
L2 ej2θ
-L3 ej3θ
L4 ej4θ
L5 ej5θ
L6 ej6θ
-L7 ej7θ
L8 ej8θ
L9 ej9θ
L10 ej10θ
-L11 ej11θ
Freq.
LTF sequence w/ CSD
L1* e-jθ
L2* e-j2θ
-L3* e-j3θ
L4* e-j4θ
L5* e-j5θ
L10* e-j10θ
L11* e-j11θ
x
h1
h2
…
x
…
…
h10
…
In total ‘M’ number of potential channel coefficient estimates from de-spreading
Selectively compute
(sub-sample)
h2
h6
h10
…
Total of ‘K’ number of channel coefficient estimates for frequency/phase tracking
…

## Slide 7: Simulation Setup
Simulation Assumption
  BW: 20MHz
  Channel Model: TGac Channel D
  Configuration:
    4 Rx AP with FOUR of 1 Tx STA
    8 Rx AP with SIX of 1 Tx STA
  Transmit timing spread among users: spread uniformly within 0us, 0.5us, and 1us
  Identical SNR among STAs
  MCS 6, Payload Size 1000 Bytes
  IPN: -41dBc (both at Tx and Rx)
  Real frequency/phase offset tracking
    ‘K’ de-spread channel coefficients in frequency domain was used in tracking
    de-spread channel coefficients in time domain (after frequency/phase compensation) used in data symbol equalization
  Real channel estimation
To compare the effect of non-orthogonality, we have also compared with applying block CSD (i.e. phase is rotated every 8 tones) [see APPENDIX]

## Slide 8: Performance with LTF P matrix masking (1/5)
In order to combat non-orthogonality of the P matrix with CSD, residual frequency/phase offset compensation MUST be performed with MANY tones
We can see that if P matrix is perfectly orthogonal freq./phase offset tracking works even with 4 values (i.e. tones)
4 Rx AP
1Tx, 4 STA w/ 1 SS
0us transmit time spread among STAs

## Slide 9: Performance with LTF P matrix masking (2/5)
Similar trend can be observed with transmit time dispersion among STAs
4 Rx AP
1Tx, 4 STA w/ 1 SS
0.5us transmit time spread among STAs

## Slide 10: Performance with LTF P matrix masking (3/5)
Similar trend can be observed with transmit time dispersion among STAs
4 Rx AP
1Tx, 4 STA w/ 1 SS
1us transmit time spread among STAs

## Slide 11: Performance with LTF P matrix masking (4/5)
8 Rx AP
1Tx, 6 STA w/ 1 SS
0us transmit time spread among STAs
Non-orthogonality issue impacts performance more critically when more spatial streams are used.

## Slide 12: Performance with LTF P matrix masking (5/5)
8 Rx AP
1Tx, 6 STA w/ 1 SS
0.5us transmit time spread among STAs
Similar trend

## Slide 13: PAPR issue with P matrix masking
PAPR effects implementation complexity/cost of the transmit RF components.
PAPR of the LTF symbols used for channel estimation should be sufficiently lower than data PAPR.
LTF sequences are typically designed such that low PAPR property is met.
Multiplication of P matrix across the ENTIRE transmitted tones, completely destroys nice PAPR property of LTF sequences.

## Slide 14: PAPR of LTF Symbols with P matrix Masking
Observation:
P matrix masked LTF can have up to 8.8 dB PAPR
There is 80% probability that data OFDM symbols have less than 8.8dB PAPR.
P matrix masked LTF OFDM symbols have higher mean/median PAPR than data OFDM symbols

## Slide 15: Conclusion
We have identified significant issues with LTF masked with P matrix for Uplink MU-MIMO as proposed in [1].
The proposal creates several implementation challenges and requires highly complex receiver implementation.
We urge that further study to be performed on LTF design for uplink MU-MIMO as it has critical impact to performance and implementation.

## Slide 16: Strawpoll
Do you agree that more analysis of implementation complexity and performance on various scenarios is needed for uplink MU-MIMO LTF design?
Y/N/A:

## Slide 17: References
[1] IEEE802.11-15/0602r1, “HE-LTF Sequence for UL MU-MIMO,” May 2015.

## Slide 18: Appendix: Example of Block CSD vs Regular CSD
Regular CSD (every tone)
Block CSD (every 4 tones)
L1
L2
L3
L4
L5
L6
L7
L8
[ 1 1 -1 1 ][ 1 1 -1 1 ]
Row ‘m’ of P matrix
x
x
[ 1 ej2πθ ej2π2θ ej2π3θ ej2π4θ ej2π5θ ej2π6θ ej2π7θ ]
CSD for SS #m
LTF sequence
Final Output Sequence
L1
L2
L3
L4
L5
L6
L7
L8
[ 1 1 -1 1 ][ 1 1 -1 1 ]
x
x
[ej2πθ ej2πθ ej2πθ ej2πθ ej2π5θ ej2π5θ ej2π5θ ej2π5θ ]
Final Output Sequence
Phase of CSD changed every few tones
Phase of CSD changed every tone
Not Orthogonal
Orthogonal