## Slide 1: NGP Use Cases Discussion
Date: 2015-07-12
Authors:

## Slide 2: Abstract
Three new use cases are presented in the contribution

## Slide 3: 1. Hospital Equipment/Drug Management
User: Doctors/Nurses who uses smart phones/Pad to trace Equipment and Drugs
Environment: A hospital has APs for 802.11 coverage. Now Wi-Fi is available in almost all the hospitals
Use case:
  There all many kinds of equipments doctors and nurses need to track, for example, oximeter, electrocardioscopy, all kinds of antivirus and antibiotics. The drugs might be sorted out and stored at certain places however precisely finding them is not easy work. And equipments may not be located at a fixed location due to random usages of the doctors and nurses.
  For each patient staying at hospital, nurses need to prepare their treatment according to the prescription from doctor and also running routine medical inspection.
  The treatment of each patient should be different even in the same ward
  A nurse with the tracing equipment when visiting certain patient immediately knows where to collect all the equipments and drugs needed for that particular patient.
Key Performance and Attributes:
  Horizontal accuracy: <0.5 m@90%, vertical accuracy: <0.5 m same floor@99%
  Latency: <500ms
  Refresh Rate: > 1 location/sec
  Number of simultaneous users – depends on the size of the hospital, typical scenario will be 50~serveral hundreds
  Power-Location Estimate Tradeoff – navigation and tracing medical care equipments
  Usage Duration – 24hours
  Impact on Network Bandwidth -- < 3 additional frames per second/device/estimate
Chaochun Wang (MTK Inc.)

## Slide 4: 2. Logistics Network Management
User: Employees of express delivery company, Logistics Robots
Environment: A Logistic Network Interim Station that has APs for 802.11 coverage. The expected AP density is about 1 AP per 4000 sq. ft. with APs supporting HT, VHT and NGP
Use case:
  When items and packages to be delivered come to the interim stations of the logistics network, they will be temporally stored for the next delivery
  In order to deliver the package to the end user timely, Grouping and categorization of the items and packages are required for the stuff members/robots to fast locate them for the next delivery. However grouping itself takes time and slow down the whole process.
  Instead, when the package enters the station, they will be tagged with Wi-Fi chip that has NGP capability. And the package will be randomly put on unified 3D shelf temporally.
  The stuff members/ Robots will locate these packages with a Wi-Fi tag tracer once the delivery order is made
Key Performance and Attributes:
  Horizontal accuracy: <0.5 m@90%, vertical accuracy: <0.5m same floor@99%
  Latency: <500ms
  Refresh Rate: > 1 location/sec
  Number of simultaneous users – depends on the size of the logistics network (a few to as many as 100s)
  Power-Location Estimate Tradeoff – navigation and tracing package for express delievry
  Usage Duration – 24 hours /7 days
  Impact on Network Bandwidth -- < 3 additional frames per second/device/estimate
Chaochun Wang (MTK Inc.)

## Slide 5: 3. Smart Push Notification/Payment
User: Consumers enter store, users of social Wi-Fi
Environment: A store, restaurant or coffee shop has APs for 802.11 coverage. Now Wi-Fi is available in almost all the restaurants and coffee shop
Use case:
  The user enters the store, restaurant and coffee shop with their phone
  Users normally has their own preference and habits. They set their profile before enter the shops.
  Push Notification only happens when the users get close enough to their preferred items in order to avoid garbage push notifications.
Key Performance and Attributes:
  Horizontal accuracy: <0.5 m@90%, vertical accuracy: same floor@99%
  Latency: <500ms
  Refresh Rate: > 1 location/sec
  Number of simultaneous users – depends on the size of the shops(a few to as many as 100s)
  Power-Location Estimate Tradeoff – navigation and shopping
  Usage Duration – depends on shopping habit (a few minutes to a few hours)
  Impact on Network Bandwidth -- < 3 additional frames per second/device/estimate
Chaochun Wang (MTK Inc.)

## Slide 6: 4. Indoor Parking for Automatic Driving Cars
User: Automatic Driving Cars, Normal cars with Automatic Driving Assistance
Environment: Indoor Parking that has APs for 802.11 coverage.
Use case:
  The user drives car into the indoor parking, or Automatic driving cars enter indoor parking
  Indoor positioning system helps cars to locate parking lots and automatically parks the car for users
Key Performance and Attributes:
  Horizontal accuracy: <0.5 m@90%, vertical accuracy: 0.5<same floor@99%
  Latency: <500ms
  Refresh Rate: > 1 location/sec
  Number of simultaneous users – depends on the size of the parking(a few to as many as 100s)
  Power-Location Estimate Tradeoff – navigation and shopping
  Usage Duration – at least 15 hours per day
  Impact on Network Bandwidth -- < 3 additional frames per second/device/estimate
Chaochun Wang (MTK Inc.)

## Slide 7: References
11-07-2988-04-0000-liaison-from-wi-fi-alliance-to-802-11-regarding-wfa-vht-study-group-consolidation-of-usage-models.ppt
11-14-1464-02-0wng-ng-positioning-overview-and-chalanges.pptx
11-15-0388-00-0ngp-ng-NGP Use Case Template .pptx
Ganesh Venkatesan (Intel Corporation)