## Slide 1: Channel Sounding for 802.11ay
Date: 2015-07-14
Authors:

## Slide 2: Abstract
In this presentation, we show the first 60 GHz ultra-wide-band measurement results at a large entrance hall scenario. We show that the coverage of 60 GHz can be very large. Another points which we like to discuses are the calibration problems of the AGC.
We like also to discuss the requirements for the outdoor measurement campaigns.

## Slide 3: Outline
Motivation
60 GHz Entrance Hall Measurements
Measurement results
Result discussion
Conclusion

## Slide 4: Motivation
ISM-band at 60 GHz
  Free and wide bandwidth available (up to 7 GHz)
  WLAN/WiGig (.11ad) and WPAN (.15.3.c)
Advanced system concepts  define measurement and modelling requirements
  Massive MIMO/pencil beam-forming  large spatial bandwidth
  Adaptive or switched selection beam-forming to mitigate shadowing
  Channel bonding  large bandwidth
Propagation channel measurements
  Double directional measurements are needed to characterized the full channel
  Polarization is an important aspect
  High dynamic range are essential to measure the different propagation effects
Channel characterization for different usage cases

## Slide 5: Summary of Measurement Activities
# | Applications and Characteristics | Propagation conditions | Experimental setup description | Responsible companies
1 | Ultra Short Range (USR) Communications -Static,D2D, -Streaming/Downloading | LOS only, Indoor <10cm | TBD | TBD
2 | 8K UHD Wireless Transfer at Smart Home -Umcompressed 8K UHD Streaming | Indoor, LOS with small NLOS chance, <5m | Living room environment, 8 TX by 16 RX, stationary | NIST
3 | Augmented Reality/Virtual Reality Headsets and Other High-End Wearables -Low Mobility, D2D -3D UHD streaming | Indoor, LOS with small NLOS chance <10m | Living room environment, 8 TX by 16 RX, non-stationary | NIST
4 | Data Center 11ay Inter-Rack Connectivity -Indoor Backhaul with multi-hop* | Indoor, LOS only <10m | Server room environment, 8 TX by 16 RX, stationary | NIST
5 | Video/Mass-Data Distribution/Video on Demand System - Multicast Streaming/Downloading - Dense Hotspots | Indoor, LOS/NLOS <100m | Entrance large hall, lecture room | Huawei, Intel
6 | Mobile Offloading and Multi-Band Operation (MBO) -Multi-band/-Multi-RAT Hotspot operation | Indoor/Outdoor, LOS/NLOS <100m | Indoor: Entrance large hall/ Outdoor: Above roof top to street level | Huawei
7 | Mobile Fronthauling | Outdoor, LOS <200m | Above roof top to street level | Huawei
8 | Wireless Backhauling -Small Cell Backhauling with single/multi-hop | Single hop: outdoor, LOS <1km Multi hop: Outdoor, LOS <150m | Above roof top, street level | Huawei, Intel

## Slide 6
60 GHz Entrance Hall Measurements

## Slide 7: Dual Polarimetric Ultra-Wideband Channel Sounder (DP-UMCS)
7 GHz BW up to 10 GHz measurable bandwidth
Maximum excess delay of 606 ns (180 m) in CS version 1 and excess delay of 4,7 µs (1404m) in CS version 2
Dual polarization measurement capability
25 dB AGC (Automatic Gain Control) with 3.5 dB steps
High instantaneous dynamic range: up to 75 dB  Version 2 provide around 80 dB
Multi-Link and Massive MIMO capabilities
Double directional measurements (with 1 TX and 2 RX)
Multiplier
X8
PA min. 23 dBm
7 GHz
Oscillator
Multiplier
X8
LNA
Gain : 35 dB
UWB Sounder RX
0 – 3.5 GHz
3.5 GHz - 10.5 GHz
H Pol.
V Pol.
CH 1
CH 2
H Pol.
V Pol.
Switch
TX Module
RX Module
56 - 66 GHz
56 - 66 GHz
PA min.
23dBm
Step
Attenuator
LNA
Gain : 35 dB
UWB Sounder TX
0 – 3.5 GHz
3.5 GHz - 10.5 GHz
Optical link
Optical link
Step
Attenuator

## Slide 8: Entrance Hall Scenario
Dimensions:
7 x 25m x 9m
Class and metal
3 different floors

## Slide 9: Entrance Hall Scenario
Entrance Hall of Zuse – Bau at TU Ilmenau
1 Tx Positions (1 Tx in the ground floor)
9 Rx Positions (all in the ground floor)
Tx 1
Rx 1
Rx 2
Rx 3
Rx 14
Rx 4
Rx 9
Rx 10
Rx 2
Rx 1

## Slide 10: Measurement Set-Up
Static access point scenario
Tx:
  Located on the side of the wall
  Height from ground 2.5 m
  30°HBW of the antenna with 14 dBi
  Output Power around 5 dBm
Rx:
  Located at several points in the hall
  Height 1.4m
  30°HBW of the antenna with 14 dBi
Frequency range:
  57.3 GHz – 64 GHz
Scanning at Tx and Rx stage via positioners
Tx: Azimuth -90°... 30° 90° Elevation -90°…30°…90°
Rx: Azimuth -180°…30°…150°
A
B
C
+
-
+
-
Tx X
Rx 1
2.8m
5m
5m
5m
Rx 2
Rx 3
Rx 4
Azimuth 0°
Azimuth 0°
Rx 12
Rx 13
Rx 14
Rx 10
Rx 9

## Slide 11: Measurement results

## Slide 12: Data Set
Data set
Output of the channel sounder:
Where:
x: Tx polarization (in direction of or )
y: Rx polarization (in direction of or )
: delay sample
: Tx azimuth position
: Tx elevation position
: Rx azimuth position

## Slide 13: Data Pre-processing
Calibration
2 steps calibration:
  Deconvolution + windowing with the UWB units back to back calibration
  Deconvolution with the in-situ LOS measurement calibration to eliminate antenna and up / down converter effects
Noise floor estimation and removal
Samples lower than the noise floor + 10dB are set to zero
Calibration issues
  AGC calibration wasn’t complete performed  problems in the Insitu calibration with the high power  The problems will be solve by a back to back calibration

## Slide 14: Tx 1 – Rx 1 pLOS
Normalized Power Elevation / Azimuth Profile at Tx
Normalized Power Azimuth / Azimuth Profile at Tx and Rx

## Slide 15: Tx 1 – Rx 9 NLOS
Normalized Power Elevation / Azimuth Profile at Tx
Normalized Power Azimuth / Azimuth Profile at Tx and Rx

## Slide 16: Tx 1 – Rx 12 pLOS
Normalized Power Elevation / Azimuth Profile at Tx
Normalized Power Azimuth / Azimuth Profile at Tx and Rx

## Slide 17: Tx 1 – Rx 13 NLOS
Normalized Power Elevation / Azimuth Profile at Tx
Normalized Power Azimuth / Azimuth Profile at Tx and Rx

## Slide 18: Power Angular Profile of all Receivers
The azimuth plane have a bigger impact than the elevation plane on the path loss of the 60 GHz channel
But we use here antennas withe a
3dB beamwidth of 30°

## Slide 19: Calculation
Power Delay Profile

## Slide 20: PDP Tx 1
Power Delay Profile Rx 1
Power Delay Profile Rx 2
Power Delay Profile Rx 3
Power Delay Profile Rx 4

## Slide 21: PDP Tx 1
Power Delay Profile Rx 9
Power Delay Profile Rx 10
Power Delay Profile Rx 12
Power Delay Profile Rx 13

## Slide 22: What is the right unambiguous range for 60 GHz measurements?

## Slide 23: List of Parameters
Tx | Rx | LOS / NLOS | DS [ns] | MED [ns] | AS at Tx [°] | ES at Tx [°] | AS at Rx [°] | Rx Energy [dB]
1 | 1 | pLOS | 27,04 | 173,18 | 71,59 | 55,42 | 86,03 | 8,23
1 | 2 | pLOS | 33,53 | 207,25 | 67,40 | 54,67 | 79,68 | 7,69
1 | 3 | pLOS | 39,87 | 160,59 | 64,29 | 47,97 | 84,16 | 7,47
1 | 4 | pLOS | 40,97 | 154,81 | 66,35 | 49,44 | 77,66 | 9,19
1 | 9 | NLOS | 28,10 | 116,14 | 53,50 | 41,22 | 73,38 | 2,77
1 | 10 | NLOS | 44,08 | 213,62 | 69,15 | 46,17 | 80,89 | 2,68
1 | 12 | pLOS | 34,99 | 160,14 | 52,91 | 43,71 | 36,17 | 3,35
1 | 13 | NLOS | 58,35 | 200,00 | 70,25 | 50,74 | 34,47 | -3,01
1 | 14 | pLOS | 25,44 | 114,07 | 50,89 | 59,07 | 73,19 | 9,85
DS: delay spread  Path extraction: 20 dB threshold from maximum peak
MED: maximum excess delay  from maximum peak to the estimated noise floor
AS: azimuth spread (at the Rx calculated for the cyclic angles since 360°measurements were available).
ES: elevation spread.
Rx Energy: un-calibrated data
The AGC was not full de-embedded (only the theoretical values)

## Slide 24: Result discussion
Double directional measurements
All was full polarimetric
9 positions
The azimuth plane at Tx has a greater impact on the power
Delay Spread
  For LOS is the DS with a threshold of 20 dB smaller than 40ns
  For NLOS is the DS with a threshold of 20 dB smaller than 60ns
Maximum Access Delay
  For LOS is the DS with a threshold of 20 dB smaller than 210ns
  For NLOS is the DS with a threshold of 20 dB smaller than 220ns
Measurement issues
  AGC calibration wasn’t performed  problems in the Insitu calibration with the high power
  Only azimuth scan at the RX Outdoor measurement with 1 TX and 2 RX and azimuth and elevation scan on booth side

## Slide 25: Conclusion/Discussion
We present 60 GHz entrance hall measurements
  Measurement bandwidth of 7 GHz  analysis of channel bonding possible
  The capability of MIMO measurements
  The unambiguous range (606 ns) of the CS system is to small for this scenarios
  Polarization effects are clearly visible
Next Steps
  Extension of the calibration  AGC calibration for dual pol. waveguide systems
  Outdoor: Above roof top to street level measurements
    How many measurement points are required/meaningful?  measuring time
    Which resolution for the azimuth and elevation scan? measuring time
    Which range for the azimuth and elevation at TX and RX for the different scenarios are useful?
     measuring time
Notes:   5G systems at mm-wave require SNR optimisation  and this will be only done with dual polarisation