## Slide 1: LRLP Topic Interest Group Supplemental Presentation for WG Motion
Date: 2015-07-17
Author:

## Slide 2: Description of Use Cases
Leverage the mass-market WLAN infrastructure for reliable, consistent, and stable access to Internet and “Cloud” services.
Applications focused on M2M and IoT
  Not for bulk data transfer
  Devices may be AC line connected or battery powered
  Scheduled or coordinated medium access compliant
Smart Grid, energy management, and sensors
  Fixed location
  Out of way location (hot water heater, pool pump)
  Poor propagation – e.g. side of white goods appliance
Indoor and outdoor applications
  Premises or property scale – not a neighborhood area network
  Eliminate need for “range extenders”

## Slide 3: Requirements
Long Range: at least 10 dB link margin improvement
Low Power: average consumption of 50uW, 5 year batt
“Zero” marginal cost for implementation
  Available in “all” next-generation 802.11 AP chipsets
  Possible to define “LRLP only” STA
Relatively low aggregate data rate ~ 512Kbps
  Actual PHY data rate may be higher
Coexistence and limited impact on primary BSS
  Protection mechanisms, media occupancy limit, duty cycle limit, etc.

## Slide 4: Next Steps
The WG Chair suggested an Interest Group as the optimal path forward for this activity
The Straw Polls in WNG indicated a preference to form an Interest Group rather than a Study Group.

## Slide 5: Motion
WG Motion:
  Form an 802.11 Long Range Low Power (LRLP) Topic Interest Group (TIG) to accomplish the following tasks:
    Specify LRLP requirements and use cases
    Establish technical feasibility of achieving the requirements for range, power consumption, and integration with 802.11 and coexistence with other 802 wireless protocols
    Generate the technical material needed to initiate standardization
  The TIG will generate a report containing the results of these tasks within four 802.11 sessions.