## Slide 1
HE NDP Frame for Sounding
Date: 2015-09-14
Authors:

## Slide 2: Background
Current SFD considers subchannel based feedback [1]:
  The amendment shall include a CSI feedback mechanism which allows for a minimum feedback granularity of less than 20 MHz.
In this document, requirements/issues for HE-NDP frame transmission that enables subchannel based feedback are discussed.

## Slide 3: VHT Sounding Protocol

## Slide 4: HE Sounding Protocol
Compared to VHT sounding protocol, following items may need to be changed:
  NDP Announcement
    An AP may need to have more control on CB feedback info
      May indicate scheduled subchannel/granularity for channel feedback
      May control sounding for not only DL MIMO but also UL MIMO
    May allow UL MU type CB feedback
  NDP
    May use HE PPDU (256 FFT) instead of VHT NDP frame (64 FFT)
  CB
    May be allowed to feedback CSI on preferred or indicated resource/subchannel only
    May consider mechanisms reducing the quantity of each CSI feedback (such as new codebook design)

## Slide 5: VHT NDP PPDU
The VHT NDP PPDU has the following properties:
  Uses the VHT PPDU format but without the Data field
  Is a VHT SU PPDU as indicated by the VHT-SIG-A field
  Has the data bits of the VHT-SIG-B field set to fixed bit pattern

## Slide 6: HE NDP PPDU
HE NDP PPDU may need to consider several factors that VHT NDP PPDU does not have:
  Pilot tones for HE-LTF field
  LTF compression
  GI for HE-LTF field

## Slide 7: Pilot tones for HE-LTF field
Pilot tones in HE-LTF field
  Single stream pilot (like 11ac) in HE-LTF shall be used for SU, DL and UL OFDMA as well as in DL MU-MIMO transmissions. [1]
  Beamformee cannot estimate CSI for pilot tones.
  # pilot tones and their location depends on allocated resources.

## Slide 8: Pilot tones for HE-LTF field
Option 1: Use of OFDM (SU) frame format for all resource allocation scenarios:
  Regardless of scheduled resource for data transmission, an AP sends HE-NDP frame using OFDM frame format.
  OFDM frame format has the least number of pilot tones.
  All non-pilot tones of DATA field correspond to non-pilot tones of HE-LTF field.
Option 2: Use of same resource allocation format with scheduled data transmission
  AP schedules each STA in frequency domain first, and allocate corresponding resource for both NDP frame and data transmission.
  As specific resource allocation needs to be indicated, HE SIG-B field needs to be included in the HE-NDP frame.
  Not easy to figure out resource type before specific scheduling is finished.

## Slide 9: Pilot tones for HE-LTF field
Our preference is to use OFDM frame format for HE NDP frame as it gives
  No HE SIG-B field needed
  Flexible to AP’s scheduling mechanism
  Simple to use
  Similar to VHT NDP frame property
    VHT NDP PPDU is a VHT SU PPDU.

## Slide 10: LTF Compression
At least 2 LTF modes exist in current SFD [1]:
  HE-LTF symbol duration of 6.4 us excluding GI (2x LTF)
  HE-LTF symbol duration of 12.8 us excluding GI (4x LTF)
Depending on operation scenario, different LTF mode needs to be used for NDP PPDU
  4x LTF for Outdoor NLOS environment
  2x LTF for most of indoor/outdoor environment
    Moreover, use of 2x LTF may reduce CB feedback overhead as there are less # of reference tones for CB feedback
Our preference is to keep LTF mode for HE NDP PPDU variable, which is indicated before HE-LTF field (E.g., HE-SIG-A field).

## Slide 11: Guard Interval
All preamble parts of VHT PPDU use long GI.
GI value for HE-LTF field has not been decided yet.
If multiple GI values are allowed for HE-LTF field, we need to consider to allow multiple GI values for HE-NDP PPDU or not.

## Slide 12: Summary
Several aspects for HE-NDP PPDU are discussed:
  Pilot tones for HE-LTF field
    OFDM frame format is preferred for pilot tone allocation.
  LTF Compression
    Both 2x and 4x LTF may need to be supported.
  GI for HE-LTF field
    Decision on allowing multiple GI values for HE-LTF field need to be made first.

## Slide 13: Straw Poll
Do you agree to add to the TG Specification Framework:
  4.y.z The spec shall define an HE-NDP for DL Sounding. The frame format of HE-NDP is based on the 11ax SU PPDU format and is shown in the diagram below. The presence and duration of packet extension at the end of HE-NDP is TBD.
L-STF
L-LTF
L-SIG
TBD
HE-SIG-A
HE-STF
HE-LTFs
Format of HE-NDP
Packet Extension

## Slide 14: References
[1] 11-15-0132r7, “Specification Framework for TGax"