## Slide 1
Bandwidth for UL MU Transmission
Date: 2015-09-14
Authors:

## Slide 2: Background
During July meeting, TGax accepted several new features such as
  Cascaded DL/UL MU transmission
  Unicast/Broadcast Trigger frame for UL MU transmission
However, several UL MU transmission procedures in current SFD text are not clearly defined when we consider those new features.
In this document, we want to modify current SFD text slightly such that UL MU transmission features can be more clearly described under newly added features.

## Slide 3: Transmission Bandwidth for UL MU
Current SFD says:
  An AP shall not allocate UL subchannel in any 20 MHz channel that is not occupied by the Trigger frame. In each 20 MHz channel occupied by the Trigger frame, there is at least one allocated subchannel.
Primary 20MHz channel.
STA2 A-MPDU to AP
TXOP
Backoff
DL
UL
STA3 A-MPDU to AP
STA0 A-MPDU to AP
STA1 A-MPDU to AP
Multi-STABA
Multi-STA BA
Multi-STA BA
Trigger
Trigger
40MHz

## Slide 4: Transmission Bandwidth for UL MU
The intention is not to allow the bandwidth of response frame (UL MU PPDU) to be greater than that of the soliciting frame (Trigger frame).
However, if Trigger frame is transmitted in DL MU transmission manner, it is possible that occupied bandwidth of UL OFDMA transmission can exist in 20 MHz channel that is not occupied by the Trigger frame.

## Slide 5: Transmission Bandwidth for UL MU
So, we propose to modify current SFD text as:
  An AP shall not allocate UL subchannel in any 20 MHz channel that is not occupied by the Trigger frame immediately preceding DL PPDU. In each 20 MHz channel occupied by the Trigger frame immediately preceding DL PPDU, there is at least one allocated subchannel for UL transmission.

## Slide 6: UL MU Transmission Success
Current SFD says:
  An UL OFDMA MPDU/A-MPDU is the acknowledgement of the trigger frame. When the AP receives MPDU correctly from at least one STA indicated by trigger frame, the frame exchange initiated by the trigger frame is successful.
Primary 20MHz channel.
STA2 A-MPDU to AP
TXOP
Backoff
DL
UL
STA3 A-MPDU to AP
STA0 A-MPDU to AP
STA1 A-MPDU to AP
Multi-STABA
Multi-STA BA
Multi-STA BA
Trigger
Trigger
40MHz

## Slide 7: UL MU Transmission Success
The intention is as long as there’s any response frame following the Trigger frame, the Trigger frame transmission is considered to be success.
However, as TGax allows multiple Trigger frames to be transmitted simultaneously, we may need to define “response frame” for Trigger frame more clearly.
As long as there’s any response frame regardless of the number of Trigger frames transmitted simultaneously, the Trigger frame transmission should be considered to be success.

## Slide 8: UL MU Transmission Success
Operation Example:
  AP schedules STA1/STA2/STA3 for UL MU transmission.
  But, only STA2 receive the Trigger frame correctly.
  Case 1: Use of Broadcast Trigger frame only
  Case 2: Simultaneous transmission of Unicast/Broadcast Trigger frame
CASE 1: Transmission success
CASE 2: Transmission failure for TRIG1

## Slide 9: UL MU Transmission Success
So, we propose to modify current SFD text as:
  An UL OFDMA MPDU/A-MPDU is the acknowledgement of the trigger frame. When the AP receives MPDU correctly from at least one STA indicated by any trigger frame, the frame exchange initiated by all the trigger frame(s) is successful.

## Slide 10: Summary
We suggest to modify current SFD text on UL MU transmission to further clarify for several cases
  Cascaded DL/UL MU transmission
  Multiple Trigger frame simultaneous transmission

## Slide 11: Straw Poll 1
Do you agree to modify sub-clause 4.1 of the TG Specification Framework as follows?
  An AP shall not allocate UL subchannel in any 20 MHz channel that is not occupied by the Trigger frame immediately preceding DL PPDU. In each 20 MHz channel occupied by the Trigger frame immediately preceding DL PPDU, there is at least one allocated subchannel for UL transmission.

## Slide 12: Straw Poll 2
Do you agree to modify sub-clause 4.1 of the TG Specification Framework as follows?
  An UL OFDMA MPDU/A-MPDU is the acknowledgement of the trigger frame. When the AP receives MPDU correctly from at least one STA indicated by any trigger frame, the frame exchange initiated by all the trigger frame(s) is successful.

## Slide 13: References
[1] 11-15-0132r7, “Specification Framework for TGax"