## Slide 1: 11ax Channel Access rule
Date: 2015-09-10
Authors:
Name | Affiliation | Address | Phone | Email
Guoqing LI | Apple | 1 Infinite Loop Cupertino, CA 95014 USA | +1-408-862-3055 | guoqing_Li@apple.com
Joonsuk Kim |  |  |  | Joonsuk.kim@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2
Name | Affiliation | Address | Phone | Email
Kazuyuki Sakoda | Sony Corporation | 1-7-1 Konan Minato-ku, Tokyo 108-0075, Japan |  | Kazuyuki.Sakoda@am.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Eisuke Sakai |  |  |  | Eisuke.Sakai@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Masahito Mori |  |  |  | Masahito.Mori@jp.sony.com
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com
Authors (continued)

## Slide 3
Authors (continued)
Name | Affiliation | Address | Phone | Email
Yakun Sun | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | yakunsun@marvell.com
Hongyuan Zhang |  |  |  | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvell..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 4
Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 5
Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 6
Authors (continued)
Name | Affiliation | Address | Phone | Email
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 7
Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 8
Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Bo Sun | ZTE | #9 Wuxing duan, Xifeng Rd, Xi’an, China |  | Sub.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | Yao.ke5@zte.com.cn
Weimin Xing |  |  |  | Xing.weimin@zte.com.cn

## Slide 9: Summary
All Wi-Fi systems follow the channel access rule defined in 802.11-2012
  Each STA contends for the channel based on CCA threshold of the primary channel
There are discussions in the 11ax to use different CCA levels for interBSS traffic and IntraBSS traffic in order to facilitate spatial reuse
  The intention is to possibility allow an STA to transmit frames when it detects interBSS traffic. It may do so by combining other techniques
The proposal describes how to accomplish this goal.

## Slide 10: Channel Access Rule of Current Wi-Fi System
Packet detected
&&
RSSI >= THD
Packet detection
RSSI
packet
Time
Normal CS CCA threshold is set to -82 dBm for 20MHz
Channel Assessment is high if detection criteria pass
Channel Assessment result
Channel Assessment result
Packet detection in 4us

## Slide 11: 11ax Channel Access Rule – Stage 1
An STA has frame to send starting the transmission process according to the backoff procedure, 9.3.4.3
(current) “If the medium is determined to be busy at any time during a backoff slot, then the backoff procedure is suspended;” and
(new) The STA continue to decode the frame and determines whether the detected frame is an inter or intra frame
  By using BSS color (in SIG-A) or MAC address (in MAC header)
  With rules to ensure that all 11ax STAs can make the decision in a consistent manner
(current) If the detected frame is a intraBSS frame, continue to follow the channel access rule
  “The medium shall be determined to be idle for the duration of a DIFS period or EIFS, as appropriate (see 9.3.2.3), before the backoff procedure is allowed to resume.”

## Slide 12: 11ax Channel Access Rule – Stage 2
(new) If the detected frame is a interBSS frame
  (new) Under TBD condition, increase CCA threshold, level B, and if CCA detection indicates the channel is idle
  (current) resume the countdown process after the medium is idle for the duration of a DIFS period or EIFS, as appropriate (see 9.3.2.3)

## Slide 13
Incoming Frame ( -72dBm)
Time
The STA decodes SIG-A, ex. BSS color, and determines it is a inter BSS frame.
STA decodes MAC header and determines it is an inter BSS legacy frame.
Inter BSS 11ax frame
Inter BSS
(legacy) frame
Current behavior
An STA follows the back off process and determines the channel is busy, level A is used for CCA threshold. In this example, input RSSI(-72dBm) is higher than level A (-82dBm). Channel sensing is high (busy) in this time period. Suspend countdown process. Not knowing whether it is a Intra or Inter frame at this time. (The diagram below is for inter frame only. There is no change of the process for intra frame)
If Channel sensing result is idle (due to higher CCA threshold, level C -62 dBm), resume the countdown process after the medium is idle for the duration of a DIFS period or EIFS. Otherwise continue to suspend the countdown process
Channel sensing result
Channel sensing detection in 4us
Initial thd level A = -82dBm
Inter thd level C = -62dBm
Input RSSI = -72dBm
New behavior
STA transmits its frame
Countdown counter = 0`

## Slide 14: Benefit of the Proposed 11ax Channel Access Rule
A simple and effective channel access rule to facilitate spatial re-use, mostly following the 802.11 channel access rule
  Benefit STAs close to the edge of a BSS
An STA can resume the countdown sooner once it determines the detected frame is a interBSS frame and the channel is idle due to the higher CCA threshold set for interBSS frame
  The interBSS and IntraBSS frames transmission may overlap in time and achieve spatial re-use
  Since the 11ax STAs transmitting frame overlapping (in time) with another BSS do not follow the observed TXOP of OBSS frame. It does not affect the OBSS STAs but may be unfair to legacy STAs of the BSS
    A possible solution is not transmitting frame cross observed TXOP boundary
  May also employ TPC to mitigate the interference between inter and intra frame transmissions
  The downside is an STA have to continue to decode the frame until it can determine where is the frame from.
    Only the STA want to participate in spatial re-use need to do it

## Slide 15: Straw Poll
Move to add deferral rules and levels section to the spec framework
  The STA determines whether the detected frame is an inter-BSS or an intra-BSS frame by using BSS color (in SIG-A) or MAC address in the MAC header. If the detected frame is an inter-BSS frame, under TBD condition, uses TBD OBSS PD level that is greater than the minimum receive sensitivity level
  NOTE–Maybe extra rules need to be added to ensure that all 11ax STAs can make the decision in a consistent manner.