## Slide 1: Tone Grouping Factors and NDP Format for 802.11ax
Date: 2015-09-13
Authors:
Name | Company | Address | Phone | Email
Sameer Vermani | Qualcomm | 5775 Morehouse Dr San Diego, CA |  | svverman@qti.qualcomm.com
Alice Chen | Qualcomm |  |  | 
Lin Yang | Qualcomm |  |  | 
Bin Tian | Qualcomm |  |  | 
Tao Tian | Qualcomm |  |  | 
Arjun Bharadwaj | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
Richard Van Nee | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | 
Allert Van Zelst | Qualcomm |  |  | 
Youhan Kim | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | 
VK Jones | Qualcomm |  |  | 

## Slide 2
Name | Affiliation | Address | Phone | Email
Qinghua Li | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-408-765-9698 | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | +408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Authors (continued)

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Sudhir Srinivasa | Marvell (Cont’d) | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Tu Nguyen |  |  |  | 
Vinko Erceg |  |  |  | 
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Eric Wong | Apple | Cupertino, CA | +1-408-9745967 | ericwong@apple.com
Chris Hartman |  |  |  | 
Aon Mujtaba |  |  |  | 
Joonsuk Kim |  |  |  | joonsuk@apple.com
Guoqing Li |  |  | +1-408-974-9164 | guoqing_li@apple.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Weimin Xing | ZTE Corp. |  |  | Xing.weimin@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Ke Yao |  |  |  | Yao.ke@zte.com.cn
Bo Sun |  |  |  | Sun.bo1@zte.com.cn
Yonggang Fang | ZTE TX |  |  | yfang@ztetx.com
Kazuyuki Sakoda | Sony Electronics |  |  | Kazuyuki.Sakoda@am.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Eisuke Sakai |  |  |  | Eisuke.Sakai@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Masahito Mori |  |  |  | Masahito.Mori@jp.sony.com

## Slide 9
Introduction
In these slides, we cover the following two topics
  Tone grouping factors for CSI feedback
    Show simulations for MU-MIMO performance
  NDP Frame Format
Propose the following
  Disallow Ng=1 feedback in 802.11ax
  Use the SU frame format for HE-NDP
Terminology: In these slides, tone grouping factor is always defined with respect to data tones of the 11ax PPDU (regardless of the LTF duration used in NDP or data packet)
  E.g., Ng=4 in 11ax means 1 out of every 4 data tones of 11ax packet

## Slide 10: Tone Grouping Factors
In 802.11ac, the process of sub-sampling the CSI feedback is called tone-grouping
  Sending one value of V or one value of S for a “group” of tones
    E.g. Tone grouping factor, Ng =2 means that one V is sent for a group of 2 tones
    Once Ng has been chosen, Ng’ = 2* Ng is the tone-grouping factor used for S
Ng=1 feedback in 11ax would be prohibitively expensive
  Would be approximately 4 times in size compared to Ng=1 feedback in 11ac
    Tones in 11ax are 4 times thinner
Based on our results, even Ng=4 for 11ax works for indoor channels
  Will show simulation results in subsequent slides
Suggest restricting Ng to be greater than equal to 2 for 11ax
  Ng=4 works well for most practical scenarios where MU-MIMO will be used
  Ng=2 might have some use for outdoor channels

## Slide 11: Simulations for Tone-grouping Factors
Compared the 20MHz DL MU-MIMO performance with various options
  Tone-grouping factor, Ng=1 and 4
  LTF durations used in NDP
    4x when Ng=1, and 1x when Ng=4
    1x LTFs in NDP have two options
      VHT-LTF with 56 tones
      HE-1x-LTF: A modified VHT-LTF with more edge tones leading to total 60 tones
  Tried both 2x and 4x LTFs in DL MU-MIMO data packet
    Minimal performance difference for indoor channels
Show that Ng=4 with 1x LTFs in NDP (and no edge tone augmentation) has good performance for indoor channels
  Similar performance as Ng=1 with 4x LTFs in NDP
  Assumed simple linear interpolation at the AP and phase alignment of V
Simulated both channel models D-NLOS and E-NLOS

## Slide 12: Simulation Assumptions
Considered a 20MHz DL MU-MIMO system with 8 Tx AP, and 3 STAs with 2 Rx antennas each, 2 streams per STA
MMSE precoding done at the AP
  Capacity averaged post processing SINRs mapped to PHY throughputs using AWGN rate table
Plot the 10th percentile and 50th percentile PHY throughputs for 200 channel realizations of D-NLOS/E-NLOS as a function of path-loss
  Sum PHY throughput at the AP
Aging Loss = -30 dBc
Tx Distortion = -35 dBc
Channel estimation loss is considered both in sounding and in actual data transmission
No quantization is considered to isolate the impact of interpolations
No smoothing at the STA is assumed

## Slide 13: Simulation Results: D-NLOS
Ng=4 feedback with 1x LTFs in NDP shows some smoothing gain compared to Ng=1 with 4x LTFs in NDP
  In reality Ng=1 can also benefit from smoothing
  Nevertheless, these results give confidence in Ng=4 with 1x LTFs in NDP

## Slide 14: Simulation Results: E-NLOS
Ng=4 feedback with 1x LTFs in NDP shows some smoothing gain compared to Ng=1 with 4x LTFs in NDP
  In reality Ng=1 can also benefit from smoothing
  Nevertheless, these results give confidence in Ng=4 with 1x LTFs in NDP

## Slide 15: HE-NDP
HE-NDP is needed to cover outdoor use-case
  May allow multiple HE-LTF durations in an HE-NDP
    A subset of 1x, 2x and 4x LTFs may be allowed
  Re-use the SU frame format for the HE-NDP
  HE-SIG-B is not needed
  May need some packet extension at the end
L-STF
L-LTF
L-SIG
RL-SIG
HE-SIG-A
HE-STF
HE-LTFs
Format of HE-NDP
Packet Extension

## Slide 16: Summary
Ng=1 feedback is very expensive for 11ax
  Has 4 times overhead when compared to the Ng=1 feedback of 11ac
Showed simulations to show that Ng=4 in 11ax gives satisfactory performance in indoor channels for MU-MIMO
Suggest disallowing Ng=1 sounding feedback in 802.11ax
Also recommend to use the SU frame format for HE-NDP

## Slide 17: Straw-poll 1
Do you agree to add the following text to the TGax spec framework document:
  “802.11ax spec shall not support Ng=1 for sounding feedback ”
  Y
  N
  A

## Slide 18: Straw-poll 2
Do you support the following HE-NDP frame format for 802.11ax?
  Packet extension at the end of HE-NDP is TBD
L-STF
L-LTF
L-SIG
RL-SIG
HE-SIG-A
HE-STF
HE-LTFs
Format of HE-NDP
Packet Extension

## Slide 19: Motion 1
Move to add the following text to the TGax spec framework document:
  “802.11ax spec shall not support Ng=1 for sounding feedback ”
  Y
  N
  A

## Slide 20: Motion 2
Move to add the following text and diagram to the SFD
The spec shall define an HE-NDP for collecting sounding feedback, whose frame format is shown in the diagram below. The presence and duration of packet extension at the end of HE-NDP is TBD.
L-STF
L-LTF
L-SIG
RL-SIG
HE-SIG-A
HE-STF
HE-LTFs
Format of HE-NDP
Packet Extension