## Slide 1: Number of BSS Color bits
Date: 2015-09-14
Authors:

## Slide 2
Authors:
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Yuichi MYuorioka | Sony Corporation | 1-7-1 Konan Minato-ku, Tokyo 108-0075, Japan |  | Yuichi.Morioka@jp.sony.com
Masahito Mori |  |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Jie Huang |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Phillip Barber | Huawei | The Lone Star State, TX |  | pbarber@broadbandmobiletech.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Zhou Lan |  | F1-17, Huawei Base, Bantian, SHenzhen | +86-18565826350 | Lanzhou1@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Wookbong Lee | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | wookbong.lee@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com

## Slide 9: Abstract
Enhancement of the spatial reuse capability is one of the key features for the 802.11ax.
  For this purpose, 802.11ax devices needs to tell if the receiving signal is from myBSS or OBSS.
  Use of information in the preamble part is a good way to do this in the early state of reception.
  BSS Color was suggested in the previous discussions.
This document presents our analytical result of how many bits are needed for BSS Color information.

## Slide 10: Introduction
To achieve spatial reuse in a dense environment, a STA should determine whether a detected frame is an intra-BSS (MyBSS) or an inter-BSS (OBSS) frame[1, 3, 4, 5].
Inclusion of BSS color information in preamble part of a HE PPDU is a good way to do this in the early stage of reception. HE-SIG-A will be the appropriate place to include this information[6-7].
  MAC address and/or BSSID can be used for the legacy frames.
We calculated the number of BSS Color bits needed in a dense environment based on the TGax Simulation Scenario[2].
  Simulation scenario 3 is used.
  The number of OBSS APs that cause interference is calculated based on path loss without shadow fading.

## Slide 11: Topology of simulation scenario 3
APs are fixed at the center of each cell area.
Interference levels between APs are calculated.
AP tx power: 20dBm,
Antenna gain: 0 dBi
Radius (R): 10m
Inter BSS distance (ICD): 2*h =10√3≒17.32m
h = sqrt(R^2-R^2/4)=5√3≒8.66m
AP1
AP2
10m
30m
AP3
17.32m

## Slide 12: AP-AP interference
CCA Threshold | Freq. Reuse | 5.2GHz |  | 2.4GHz | 
 |  | Distance (possible to detect APs) | # of interfering APs | Distance (possible to detect APs) | # of interfering APs
-76dBm | 1 | 68m | 54 | 106m | 138
 | 3 |  | 18 |  | 42
-82dBm | 1 | 101m | 120 | 157m | 300
 | 3 |  | 36 |  | 96
Chart: d (Distance from an AP) [m]
| 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160
frequency reuse 1 | 0 | 0 | 4 | 4 | 10 | 14 | 14 | 14 | 26 | 32 | 38 | 50 | 54 | 54 | 78 | 78 | 84 | 100 | 112 | 118 | 142 | 154 | 160 | 188 | 188 | 200 | 228 | 240 | 258 | 282 | 300
frequency reuse 3 | 0 | 0 | 0 | 0 | 6 | 6 | 6 | 6 | 6 | 12 | 18 | 18 | 18 | 18 | 30 | 30 | 36 | 36 | 36 | 42 | 54 | 54 | 60 | 60 | 60 | 72 | 84 | 84 | 90 | 90 | 108
Chart: Distance from an AP [m]
-82dBm
-76dBm

## Slide 13: Evaluation
It is necessary to assign 6 bits or more for BSS identifier to identify all OBSS APs that are detected by an AP.
  The calculation result shows that 36 APs will be detected under the following conditions: CCA threshold -82dBm, 5.2GHz, 3 frequency reuse.
If the 80 MHz channel is used, the number of independent channels is limited. As the worst case, we may need to consider 1 frequency reuse in a geographical area in which radars are operating.
In this case, to identify all OBSS APs detected by an AP, the number of BSS Color bits should be at least 6.
  The calculation result shows that 54 APs will be detected under the following conditions: CCA threshold: -76dBm, 5.2GHz, 1 frequency reuse.

## Slide 14: Conclusion
We calculated the number of BSS Color bits that is needed to enhance the spatial reuse capability in a dense environment.
6 bits are needed for the BSS Color in a dense environment.

## Slide 15: References
[1] John Son, “Further Considerations on Enhanced CCA for 11ax,” doc.: IEEE 802.11-14-0847-01
[2] Simone Merlin, “TGax simulation scenarios,” doc.: IEEE 802.11-14-0980-14
[3] Masahito Mori, “Performance Analysis of BSS Color and DSC,” doc.: IEEE 802.11-14-1403-00
[4] Masahito Mari, “Performance Analysis of BSS Color and DSC,” doc.: IEEE 802.11-15-0045-00
[5] Yasu Inoue, “Discussion on The Receiver Behavior for CCAC/DSC with BSS Color,” doc.:IEEE 802.11-15-0595-02
[6] Jaiyin Zhang, “HE-SIGA Contents,” IEEE 802.11-15-1077-00
[7] Alfred Asterjadhi, “Identifiers in HE PPDUs for Power Saving,” IEEE 802.11-15-1122-00

## Slide 16: Straw Poll
Do you support to assign 6 bits for BSS Color?
  Y:
  N:
  A:

## Slide 17: APPENDIX

## Slide 18: Appendix 1: Calculation of the number of APs within a circle of radius r
15m
30m
17.3m
r
L
pr
，
If , the number of APs is
, the numbers of APs is
Let Kz be the number of interference APs when
“-1” at the end is for the AP itself.
If we use 3 frequency reuse, h should be replaced by h’ (3h).

## Slide 19: Appendix 1: Calculation of the number of APs within a circle of radius r
R
 | R (m) |  | R (m)
1 | 17.3 | 11 | 190.5
2 | 34.6 | 12 | 207.8
3 | 52.0 | 13 | 225.2
4 | 69.3 | 14 | 242.5
5 | 86.6 | 15 | 259.8
6 | 103.9 | 16 | 277.1
7 | 121.2 | 17 | 294.4
8 | 138.6 | 18 | 311.8
9 | 155.9 | 19 | 329.1
10 | 173.2 | 20 | 346.4

## Slide 20: Appendix 2: Number of detected BSSs in Shinagawa, Tokyo.
Chart: Center Freq. (MHz)
| 5180 | 5200 | 5220 | 5240
Number of detected unique MAC address | 20 | 38 | 31 | 22
Number of BSSs
The numbers are based on data collected at Shinagawa Station in 2015.
We counted the number of source MAC addresses from which 100 or more beacons are received in about 90 seconds.
Multiple MAC addresses for one device are not considered.