## Slide 1: LTF Design for Uplink MU-MIMO
Date: 2015-09-14
Authors:

## Slide 2: Introduction
LTF Sequence masking with orthogonal codes was proposed for Uplink MU-MIMO operation in [1].
Issues with LTF sequence masking with orthogonal codes were identified in [2].
This contribution presents further simulation results and an alternative method on obtaining orthogonality between spatial stream for frequency and phase offset compensation

## Slide 3: Per-Stream Orthogonality using P-matrix
P matrix masking
  Proposal in [1] obtains per-stream pseudo-orthogonality by masking P-matrix in the frequency domain.
L1
L2
L3
L4
L5
L6
L7
L8
[ 1 1 -1 1 ][ 1 1 -1 1 ]
Row ‘m’ of P matrix
x
x
[ 1 ej2πθ ej2π2θ ej2π3θ ej2π4θ ej2π5θ ej2π6θ ej2π7θ ]
CSD for SS #m
LTF sequence
Final Output Sequence
Orthogonal Code

## Slide 4: Per-Stream Orthogonality using CSD
Orthogonality CSD
  Interestingly, per-stream orthogonality can be also obtain without P-matrix masking, if the CSD is orthogonal between streams.
L1
L2
L3
L4
L5
L6
L7
L8
x
x
[ 1 ej2πθ ej2π2θ ej2π3θ ej2π4θ ej2π5θ ej2π6θ ej2π7θ ]
CSD for SS #m
LTF sequence
Final Output Sequence
No P-matrix Masking
Orthogonal Code

## Slide 5: Per-Stream Orthogonality using CSD (cont.)
Lk
Lk+1
Lk+2
Lk+3
Lk+4
Lk+5
Lk+6
Lk+7
Lk+8
Lk+9
Lk+10
Lk+11
Lk+12
…
…
…
Spatial Stream # n
Spatial Stream # m
Lk
Lk+1
Lk+2
Lk+3
Lk+4
Lk+5
Lk+6
Lk+7
Lk+8
Lk+9
Lk+10
Lk+11
Lk+12
…
…
ej2πn/8
ej2π2n/8
ej2π3n/8
ej2π4n/8
ej2π5n/8
ej2π6n/8
ej2π7n/8
ej2π8n/8
ej2πn/8
ej2π2n/8
ej2π3n/8
ej2π4n/8
ej2π5n/8
x
x
x
x
x
x
x
x
x
x
x
x
x
ej2πm/8
ej2π2m/8
ej2π3m/8
ej2π4m/8
ej2π5m/8
ej2π6m/8
ej2π7m/8
ej2π8m/8
ej2πm/8
ej2π2m/8
ej2π3m/8
ej2π4m/8
ej2π5m/8
x
x
x
x
x
x
x
x
x
x
x
x
x
CSD operation
CSD operation
full CSD cycle
Instead of performing two step multiplication (P-matrix & CSD), simply perform one step multiplication (only CSD), where the CSD values are chosen such that spatial streams are orthogonal.

## Slide 6: Proposed CSD values for UL MU-MIMO
No change to the waveform equations compared to 11ac. Simply use different CSD values.
With 78.125kHz subcarrier spacing, candidate values are THE-CSD(m) = [ 0ns, -1600ns, -3200ns, -4800ns, -6400ns, -8000ns, -9600ns, -11200ns]
  CSD is applied to each tone in the LTF and Data OFDM symbols just like HT and VHT PPDU.
Modulated subcarrier with CSD, k is the subcarrier index
m is the spatial stream number.

## Slide 7: Cyclic Orthogonal Property of CSD
Lk
Lk+1
Lk+2
Lk+3
Lk+4
Lk+5
Lk+6
Lk+7
Lk+8
Lk+9
Lk+10
Lk+11
Lk+12
…
…
…
Spatial Stream # n
Spatial Stream # m
Lk
Lk+1
Lk+2
Lk+3
Lk+4
Lk+5
Lk+6
Lk+7
Lk+8
Lk+9
Lk+10
Lk+11
Lk+12
…
…
At HE-LTF OFDM symbol #1
Note:
CSD results in cyclic orthogonality just like proposal [1].
ej2πn/8
ej2π2n/8
ej2π3n/8
ej2π4n/8
ej2π5n/8
ej2π6n/8
ej2π7n/8
ej2π8n/8
ej2πn/8
ej2π2n/8
ej2π3n/8
ej2π4n/8
ej2π5n/8
x
x
x
x
x
x
x
x
x
x
x
x
x
ej2πm/8
ej2π2m/8
ej2π3m/8
ej2π4m/8
ej2π5m/8
ej2π6m/8
ej2π7m/8
ej2π8m/8
ej2πm/8
ej2π2m/8
ej2π3m/8
ej2π4m/8
ej2π5m/8
x
x
x
x
x
x
x
x
x
x
x
x
x
CSD operation
Orthogonal in Frequency Domain
Orthogonal in Frequency Domain
Both boxes results in perfect orthogonality

## Slide 8: CSD and PAPR
CSD operation (i.e. multiplication of linearly increasing phase) in frequency domain is equivalent to cyclically rotating time domain signals.
CSD does not change dynamic range of transmitted signals and therefore retains PAPR property of the modulated signal.
  This is the biggest benefit of CSD.
  Per-stream orthogonality can be achieved with affecting the PAPR of the LTF sequence. Therefore, LTF sequence can be designed without any consideration of UL MU-MIMO operation.
The biggest problem with P-matrix masking in LTF symbols is unpredictable changes to PAPR property of the underlying LTF sequence [See Appendix A for PAPR results].

## Slide 9: Simulation Setup
BW: 20MHz
Channel Model: TGac Channel D
Configuration:
  4 Rx AP with FOUR of 1 Tx STA
  8 Rx AP with SIX of 1 Tx STA
Identical SNR among STAs
Transmit timing spread among users: spread uniformly within 0us, 0.5us, and 1us
MCS 6, Payload Size 1000 Bytes
IPN: -41dBc (both at Tx and Rx)
Carrier Frequency Offset: uniformly spread across ±500Hz (±0.1 ppm @ 5GHz)
Real frequency/phase offset tracking
  ‘K’ de-spread channel coefficients in frequency domain was used in tracking
  de-spread channel coefficients in time domain (after frequency/phase compensation) used in data symbol equalization
Real channel estimation

## Slide 10: Simulation Setup (cont.)
Simulated Algorithms
  P-matrix masking with 11ac CSD
    Frequency domain block-wise de-spreading using conjugate of P-matrix (MRC) after removal of CSD
    Frequency domain block-wise de-spreading using inverse of P-matrix & CSD (ZF)
      Comparison between MRC de-spreading vs. ZF de-spreading shown in Appendix B.
  P-matrix masking with Block-wise CSD (just for reference)
    Block-wise de-spreading using conjugate of P-matrix (MRC) after removal of CSD
    CSD phase value is constant over a block of subcarriers. CSD phase values increment every 8 tones. An example shown in Appendix C.
  Orthogonal CSD
    Frequency domain block-wise de-spreading using conjugate of CSD
    Time domain de-spreading using time-domain windowing
      Detailed explanation of time domain processing is shown in Appendix D
    CSD phase values for each stream randomly chosen from
      THE-CSD(m) = {0ns, -1600ns, -3200ns, -4800ns, -6400ns, -8000ns, -9600ns, -11200ns}

## Slide 11: Performance with LTF P matrix masking (1/6)
Notes:
K = 242 uses all available tones for frequency/phase offset compensation
K = 8 only uses 8 tones for frequency/phase offset compensation (lower complexity)
Further details of K shown in [Appendix E]

## Slide 12: Performance with LTF P matrix masking (2/6)

## Slide 13: Performance with LTF P matrix masking (3/6)

## Slide 14: Performance with LTF P matrix masking (4/6)

## Slide 15: Performance with LTF P matrix masking (5/6)

## Slide 16: Performance with LTF P matrix masking (6/6)

## Slide 17: Conclusion
Use of orthogonal CSD in Uplink MU-MIMO results in better performance than the P-matrix masking approach proposed in [1].
  Better or equal performance in all simulation scenarios.
  Better performance when large transmit time spread among STAs.
Orthogonal CSD operations does not impact PAPR properties of the LTF sequence.
  Low PAPR property of the LTF sequence can be kept.
Support of orthogonal CSD is simple
  No need for P-matrix masking
  Orthogonal CSD results in small set of phase values, {1, 1+j, j, 1-j, -1, -1-j, -j, 1-j}, that can simplify complex value multiplication.

## Slide 18: Strawpoll
Do you agree add the following statement to SFD:
  CSD parameters, that result in per-stream orthogonality within a HE-LTF OFDM symbol, shall be used in HE-LTF of uplink MU-MIMO transmission.
Y/N/A:

## Slide 19: References
[1] IEEE802.11-15/0602r1, “HE-LTF Sequence for UL MU-MIMO,” May 2015.
[2] IEEE802.11-15/0845r0, “LTF Design for Uplink MU-MIMO,” July 2015.

## Slide 20: APPENDIX

## Slide 21: Appendix A: PAPR of LTF Symbols with P matrix Masking
Observation:
P matrix masked LTF can have up to 8.8 dB PAPR
There is 80% probability that data OFDM symbols have less than 8.8dB PAPR.
P matrix masked LTF OFDM symbols have higher mean/median PAPR than data OFDM symbols

## Slide 22: Appendix B: Comparison between MRC and ZF de-spreading
Rx (AP)
Tx (STA1)
Tx (STA1)
Tx (STA3)
h1
h2
h3
If ck is orthogonal
(y’ is received signal with LTF sequence removed)
Conjugate de-spreading completely removes interference
If ck is non-orthogonal
Inverse de-spreading can remove interference
ZF
MRC
Both schemes assume Channel is FLAT within the code length
ck is the p-matrix row vector (with CSD applied)

## Slide 23: Appendix C: Comparison of Regular CSD vs. Block CSD
Regular CSD (every tone)
Block CSD (every 4 tones)
L1
L2
L3
L4
L5
L6
L7
L8
[ 1 1 -1 1 ][ 1 1 -1 1 ]
Row ‘m’ of P matrix
x
x
[ 1 ej2πθ ej2π2θ ej2π3θ ej2π4θ ej2π5θ ej2π6θ ej2π7θ ]
CSD for SS #m
LTF sequence
Final Output Sequence
L1
L2
L3
L4
L5
L6
L7
L8
[ 1 1 -1 1 ][ 1 1 -1 1 ]
x
x
[ej2πθ ej2πθ ej2πθ ej2πθ ej2π5θ ej2π5θ ej2π5θ ej2π5θ ]
Final Output Sequence
Phase of CSD changed every few tones
Phase of CSD changed every tone
Not Orthogonal
Orthogonal
(Example Only)

## Slide 24: Appendix D: Time Domain Processing using Windowing (1/3)
Rx (AP)
Tx (STA1)
Tx (STA1)
Tx (STA3)
h1
h2
h3
Ck is the CSD matrix.
Different STAs use different CSD phase value, θk
Number of diagonal terms is equal to number of subcarriers
hk is the channel vector for the entire frequency for STA #k

## Slide 25: Appendix D: Time Domain Processing using Windowing (2/3)
Power
time
0
N-1
h(1)
h(2)
h(3)
Channel response for STA 2, h(2), is shifted in time domain. The shift amount depends on θ
Channel response for STA 1, h(1), is centered in DC
Determined by CSD for STA 2
Determined by CSD for STA 3

## Slide 26: Appendix D: Time Domain Processing using Windowing (3/3)
Power
time
0
N-1
h(1)
h(2)
h(3)
Channel response for STA 2, h(2), is shifted in time domain. The shift amount depends on θ
Channel response for STA 1, h(1), is centered in DC
Step 1) Convert received signal to time domain after removal of LTF sequence (just leave the CSD and channel in the received signal)
Step 2) Window (i.e. time domain masking) each channel response and convert it back to frequency domain
Power
time
0
N-1
h(1)
zero out
Convert back to frequency domain.
This completely removes channel from STA 2 and STA 3
Step 3) Perform different windowing and convert back to frequency domain for other channel responses.

## Slide 27: Appendix E: Residual Frequency/Phase Offset Compensation with P matrix masked LTF symbols
perform de-spreading per stream
Received LTF symbols (freq-domain)
D
estimate residual
frequency/phase offset
Compensated LTF symbols for time domain de-spreading processing
‘K’ de-spreaded tones used for residual frequency/phase offset
Nss x 242
Nss x K
Nss x K
fo &θ per STA
Nss x 242
Note:
We have performed tests with various K.
Obviously high K values means higher complexity or larger die size at the AP receiver.

## Slide 28: Appendix E: Residual Frequency/Phase Offset Compensation with P matrix masked LTF symbols (cont.)
L1 ejθ
L2 ej2θ
-L3 ej3θ
L4 ej4θ
L5 ej5θ
L6 ej6θ
-L7 ej7θ
L8 ej8θ
L9 ej9θ
L10 ej10θ
-L11 ej11θ
Freq.
LTF sequence w/ CSD
L1* e-jθ
L2* e-j2θ
-L3* e-j3θ
L4* e-j4θ
L5* e-j5θ
L10* e-j10θ
L11* e-j11θ
x
h1
h2
…
x
…
…
h10
…
In total ‘M’ number of potential channel coefficient estimates from de-spreading
Selectively compute
(sub-sample)
h2
h6
h10
…
Total of ‘K’ number of channel coefficient estimates for frequency/phase tracking
…