## Slide 1: Technical Feasibility for LRLP
Date: 2015-09-14
Authors:

## Slide 2: Contents of this Contribution
Introduction to LRLP
Integration with legacy 802.11 devices
Power consumption requirements

## Slide 3: Long Range Low Power Operation
Longer Range operation
  In mainstream 802.11
Lower Power operation
  Enable battery powered IoT
Integrated with mainstream networks
  Interoperable in mixed BSS case
Integrated with mainstream products
  Negligible incremental cost for implementation at an AP
  Acceptable to have a specialized low-cost silicon for LRLP STA, but the AP should be based on standard silicon.
Intended for M2M – managed impact on existing network
  Medium Occupancy Limit, average occupancy limit
  Other mechanisms as appropriate

## Slide 4: Usage Configuration (20MHz + LRLP) BSS
September 2015
Chittabrata Ghosh, Intel

## Slide 5: Integration with Legacy 802.11 Devices
LRLP STA not required to support legacy 20MHz Tx or Rx
  I.e. No detection or transmission of legacy preambles required for LRLP STA
LRLP AP will be required to support legacy 20MHz Tx & Rx
  LRLP AP will…
    Perform CCA and legacy network access
    Protect DL LRLP transmissions using legacy preambles
    Protect UL LRLP transmissions using legacy preambles and triggering UL from LRLP STAs
Example LRLP concept…
September 2015
Chittabrata Ghosh, Intel
wideband
narrowband

## Slide 6: LRLP Power Consumption Targets
Narrowband (e.g., 2MHz) + low MCS only transceiver design can allow power reduction compared to legacy 20MHz transceiver
  Rx expected to be able to achieve significant reduction (E.g. >50% reduction)
  Tx reductions expected to be more modest (assuming equivalent Tx power: >10dBm)
  Listen (LRLP Preamble detect + preamble decode) will target most significant reductions
September 2015
Chittabrata Ghosh, Intel
Implications of Coin Cell Battery operated LRLP STAs…
  Tx state power consumption targeting a ~50% reduction by lowering transmit power to 0dBm
  Reduced range LRLP STA designs expected to be able to meet coin cell battery peak power limitations.
  Average Power for reasonable coin cell battery life still a challenge. What’s needed?
    Highly optimized beacons and keep alive protocols
    Extended listen intervals to maximize deep sleep occupancy

## Slide 7: LRLP Power Consumption Targets
September 2015
Chittabrata Ghosh, Intel
Implications of Coin Cell Battery operated LRLP STAs…
  Example Coin Cell Battery Properties
    Nominal Voltage: 3.0V
    Typical Capacity: 240mAh
    Duty Cycled Peak Power: ~144mW (60mA @ 2.4V)
    Average Power Consumption for 1yr Battery Life: ~60uW
  LRLP Tx power consumption at full range (264mW) expected to be major bottleneck for coin cell battery operation
    Reduced range w/ Tx power at 0dBm possible mitigation for peak power issue

## Slide 8: LRLP Comprehensive Current Consumption Targets
September 2015
Chittabrata Ghosh, Intel
Power State | Average Current Consumption [mA] – Legacy 20MHz Transceiver [2] | Average Current Consumption [mA] – LRLP STA Transceiver (LRLP Full Range: Tx Pwr >10dBm) | Average Current Consumption [mA] – LRLP STA Transceiver (LRLP Full Range: Tx Pwr =0dBm)
Transmit | 280 | 240 | 120
Receive | 100 | <50 | <50
Listen | 50 | <5 | <5
Shallow Sleep | 0.9 | <0.9 | <0.9
Deep Sleep | 0.003 | 0.003 | 0.003

## Slide 9: Summary
We have presented …
  High level concept for LRLP integration with legacy 802.11 networks
  Initial power consumption targets for LRLP only STAs
  Introduction to analysis of challenges for coin cell operated LRLP only STA designs

## Slide 10: References
[1] IEEE 11-15/0775r1: Integrated Long Range Low Power Operation for IoT
[2] C. Ghosh et. al., “Sleep states in-IEEE 802.11ax Simulation Scenarios,” IEEE 11-15-314r2, March 2015