## Slide 1: Box5 Calibration Results
Date: 2015-09-13
Authors:

## Slide 2: PHY Parameters
PHY parameters | 
BW | All BSSs at 5GHz [80 MHz, no dynamic bandwidth]
Primary channel | Aligned primary 20MHz channel for each co-80MHz-channel BSS; The detection of preamble and BA should only focus on primary 20MHz
Channel model | TGac D NLOS per link
Shadow fading | iid log-normal shadowing (5 or 0 dB standard deviation) per link
Preamble type | Control: legacy 20us; Data: 11ac (20us+20us for 1antenna case)
Legacy control frame rate | Basic 6Mbps rate for RTS/CTS/ACK/BA (MCS0) [1]
AP/STA TX Power | 20/15 dBm per antenna
Power Spectral density | Scaled to 80 MHz
number of antennas at AP /STA | 1/1
AP /STA antenna gain | 0/-2 dBi
Noise Figure | 7dB
CCA-ED threshold | -56 dBm (measured across the entire bandwidth after large-scale fading)
Rx sensitivity/CCA-SD | -76 dBm (a packet with lower rx power is dropped)
Link Adaption | Fixed MCS =5 for 11ac SS6 and TBD for 11ax SS1-4
Channel estimation | Ideal unless otherwise specified
PHY abstraction | RBIR, BCC (see appendix 1&3 in [2])
Symbol length | 4us with 800ns GI per OFDM symbol

## Slide 3: MAC Parameters
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3 ]
Queue length | A single queue for each traffic link is set inside AP/STA sized of 2000 packets
Traffic type | UDP CBR with rate 10^8bps Random start time during a 10ms interval
MPDU size | 1544 Bytes (1472 Data + 28 IP header + 8 LLC header + 30 MAC header + 4 delimiter + 2 padding)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU, immediate BA without explicit request], Max aggregation: 32 MPDUs
Max number of retries | 10
Beacon | Disabled unless otherwise specified
RTS/CTS | OFF unless otherwise specified
Running time | >= 10s per drop
Output metric | -CDF or Histogram of per non-AP STA throughput (received bits/overall simulation time) -PER of all AP/STA (1 - # of success subframes / # of transmitted subframes)

## Slide 4: 11ac Scenario 6 – OBSS Enterprise [3]
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)

## Slide 5: 11ac SS6 Traffic Flow Model
DL/UL traffic assigned for each STA
STA | DL | UL | STA | DL | UL
STA1 | y | y | STA23 | n | y
STA2 | y | y | STA25 | y | y
STA4 | y | y | STA26 | y | y
STA5 | y | y | STA28 | y | y
STA7 | y | y | STA29 | y | y
STA8 | y | y | STA3 | y | y
STA10 | y | n | STA9 | y | n
STA11 | y | n | STA15 | y | n
STA13 | y | n | STA21 | n | y
STA14 | y | n | STA27 | y | y
STA16 | y | n | STA6 | y | y
STA17 | y | n | STA12 | y | n
STA19 | y | n | STA18 | y | n
STA20 | y | n | STA24 | n | y
STA22 | n | y | STA30 | y | y
“y” means having DL/UL traffic flow; “no” means not having DL/UL traffic flow

## Slide 6: Step-by-Step Calibration of 11ac SS6
1 BSS (upper-right corner BSS B)
  DL only case
  UL only case
    1 STA: each STA-AP
    2 STAs: 3+9, 3+15, 3+27
    3 STAs: 3+9+15, 3+9+27
    5 STAs
  DL & UL case
2 BSS (A+B)
  Both DL only
  Both UL only
  A DL and B UL
  A UL and B DL
3 BSS
  DL only
  UL only
  Mixed DL & UL
Note:
No shadowing is assumed
For 2 BSS and 3 BSS cases, traffic flow model is defined as in slide 7.

## Slide 7: 1 BSS
all UL | STA | Throughput
 | 3 | 31.93
 | 9 | 31.21
 | 15 | 43.62
 | 21 | 29.03
 | 27 | 31.54
DL & UL | DL | STA | Throughput
 |  | 3 | 7.265
 |  | 9 | 6.72
 |  | 15 | 6.73
 |  | 21 | 6.52
 |  | 27 | 6.35
 | UL | 3 | 23.71
 |  | 9 | 25.94
 |  | 15 | 30.05
 |  | 21 | 27.44
 |  | 27 | 23.78

## Slide 8: 2 BSS
Case | STA |  | Throughput
A+B DL | A | 1 | 6.72
 |  | 2 | 6.44
 |  | 4 | 6.25
 |  | 5 | 6.21
 |  | 7 | 5.96
 |  | 8 | 5.8
 |  | 10 | 5.76
 |  | 11 | 5.7
 |  | 13 | 5.58
 |  | 14 | 5.55
 |  | 16 | 5.48
 |  | 17 | 5.43
 |  | 19 | 5.38
 |  | 20 | 5.33
 |  | 25 | 2.98
 |  | 26 | 2.96
 |  | 28 | 2.944
 |  | 29 | 2.944
 | B | 3 | 28.28
 |  | 9 | 28.046
 |  | 15 | 27.28
 |  | 27 | 26.59
A+B UL | A | STA | Throughput
 |  | 1 | 2.66
 |  | 2 | 4.86
 |  | 4 | 4.3
 |  | 5 | 8.38
 |  | 7 | 5.55
 |  | 8 | 3.89
 |  | 22 | 8.31
 |  | 23 | 5.51
 |  | 25 | 3.43
 |  | 26 | 6.9
 |  | 28 | 6.78
 |  | 29 | 7.77
 | B | 3 | 17.84
 |  | 21 | 25.46
 |  | 27 | 24.81

## Slide 9: 2-BSS
A DL B UL | A | STA | Throughput
 |  | 1 | 0.307
 |  | 2 | 0.298
 |  | 4 | 0.32
 |  | 5 | 0.304
 |  | 7 | 0.342
 |  | 8 | 0.342
 |  | 10 | 0.356
 |  | 11 | 0.289
 |  | 13 | 0.278
 |  | 14 | 0.364
 |  | 16 | 0.345
 |  | 17 | 0.317
 |  | 19 | 0.286
 |  | 20 | 0.301
 |  | 25 | 0.286
 |  | 26 | 0.307
 |  | 28 | 0.339
 |  | 29 | 0.3375
 | B | 3 | 38.434
 |  | 21 | 56.206
 |  | 27 | 60.605
A UL B DL | A | STA | Throughput
 |  | 1 | 4.57
 |  | 2 | 15.298
 |  | 4 | 16.817
 |  | 5 | 18.322
 |  | 7 | 6.69
 |  | 8 | 13.911
 |  | 22 | 9.963
 |  | 23 | 8.12
 |  | 25 | 6.026
 |  | 26 | 7.694
 |  | 28 | 10.661
 |  | 29 | 19.276
 | B | 3 | 0.1888
 |  | 9 | 0.241
 |  | 15 | 0.241
 |  | 27 | 0.309

## Slide 10: 3-BSS
A+B+C DL | A | STA | Throughput
 |  | 1 | 2.18
 |  | 2 | 2.244
 |  | 4 | 2.317
 |  | 5 | 2.252
 |  | 7 | 2.194
 |  | 8 | 2.22
 |  | 10 | 2.212
 |  | 11 | 2.246
 |  | 13 | 2.226
 |  | 14 | 2.198
 |  | 16 | 2.149
 |  | 17 | 2.07
 |  | 19 | 2.2
 |  | 20 | 2.241
 |  | 25 | 2.318
 |  | 26 | 2.093
 |  | 28 | 2.205
 |  | 29 | 2.424
 | B | 3 | 15.849
 |  | 9 | 16.955
 |  | 15 | 15.33
 |  | 27 | 15.623
 | C | 6 | 1.024
 |  | 12 | 1.061
 |  | 18 | 1.02
 |  | 30 | 0.9544
A+B+C UL | A | STA | Throughput
 |  | 1 | 4.693
 |  | 2 | 6.669
 |  | 4 | 7.614
 |  | 5 | 8.525
 |  | 7 | 9.329
 |  | 8 | 7.137
 |  | 22 | 8.718
 |  | 23 | 8.718
 |  | 25 | 6.2
 |  | 26 | 5.341
 |  | 28 | 7.73
 |  | 29 | 6.955
 | B | 3 | 3.012
 |  | 21 | 1.572
 |  | 27 | 1.362
 | C | 6 | 3.137
 |  | 24 | 1.767
 |  | 30 | 1.494