## Slide 1: System Level Simulator Evaluation with/without Capture Effect
Date: 2011-11-09
Authors:

## Slide 2: Outline
Background
Evaluation methodology
Topology
Assumptions
Results for 1 BSS
Results for 2 BSS

## Slide 3: Capture Effect
If a receiver receives two packets:
  No Capture Effect: Receiver obtains packets based on first come, first serve policy.
  Capture Effect: Receiver obtains the packet with higher energy.
Capture effect is beneficial when there is a collision. In conclusion:
  In one BSS, packets with higher SNR has a higher chance of survival.
  If two BSS don’t have any overlap, packets from own BSS have priority to packets from OBSS

## Slide 4: Evaluation Methodology
Investigating correlation between STA’s average SNR and STA’s throughput.
Average SNR is calculated based on log-normal path-loss model with no shadowing
Throughput is measured from simulation

## Slide 5: Simulation Topology
AP A | (0,0)
AP B | (40,20)
AP C | (-40,-20)
STA3 | (7.5+xb, ‑9.5+yb)
STA9 | (7+xb, -7.5+yb)
STA15 | (3+xb, -0.5+yb)
STA21 | (-6.5+xb, -3+yb)
STA27 | (‑6+xb, 2.5+yb)
STA6 | (-5.5+xc,4.5+yc)
STA12 | (7+xc,7+yc)
STA18 | (10+xc,0.5+yc)
STA24 | (3+xc,2.5+yc)
STA30 | (9.5+xc,3.5+yc)
STA1 | (5,-9.5)
STA2 | (3.5,7.5)
STA4 | (-4.5,0.5)
STA5 | (-1.5,6)
STA7 | (-9,-5)
STA8 | (-8.5,8.5)
STA10 | (-3,0.5)
STA11 | (-0.5,8)
STA13 | (-4,-4)
STA14 | (7.5,-1)
STA16 | (8,-6)
STA17 | (0,-7.5)
STA19 | (-2.5,-4.5)
STA20 | (0.5,-2)
STA22 | (0,-4.5)
STA23 | (-1.5,7)
STA25 | (3.5,-5)
STA26 | (9,9.5)
STA28 | (-8,-5.5)
STA29 | (1.5,3.5)

## Slide 6: Simulation Assumption (Box5 calibration)
PHY parameters | 
BW | All BSSs at 5GHz [80 MHz, no dynamic bandwidth]
Primary channel | Aligned primary 20MHz channel for each co-80MHz-channel BSS; The detection of preamble and BA should only focus on primary 20MHz
Channel model | TGac D NLOS per link
Shadow fading | iid log-normal shadowing (5 or 0 dB standard deviation) per link
Preamble type | Control: legacy 20us; Data: 11ac (20us+20us for 1antenna case)
Legacy control frame rate | Basic 6Mbps rate for RTS/CTS/ACK/BA (MCS0) [1]
AP/STA TX Power | 20/15 dBm per antenna
Power Spectral density | Scaled to 80 MHz
number of antennas at AP /STA | 1/1
AP /STA antenna gain | 0/-2 dBi
Noise Figure | 7dB
CCA-ED threshold | -56 dBm (measured across the entire bandwidth after large-scale fading)
Rx sensitivity/CCA-SD | -76 dBm (a packet with lower rx power is dropped)
Link Adaption | Fixed MCS =5 for 11ac SS6 and TBD for 11ax SS1-4
Channel estimation | Ideal unless otherwise specified
PHY abstraction | RBIR, BCC (see appendix 1&3 in [2])
Symbol length | 4us with 800ns GI per OFDM symbol
MAC parameters | 
Access protocol | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=3 ]
Queue length | A single queue for each traffic link is set inside AP/STA sized of 2000 packets
Traffic type | UDP CBR with rate 10^8bps Random start time during a 10ms interval
MPDU size | 1544 Bytes (1472 Data + 28 IP header + 8 LLC header + 30 MAC header + 4 delimiter + 2 padding)
Aggregation | [A-MPDU / max aggregation size / BA window size, No A-MSDU, immediate BA without explicit request], Max aggregation: 32 MPDUs
Max number of retries | 10
Beacon | Disabled unless otherwise specified
RTS/CTS | OFF unless otherwise specified
Running time | >= 10s per drop
Output metric | -CDF or Histogram of per non-AP STA throughput (received bits/overall simulation time) -PER of all AP/STA (1 - # of success subframes / # of transmitted subframes)

## Slide 7: 1BSS - Received Power and Average SNR for each STA at AP
 |  | RxP [dBm] | SNR [dB]
STA# for BSS A | 1 | -65.0399 | 28.94976
 | 2 | -61.0858 | 32.90389
 | 4 | -52.5633 | 41.42639
 | 5 | -56.6573 | 37.33242
 | 7 | -64.4041 | 29.58562
 | 8 | -66.7589 | 27.23079
 | 10 | -49.1072 | 44.88251
 | 11 | -60.599 | 33.3907
 | 13 | -55.3013 | 38.68835
 | 14 | -59.7223 | 34.2674
 | 16 | -63.9612 | 30.02847
 | 17 | -59.5884 | 34.40133
 | 19 | -53.868 | 40.12167
 | 20 | -45.7297 | 48.26004
 | 22 | -52.51 | 41.47967
 | 23 | -58.8809 | 35.10883
 | 25 | -56.4559 | 37.53377
 | 26 | -68.0498 | 25.93994
 | 28 | -63.5111 | 30.47855
 | 29 | -51.0595 | 42.93024
 |  | RxP [dBm] | SNR [dB]
STA# for BSS B | 3 | -66.8634 | 27.12632
 | 9 | -64.3501 | 29.63959
 | 15 | -49.1072 | 44.88251
 | 21 | -58.8809 | 35.10883
 | 27 | -57.4132 | 36.57651
 |  | RxP [dBm] | SNR [dB]
STA# for BSS C | 6 | -66.8634 | 35.22088
 | 12 | -64.3501 | 30.18202
 | 18 | -49.1072 | 30.0095
 | 24 | -58.8809 | 42.71123
 | 30 | -57.4132 | 29.84081
There are no hidden nodes in one BSS Transmission. Therefore, the collision in uplink transmission happens only when two nodes have a same back-off value.

## Slide 8: 1 BSS - Correlation between Average SNR and Throughput
BSS A, uplink traffic
Throughput is average of throughputs over 20 runs with different seeds.
Throughput obtained from simulation is correlated with calculated SNR.
Chart: SNR
| 28.949760000000001 | 32.903889999999997 | 41.426389999999998 | 37.332419999999999 | 29.585619999999999 | 27.230789999999999 | 44.882510000000003 | 33.390700000000002 | 38.68835 | 34.267400000000002 | 30.028469999999999 | 34.401330000000002 | 40.121670000000002 | 48.260039999999996 | 41.479669999999999 | 35.108829999999998 | 37.533769999999997 | 25.93994 | 30.478549999999998 | 42.930239999999998
 | 3.6151 | 4.1898 | 8.5863 | 7.4629 | 4.0799 | 2.9451 | 10.1535 | 6.0321 | 8.5835 | 7.4263 | 3.9972 | 6.5116 | 8.6321 | 14.2869 | 10.9056 | 6.0573 | 7.9729 | 2.5325 | 4.8526 | 9.7826

## Slide 9: 1 BSS - Correlation between Average SNR and Throughput (With Capture Effect)
BSS A, uplink traffic
Throughput is average of throughputs over 20 runs with different seeds.
Capture Effect Threshold is 10dbm
Capture effect helps STAs with higher SNR achieve better throughput. In the case of collision (because of same back-off), packets with higher SNR have better chance of survival.
Chart: Throughput
| 28.949760000000001 | 32.903889999999997 | 41.426389999999998 | 37.332419999999999 | 29.585619999999999 | 27.230789999999999 | 44.882510000000003 | 33.390700000000002 | 38.68835 | 34.267400000000002 | 30.028469999999999 | 34.401330000000002 | 40.121670000000002 | 48.260039999999996 | 41.479669999999999 | 35.108829999999998 | 37.533769999999997 | 25.93994 | 30.478549999999998 | 42.930239999999998
Without Capture Effect | 3.6151 | 4.1898 | 8.5863 | 7.4629 | 4.0799 | 2.9451 | 10.1535 | 6.0321 | 8.5835 | 7.4263 | 3.9972 | 6.5116 | 8.6321 | 14.2869 | 10.9056 | 6.0573 | 7.9729 | 2.5325 | 4.8526 | 9.7826
With Capture Effect | 2.958 | 4.3244 | 8.7175 | 7.8825 | 3.7814 | 2.4499 | 10.1259 | 6.5661 | 8.8708 | 7.5599 | 3.7509 | 6.2591 | 8.2856 | 14.4915 | 10.8459 | 6.7299 | 8.2376 | 1.8757 | 4.9265 | 10.5644

## Slide 10: 2BSS (Received Power at AP [BSS A] when OBSS STA transmits)
RxP [dBm] |  | STA # of BSS A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29
Interference Source STA# | 3 | -89.4752 | -88.5173 | -91.2973 | -90.1819 | -92.8344 | -92.1575 | -90.8687 | -89.8253 | -91.4543 | -87.6369 | -88.0645 | -90.6653 | -91.0801 | -90.0041 | -90.368 | -90.1568 | -89.3711 | -86.4575 | -92.6183 | -89.3317
 | 9 | -89.6177 | -88.4081 | -91.2763 | -90.0975 | -92.856 | -92.0509 | -90.8508 | -89.7134 | -91.4828 | -87.6817 | -88.191 | -90.7495 | -91.1198 | -90.0273 | -90.4191 | -90.0593 | -89.4484 | -86.3009 | -92.6472 | -89.2833
 | 15 | -89.7417 | -87.5131 | -90.7735 | -89.323 | -92.545 | -91.2135 | -90.3549 | -88.8218 | -91.1806 | -87.4064 | -88.2398 | -90.6587 | -90.8573 | -89.6867 | -90.1937 | -89.231 | -89.3159 | -85.1935 | -92.3629 | -88.6461
 | 21 | -86.6159 | -83.3868 | -87.5664 | -85.7195 | -89.7592 | -88.08 | -87.0547 | -85.0777 | -88.1254 | -83.4612 | -84.7143 | -87.594 | -87.7501 | -86.2852 | -86.9593 | -85.6 | -85.9311 | -80.2628 | -89.5514 | -84.8864
 | 27 | -88.1981 | -84.5581 | -88.5999 | -86.7057 | -90.7386 | -88.7378 | -88.149 | -86.0212 | -89.2656 | -85.1845 | -86.4831 | -88.9391 | -88.9585 | -87.594 | -88.2792 | -86.5454 | -87.4335 | -81.7081 | -90.5697 | -86.1115
As shown above, almost all STAs of BSS B are hidden to STAs of BSS A.

## Slide 11: 2BSS (Average SNR at AP [BSS A] when OBSS STA transmits)
RxP [dBm] |  | STA # of BSS A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 14 | 16 | 17 | 19 | 20 | 22 | 23 | 25 | 26 | 28 | 29
Interference Source STA# | 3 | 21.99122 | 25.94535 | 34.46785 | 30.37389 | 22.62709 | 20.27225 | 37.92397 | 26.43216 | 31.72981 | 27.30887 | 23.06994 | 27.44279 | 33.16314 | 41.3015 | 34.52114 | 28.1503 | 30.57523 | 18.9814 | 23.52001 | 35.97171
 | 9 | 21.98801 | 25.94215 | 34.46464 | 30.37068 | 22.62388 | 20.26904 | 37.92076 | 26.42895 | 31.72661 | 27.30566 | 23.06673 | 27.43959 | 33.15993 | 41.29829 | 34.51793 | 28.14709 | 30.57202 | 18.9782 | 23.51681 | 35.9685
 | 15 | 21.62487 | 25.579 | 34.1015 | 30.00753 | 22.26073 | 19.9059 | 37.55762 | 26.0658 | 31.36346 | 26.94251 | 22.70358 | 27.07644 | 32.79678 | 40.93514 | 34.15478 | 27.78394 | 30.20887 | 18.61505 | 23.15366 | 35.60535
 | 21 | 18.6172 | 22.57134 | 31.09383 | 26.99987 | 19.25307 | 16.89823 | 34.54995 | 23.05814 | 28.3558 | 23.93485 | 19.69592 | 24.06878 | 29.78912 | 37.92748 | 31.14712 | 24.77628 | 27.20121 | 15.60739 | 20.146 | 32.59769
 | 27 | 19.72989 | 23.68402 | 32.20651 | 28.11255 | 20.36575 | 18.01092 | 35.66264 | 24.17082 | 29.46848 | 25.04753 | 20.8086 | 25.18146 | 30.9018 | 39.04016 | 32.2598 | 25.88896 | 28.31389 | 16.72007 | 21.25868 | 33.71037

## Slide 12: 2 BSS - Correlation between Average SNR and Throughput
(BSS A, uplink traffic. BSS B only node 3 transmits )
STA 3 transmits, full buffer, uplink traffic
Throughput obtained from simulation is correlated with nodes path-loss when there is a interference from node 3.
Chart: SNR
| 21.991219999999998 | 25.945350000000001 | 34.467849999999999 | 30.373889999999999 | 22.627089999999999 | 20.27225 | 37.923969999999997 | 26.43216 | 31.729810000000001 | 27.308869999999999 | 23.069939999999999 | 27.442789999999999 | 33.163139999999999 | 41.301499999999997 | 34.521140000000003 | 28.150300000000001 | 30.575230000000001 | 18.981400000000001 | 23.520009999999999 | 35.971710000000002
 | 3.5976 | 4.4785 | 7.7509 | 6.5969 | 4.13 | 3.0359 | 8.8049 | 6.1796 | 7.6476 | 7.0758 | 4.0501 | 5.8178 | 7.8179 | 10.996 | 9.0325 | 6.004 | 6.9447 | 2.6349 | 4.7321 | 8.9034
First row of table from previous slide

## Slide 13: 2 BSS - Correlation between average SNR and Throughput (with Capture Effect)
(BSS A, uplink traffic. BSS B only node 3 transmits )
STA 3 transmits, full buffer, uplink traffic
Capture effect threshold = 20dbm
Capture effect helps STAs achieve better throughput. Since packets from own BSS have priority to packets from OBSS. Therefore, collision rate decreases.
Chart: SNR
| 21.991219999999998 | 25.945350000000001 | 34.467849999999999 | 30.373889999999999 | 22.627089999999999 | 20.27225 | 37.923969999999997 | 26.43216 | 31.729810000000001 | 27.308869999999999 | 23.069939999999999 | 27.442789999999999 | 33.163139999999999 | 41.301499999999997 | 34.521140000000003 | 28.150300000000001 | 30.575230000000001 | 18.981400000000001 | 23.520009999999999 | 35.971710000000002
With Capture Effect | 3.5976 | 4.4785 | 7.7509 | 6.5969 | 4.13 | 3.0359 | 8.8049 | 6.1796 | 7.6476 | 7.0758 | 4.0501 | 5.8178 | 7.8179 | 10.996 | 9.0325 | 6.004 | 6.9447 | 2.6349 | 4.7321 | 8.9034
Without Capture Effect | 2.0751 | 3.2994 | 7.5508 | 6.2807 | 2.7324 | 2.0818 | 8.4191 | 4.7348 | 7.0014 | 5.817 | 2.6784 | 4.3281 | 7.0404 | 9.4107 | 8.4246 | 5.3895 | 6.7408 | 1.4824 | 3.7604 | 7.7705

## Slide 14: 2 BSS – BSS A & BSS B, UP Link Traffic
With capture effect, nodes in border have better gain as they experience more collision
 | STA | No Capture Effect | Capture Effect | Gain(%)
BSS A | 1 | 1.122948909 | 3.296319667 | 1.93541375
 | 2 | 1.776355455 | 3.669496667 | 1.06574459
 | 4 | 4.124025909 | 5.015168667 | 0.21608564
 | 5 | 3.760308636 | 4.516448667 | 0.20108457
 | 7 | 1.886621364 | 3.633383333 | 0.9258678
 | 8 | 1.217798545 | 2.999523333 | 1.46307022
 | 10 | 5.148343182 | 5.363616333 | 0.04181406
 | 11 | 2.419128636 | 4.311519 | 0.78226116
 | 13 | 4.437605909 | 5.160284 | 0.16285315
 | 14 | 2.424928182 | 4.899046667 | 1.02028526
 | 16 | 1.448786818 | 3.590217667 | 1.47808554
 | 17 | 2.828862273 | 4.176284333 | 0.47631236
 | 19 | 4.070106818 | 4.823057667 | 0.18499535
 | 20 | 4.825840455 | 6.469788 | 0.34065518
 | 22 | 4.622865 | 5.472740667 | 0.18384177
 | 23 | 3.097391364 | 4.35214 | 0.40509851
 | 25 | 4.119923182 | 5.045312 | 0.22461312
 | 26 | 0.975462591 | 3.195248333 | 2.27562365
 | 28 | 2.316607727 | 3.670213667 | 0.5843052
 | 29 | 4.449205 | 5.375541 | 0.20820259
BSS B | 3 | 0.715588409 | 2.524070333 | 2.52726554
 | 9 | 0.861360909 | 2.768849 | 2.21450506
 | 15 | 0.907483864 | 2.909578 | 2.20620357
 | 21 | 0.129589523 | 0.957944267 | 6.39214287
 | 27 | 0.086910373 | 1.0006351 | 10.513414

## Slide 15: Conclusion
Analytical results can be used in simulation evaluation
Results from capture effect and non-capture effect shall be compared

## Slide 16: References
[1] 11-14/0571r5 Evaluation Methodology
[2] 11-14/1177r2 Box5 Calibration Discussion
[3] 11-09/0451r16 TGac Functional Requirements and Evaluation Methodology
[4] 11-14/1523r5 Offline Discussion Minutes of SLS Calibration
[5] 11-14/1392r7 Simulation Results for Box5 calibration
[6] 11-15/0638r1 Simulation Results for Box5
[7] 11-15/0613r0 Box 5 Calibration Result
[8] 11-15/0610r1 Simulation Results for Box 5 Calibration
[9] 11-14/0571r8 Evaluation Methodology