## Slide 1: Extended Range Support for 11ax
Date: 2015-11-09
Authors:
Name | Company | Address | Phone | Email
Sameer Vermani | Qualcomm | 5775 Morehouse Dr San Diego, CA |  | svverman@qti.qualcomm.com
Tao Tian | Qualcomm |  |  | 
Lin Yang | Qualcomm |  |  | 
Bin Tian | Qualcomm |  |  | 
Alice Chen | Qualcomm |  |  | 
Arjun Bharadwaj | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
Richard Van Nee | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | 
Allert Van Zelst | Qualcomm |  |  | 
Youhan Kim | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | 
VK Jones | Qualcomm |  |  | 

## Slide 2: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Zhou Lan |  |  |  | Zhou.lan@mediaTek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 8: Outline
In [1], it was proposed to have a repeated HE-SIG-A for range extension purposes
In these slides, we show
  Performance of the preamble with repeated HE-SIG-A
    Look at performance bottlenecks of the preamble performance
  Can remove/mitigate the bottlenecks of preamble performance through L-STF/LTF boost
  5-6 dB performance gain is on offer through the extended range mode
    Measured as preamble performance advantage over MCS0 20MHz payload
Based on above, propose power-boosting the L-STF and L-LTF by 3dB for the extended range mode
Normal Mode
Range extension mode

## Slide 9: Supporting the Extended Range Mode
Preamble needs to keep up with lower SNR operation to realize the range benefit
Doing it within the existing preamble framework is possible
  By repeating L-SIG, HE-SIGA [1]
  Possible 3dB power boosting of some training fields if needed
In the following slides, we study the performance of the preamble with HE-SIG-A repetition
  Look at the performance bottlenecks in the preamble
    L-STF becomes a bottleneck Can be removed by boosting it by 3dB
    Once L-STF bottleneck is removed, repeated HE-SIG-A decoding or RL-SIG detection becomes the bottle neck Mitigated by boosting L-LTF by 3dB
  Also, answer the question: Eventually, how much better can the preamble perform compared to MCS0 data?

## Slide 10: Simulations
Analyzed the capability of the HE preamble in the presence of SIG field repetition for the following 3 cases:
  Without any training field boost
  With L-STF power boost
  With L-STF and L-LTF power boost
Parameters used
  D-NLOS channel
  32 byte and 1000 byte packets
  BCC coding
  Looked at both 1 % and 10% PERs
  All impairments and tracking loops are turned ON
  4 symbol SIG-A used (with repetition)
  Realistic PA model to model the impact of clipping when STF/LTF are boosted

## Slide 11: Performance of existing preamble with SIG repetition in absence of any training field boost
Green columns show MCS0 payload-only performance
We show performance of various sub-fields of the preamble and show what is the bottle neck in red
  L-STF is the bottle-neck in this case
The gain on offer by going to lower data-rates is shown below
  Difference in the preamble bottle-neck and payload performance
DNLOS | L-STF Detection | RL-SIG Detection | L-SIG + RL-SIG Decoding | HE-SIGA rep2 Decoding | MCS0 BCC (32 Bytes) | MCS0 BCC (1000 Bytes)
PER = 1% | 6.5dB | 5.5dB | 4.5dB | 5.2dB | 9.1dB | 11.0dB
PER = 10% | 1.5dB | 0.8dB | 0.8dB | 1.2dB | 5.7dB | 7.3dB
DNLOS | Gain Compared to MCS0 BCC (32 Bytes) | Gain Compared to MCS0 BCC (1000 Bytes)
PER = 1% | 2.6dB | 4.5dB
PER = 10% | 4.2dB | 5.8dB

## Slide 12: Performance of existing preamble with SIG repetition with L-STF boost
Green columns show MCS0 payload-only performance
With L-STF boosted, it no longer remains the bottle neck
  RL-SIG detection and HE-SIG-A decoding is the bottle-neck in this case at 1% and 10% respectively
The gain on offer by going to lower data-rates is shown below
  Difference in the preamble bottle-neck and payload performance
DNLOS | L-STF Detection | RL-SIG Detection | L-SIG + RL-SIG Decoding | HE-SIGA rep2 Decoding | MCS0 BCC (32 Bytes) | MCS0 BCC (1000 Bytes)
PER = 1% | 4.8dB | 5.5dB | 4.5dB | 5.2dB | 9.1dB | 11.0dB
PER = 10% | -0.2dB | 0.7dB | 0.8dB | 1.2dB | 5.7dB | 7.3dB
DNLOS | Gain Compared to MCS0 BCC (32 Bytes) | Gain Compared to MCS0 BCC (1000 Bytes)
PER = 1% | 3.6dB | 5.5dB
PER = 10% | 4.5dB | 6.1dB

## Slide 13: Performance of existing preamble with SIG repetition with L-STF & L-LTF boost
Green columns show MCS0 payload-only performance
With both L-STF and L-LTF boosted
  L-STF detection and HE-SIG-A decoding are the bottle-necks at 1% and 10% PER respectively
The gain on offer by going to lower data-rates is shown below
  Difference in the preamble bottle-neck and payload performance
DNLOS | L-STF Detection | RL-SIG Detection | L-SIG + RL-SIG Decoding | HE-SIGA rep2 Decoding | MCS0 BCC (32 Bytes) | MCS0 BCC (1000 Bytes)
PER = 1% | 4.8dB | 4.3dB | 3.9dB | 4.6dB | 9.1dB | 11.0dB
PER = 10% | -0.2dB | -2.0dB | 0.3dB | 0.6dB | 5.7dB | 7.3dB
DNLOS | Gain Compared to MCS0 BCC (32 Bytes) | Gain Compared to MCS0 BCC (1000 Bytes)
PER = 1% | 4.3dB | 6.2dB
PER = 10% | 5.1dB | 6.7dB

## Slide 14: Summary
When compared to MCS0 payload performance
  5-6 dB better preamble performance is on offer by introducing lower data rates in payload and repetition of SIG fields in the existing SU preamble
    Boosting of L-STF increases the gain by another 1dB at 1% PER
    Boosting of both L-STF & L-LTF increases the gain even further
Power boost on L-STF and L-LTF is needed to maximize the gain of the extended range mode
  Propose a 3dB boost on both the fields

## Slide 15: Pre-motion 1
Do you support adding the following to the spec framework
“L-STF power is boosted by 3 dB in the extended range preamble”

## Slide 16: Pre-motion 2
Do you support adding the following to the spec framework
“L-LTF power is boosted by 3 dB in the extended range preamble”

## Slide 17: References
[1] 11-15-0826-03-00ax-he-sig-a-transmission-for-range-extension