## Slide 1: Feasibility of SU-MIMO under Array Alignment Method
Date: 2015-11-09
Authors:

## Slide 2: Abstract
This presentation investigates the feasibility of SU-MIMO using array alignment method based on the channel models adopted in 802.11ad.
A simulation methodology is proposed for evaluating the performance of SU-MIMO in an 802.11ay environment.
The condition number of the MIMO channel, the achievable capacity, and the distribution of the capacity are investigated.
The effect of antenna array separation and link distance is considered.

## Slide 3: Methodology for SU-MIMO Analysis
The channel models developed for 802.11ad [1] are utilized to generate channel impulse responses between the phased antenna arrays (PAAs).
Independent channel impulse responses are generated for each TX and RX PAA link. It is assumed the rays departing or arriving from the backside of the devices are blocked.
The array responses of TX and RX PAAs are calculated using the angle-of-arrival (AoA) and angle-of-departure (AoD) of the rays.
After applying phase vectors for each PAA, the channel impulse response is calculated and the performance metrics are determined.
Performance metrics:
Channel capacity
Condition number
Received signal strength indicator (RSSI)

## Slide 4: Array Alignment Method
For the array alignment method, the boresights of each pair of TX PAA and RX PAA are aligned with each other.
It is achieved by adjusting the phase of each antenna element [1].
RX PPA 2
RX PPA 1
RX
TX PPA 2
TX PPA 1
TX
x
z
y
Boresight
Isotropic antenna
element
Antenna patterns for PAA where
and .
and .
and .
Boresight
Boresight
Boresight

## Slide 5: Simulation Setup for STA-STA Scenario
We consider the same deployment scenario (conference room) as that given in reference [2] with the following parameters:
Both TX PAA and RX PAAs have the same geometry of elements ().
Distance between the geometrical centers of TX/RX PAAs: cm.
Distance between TX and RX devices: cm.
It is assumed that TX PAA 1 beamforms with RX PAA 1 and TX PAA 2 beamforms with RX PAA 2.
The bandwidth is GHz.
The output power of each TX PAA is dBm. The noise figure is dB [3].
d: Antenna (Array) Distance
D: Link Distance

## Slide 6: Result: RSSI & Condition Number in LOS
The RSSI results follow the measurement results provided in reference [2].
Low condition number is achievable in a LOS condition if there is a sufficient amount of isolation between the links. This is enabled through high gain beamforming.
Low condition number may also be achieved in a LOS condition if the channel vectors are configured or designed to be orthogonal.
Channel vectors are orthogonal
Isolated links

## Slide 7: Result: Channel Capacity in LOS
When the link distance increases, RSSI decreases and so does channel capacity.
When the distance between PAAs, i.e., , increases, the links become more isolated from each other. Hence, the channel capacity does not fluctuate drastically.
Lack of isolation does not imply lower capacity.

## Slide 8: Result: Condition Number in LOS+NLOS
The average RSSI and average condition number are calculated based on the wideband response. For each link distance, the averaged results are provided over 500 realizations.
The impact of NLOS components on the condition number seems negligible due to the heavy beamforming on the LOS component.
Scenario: Conference room
Subscenario: STA-STA

## Slide 9: Simulation Setup for STA-AP Scenario
We consider an asymmetrical scenario where an AP transmits to a STA.
Both TX PAAs and RX PAAs have the same geometry of elements ().
The distance between the geometrical centers of RX PAAs at STA: cm.
The distance between the geometrical centers of TX PAAs at AP: cm.
The horizontal distance between TX and RX devices: cm.
It is assumed that TX PAA 1 beamforms with RX PAA 1 and TX PAA 2 beamforms with RX PAA 2.
AP
STA
d: STA Antenna (Array) Distance
dAP: AP Antenna (Array) Distance
D: (Horizontal) Link Distance
x
y
z

## Slide 10: Result: Channel Capacity in LOS
More
Less
Isolation
When is small, the signal strength from the interfering links become strong. Provided that the condition number is low, full MIMO capacity is achievable. However, the capacity fluctuates dramatically with the distance.
When the distance between PAAs at AP, i.e., , is large, the condition number is close to 1. However, the capacity is not necessarily improved.

## Slide 11: Distribution of the Capacity in LOS
Fixed location
and orientation
2x8 PPA 2
2x8 PPA 1
RX
Directions of PAAs at STA
2x8 PPA 2
2x8 PPA 1
TX
Directions of PAAs at AP
Scenario: Conference room
Subscenario: STA-AP
The location of the STA and the rotation of the PAAs around vertical axis are chosen randomly.
For each drop, the channel capacity is calculated. After independent drops, the distribution of the capacity is obtained.
The vertical distance is in the range between and cm due to the geometry.
Random location
and orientation

## Slide 12: Result: Distribution of the Capacity
It is more likely to have better SU-MIMO performance when the links are not isolated. This is due to the fact that the receiver can exploit the energy from the interfering link if the condition number is low.
Isolated
links
Isolated
links

## Slide 13: Summary
In this study, we analyze the feasibility of SU-MIMO under the strategy of array alignment method.
Given the PAA configuration presented, when the links are isolated by decreasing the link distance or increasing the distance between PAAs at TX and RX, the condition number gets closer to 1.
When the arrays are aligned with each other, the links may not be isolated. In this case, the condition number of the MIMO channel fluctuates depending on the link distance and the physical separation of the PAAs at TX and RX.
When the links are not isolated AND the condition number is close to 1, the SU-MIMO channel capacity can be achieved.

## Slide 14: References
A. Maltsev, et al, “Channel Models for 60 GHz WLAN Systems,” IEEE doc. 11-09/0334r8.
A. Maltsev, et al, “Experimental Measurements for Short Range LOS SU-MIMO,” IEEE doc. 11-15/0632r1.
G. Venkatesan, et al, “TGay Evaluation Methodology,” IEEE doc. 11-15/0866.

## Slide 15: Appendix

## Slide 16: Channel Model (1/2)
.
.
.
Effective channel after analog beamforming
The channel is obtained as
,
where is the space-time channel between th TX PAA and th RX PAA, which can be calculated as
and
is the total number of paths between th RX PAA and th TX PAA,
and are the th path’s elevation and azimuth angles of arrival, and are the th path’s elevation and azimuth angles of departure, is the delay for th path’s between th RX PAA and th TX PAA,
is the combined array response of th RX PAA and th TX PAA to the th ray.
.
.
.

## Slide 17: Channel Model (2/2)
x
z
y
d
x
d
y
th impinging ray
Antenna
element
The matrix can be explicitly given by
,
where is the vectorization operation, is the array response to th ray which arrives at elevation angle and azimuth angle, given by
and
where is the wavelength, and are the distances between antenna elements on x-axis and y-axis, and and are the indices for the antenna elements [1].