## Slide 1: Multiple NAVs for Spatial Reuse
Date: 2015-11-09
Authors:
Name | Affiliation | Address | Phone | Email
Evgeny Khorov | IITP |  |  | khorov@frtk.ru
Anton Kiryanov | IITP |  |  | ant456@ya.ru
Sigurd Schelstraete | Quantenna |  |  | sigurd@quantenna.com
Huizhao Wang | Quantenna |  |  | hwang@quantenna.com

## Slide 2: NAV Reset Rules
Current 802.11 [1] specifies that
in a non-DMG BSS, a STA shall interpret the reception of a CF-End frame as NAV reset, i.e., it resets its NAV timer to 0 at the end of the PPDU containing this frame.
Current .11ax SFD also contains the following rule:
When a STA receives a CF-End from an OBSS STA, if the last NAV update was caused by an intra-BSS frame, the STA should not reset its NAV. (MAC Motion 33, September 17, 2015, see [2]).
As shown in [2], it helps to avoid resetting the NAV set by myBSS frame due to an OBSS CF-End frame and prevent possible collisions
What for:
- a CF-End from intra-BSS STA, if the last NAV update was caused by an OBSS frame;
- a CF-End from an OBSS STA, if the last NAV update was caused by another OBSS frame?

## Slide 3: Current .11ax SFD
When a STA receives a CF-End from an OBSS STA, if the last NAV update was caused by an intra-BSS frame, the STA should not reset its NAV. (MAC Motion 33, September 17, 2015, see [2]).
AP1
AP2
STA1a
STA2a
STA2b sets NAV
STA2b sets NAV
STA2b’s
TX range
STA2b
CF-end
RTS
CTS
Frame
ACK
RTS
CTS
Frame
BSS1
BSS2
STA2b does not reset NAV

## Slide 4: Problem
Collision
When a STA receives a CF-End from an OBSS STA, if the last NAV update was caused by an intra-BSS frame, the STA should not reset its NAV. (MAC Motion 33, September 17, 2015, see [2]).
When a STA receives a CF-End from an intra-BSS STA, if the last NAV update was caused by an OBSS frame, there is a problem
BSS1
BSS2
AP1
AP2
STA1a
STA2a
STA1b sets NAV
STA1b sets NAV
STA1b’s
TX range
STA1b
CF-end
RTS
CTS
Frame
ACK
RTS
CTS
Frame
RTS
STA1b reset NAV

## Slide 5: A More Complex Problem
When a STA receives a CF-End from an OBSS STA, if the last NAV update was caused by another OBSS frame, ...
BSS1
BSS2
BSS3
AP1
AP2
STA3
AP3
CF-end
STA1
Frame
STA2
Frames
CTS
Collision
AP2 increases
NAV
AP2 resets NAV
RTS
AP2 transmits
RTS
CTS
Frames
AP2 sets NAV
ACK
It is not sufficient to distinguish just between Intra-BSS and OBSS frames.
AP2’s
TX range

## Slide 6: Solution
Problem: The NAV value is set by a frame from one BSS and is reset by a frame from another BSS.
Solution: Use multiple NAVs. Each NAV corresponds to a particular BSS.
BSS1
BSS2
BSS3
AP1
AP2
STA3
AP3
CF-end
STA1
STA2
Frames
CTS
AP2 sets NAV2
AP2 resets NAV1
RTS
AP2 does NOT transmit because
of NAV2!
RTS
CTS
Frames
AP2 sets NAV1
ACK
AP2’s
TX range

## Slide 7: Multiple NAVs Details
Each STA maintains multiple NAVs.
Each NAV corresponds to a particular BSS heard by the STA.
  E.g., in case of 3 BSSs operating in the same area, each STA maintains 3 NAVs: one NAV for its own BSS and the other 2 NAVs for the alien 2 BSSs.
NAV corresponding to a particular BSS can be reset or increased only by reception of frames from that BSS.
Since some frames may not contain BSSID (e.g. CTS, etc.), BSS color can be used to distinguish overlapped BSSs.
If at least one NAV indicates that the medium is busy, then the medium is considered to be busy.
Note: The concept of multiple NAVs does not forbid using adaptive CCA thresholds.
A history of the multiple NAV concept can be found in [3].

## Slide 8: Multiple NAVs Complexity
In practice, the STA only needs to track as many NAVs as the number of colors it sees
The STA may keep only N (e.g., N=2 or 3) highest NAVs with the corresponding colors
Memory usage
The number of NAVs at a STA is limited by the number of BSS colors.
Computational complexity
  update the necessary NAV value, check whether this value is greater than current maxNAV and update maxNAV if necessary
  reset the necessary NAV, find the maximum value over remaining NAVs and update maxNAV if necessary
  When a NAV value is set (increased) the STA shall
  When a CF-end is received the STA shall
  check whether this value is among N highest ones, update them and maxNAV if necessary
  check whether NAV to be reset is among N highest ones, reset it if necessary and update maxNAV if necessary

## Slide 9: Straw Poll 1
Do you agree to add the following text in SFD:
  An HE STA should have a mechanism to remember and distinguish NAVs set by intra-BSS frame and OBSS frame. A CF-end frame that comes from intra-BSS (OBSS) should not reset NAV that was set by a frame from OBSS (intra-BSS). To determine which BSS is the origin of a frame, the HE STA may use BSS color.
  Y
  N
  A

## Slide 10: Straw Poll 2
Do you agree to add the following text in SFD:
  An HE STA should have a mechanism to remember and distinguish NAV values set by frames from different BSSs. A CF-end frame that comes from one BSS should not reset NAV that was set by a frame from another BSS. To determine which BSS is the origin of a frame, the HE STA may use BSS color.
  Y
  N
  A

## Slide 11: Reference
  [1] IEEE P802.11-REVmcTM/D4.0
  [2] Jeongki Kim (LG Electronics), “15/1067r0 MU TXOP truncation”.
  [3] Mathilde Benveniste (Avaya Labs), “04/1093r4
  Multiple NAV Protection – Revisited Multiple NAV Protection – Revisited”