## Slide 1: Random access based buffer status report
Date: 2015-11-12
Authors:

## Slide 2: Buffer Status Report in 11ax
Buffer status report scheme was agreed in the last meeting[1]
  A “BS report” frame can be any frame that contains QoS Control field
    AP elicits for BS reports via the Trigger frame
    It is also allowed that STAs send BSR in unsolicited manner
    AP might save BSRs on its UL data queue
QoS Data
QoS Data
Trigger
QoS Data
Ack
DL Data 3
DL Data 5
BA/QoS Data
BA/QoS Data
Beacon
BA
Buffer Status Report
Trigger
QoS Data/Null
Ack
SU
MU

## Slide 3: Considerations on the proposed BSR
For any UL STAs, it is necessary to deliver BSR to be assigned in UL MU transmission
Not every STA is allowed to send BSR
  Impossible for AP to solicit BSR for every associated STAs with trigger frames
  Only those who granted resource by contention can get chances for BSR in unsolicited manner
  What about the others?

## Slide 4: Necessity of random access BSR
Opportunity for BSR needs to be equalized
In order to provide better fairness for UL MU transmission, random access of BSR can be considered
  PCF-like BS polling may require excessive delay

## Slide 5: Random Access BSR
AP triggers RA BSR with TF-R
  AP might choose whether it trigger RA BSR or not
    Depending on UL data queue
    Not mandatory for every UL MU transmission
STAs transmit BSR through randomly chosen RU for RA
AP acknowledges the result of RA BSR
  AP may decide whether it triggers UL Data transmission right after RA BSR or not, depending on the UL queue status
RA BSR can be also useful, when
  AP has no information on UL data to trigger at all
  Relatively small amount (# of STAs or datasize) of data is required, instantly, for UL MU transmission
    More flexible and efficient resource use

## Slide 6: Expected form of RA BSR
AP might allow the whole channel solely for RA BSR
  STAs might send BSR with QoS Data/Null format with fixed datasize and MCS
    AP cannot differentiate MCS for random-accessing STAs
RA BSR can be triggered with UL data as well
  Random-accessing STA may add fragmented UL data within given duration
Indication method for RA BSR must be defined
  RA BSR is another type of UL MU frames

## Slide 7: Indication for RA BSR in TF
Indication for RA BSR
  Option 1) 1-bit indication in common info field
    Small overhead
    Not applicable for mixed case of RA BSR and UL data
  Option 2) indication bit for each perSTA info field
    Easy to coexist with other types of UL MU frames
    Relatively large overhead
  Option 3) Assigning a reserved AID for RA BSR
    Similar with ‘AID 0’ in TF-R
    No overhead required
    Scalability of AID must be further considered

## Slide 8: Conclusion
BSR scheme in 11ax might cause unfairness problem in terms of opportunity for UL transmission
Random Access BSR can be considered as an additional option for relieving mentioned problem

## Slide 9: Strawpoll
Do you agree to add to the TG Specification Frame work document?
4.x.y AP may transmit Trigger Frame to elicit buffer status report using random access

## Slide 10: Reference
[1] 11-15-1120-00-00ax-buffer-status-report