## Slide 1: Requirements for UL MU Transmission
Date: 2016-01-18
Authors:
Name | Affiliation | Address | Phone | Email
Arjun Bharadwaj | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 4: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 6: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com

## Slide 11: Introduction
UL OFDMA and UL MU-MIMO rely on transmission accuracy and synchronization by STAs for effective operation
Minimum requirements need to be specified to enable UL MU features
  Similar to previous amendments
In this document, recommendations for several requirements are proposed
  Tx power control requirements
  RSSI measurement accuracy requirements
  CFO requirements
  Timing requirements
  LO Leakage requirements
  Sampling Frequency Offset

## Slide 12: STA Categories
802.11 specification allows for device implementations with a wide range of capabilities
  Some devices are capable of supporting all the MCS, process a large number of spatial streams and support BWs up to 160Mhz
  Other low cost implementations have limited capabilities
For UL MU transmissions, devices that are carefully calibrated can meet strict requirements in power and measurement accuracy
  Low cost devices may not undergo this process and may support features that do not require strict requirements
We propose two device classes
  Class A: High capability devices with stricter requirements
  Class B: Low cost devices that have limited capabilities with looser requirements

## Slide 13: Tx Power Dynamic Range
UL MU transmissions are affected by power imbalance between users
  UL MU-MIMO transmissions are impacted to a larger extent than UL OFDMA
Dynamic range for STAs need to be high enough so that strong users can be paired with weaker users (by lowering the Tx power appropriately)
  On the other hand, it can be challenging to ensure good performance at low power levels for high powered STAs
Propose to define dynamic range by specifying a min required Tx power as follows:
  Required minimum Tx power is: max(P-32, -10) dBm
    P is the max power per antenna (at MCS0)
  When STAs transmit at and above the min power, Tx EVM requirements for a high MCS (at least MCS7) needs to be supported
    Adequate performance needs to be maintained when the STA transmits at its min power

## Slide 14: Absolute Tx Power and RSSI Measurement Accuracy
Inaccuracies in Tx power setting and RSSI measurements can results in excessive interference in UL MU transmissions
  Requirements need to be specified to ensure adequate performance
High capability STAs are likely to be well calibrated and can meet tight accuracy requirements
  However, low cost devices may not have undergone calibration
    Requirements would need be loosed somewhat for low capability devices
Parameter | 11ax Minimum Requirements |  | Comments
 | High Capability STA | Low Capability STA | 
Absolute Transmit Power accuracy | +/-3dB | +/-9dB | Accuracy of achieving a specified transmit power level
RSSI Measurement Accuracy | +/- 2 dB | +/- 5 dB | Difference between the actual RSSI and the measured RSSI Requirements are valid from minimum RX to maximum RX input power

## Slide 15: CFO Requirements
CFO correction is required at the STA to reduce the amount of residual CFO at the AP during UL MU transmissions
  Minimal CFO is essential to reduce interference between users
  Requirement seeks to ensure that the residual CFO is maintained at manageable levels
Propose to define requirement based on the 10% point in the CCDF curve of the residual CFO
  Measured at high Rx power (-60dBm) in AWGN channel
Parameter | 11ax Minimum Requirements | Comments
Residual CFO requirement | 350 Hz | Channel: AWGN Rx power level: -60dBm Requirement is based on the 10% point in the CCDF of the residual CFO

## Slide 16: Timing Requirements
  UL MU transmissions (both UL ODFMA and UL MU-MIMO) need to be received at the AP in a synchronized fashion
    Reduces inter-user interference which is necessary for the AP to decode packets from multiple users
  Triggered transmissions occur xIFS time after the reception of the trigger frame
    Requirements needs to be specified to ensure the accuracy of this timing without imposing undue restrictions on implementation
  We propose that a timing accuracy of +/-0.4µs relative to the Trigger frame is specified
    Note that this requirement is as seen by the AP and does not include round trip delay.

## Slide 17: LO Leakage Requirement
  In 11ac, there are two definitions for LO Leakage: LO is in the center of the transmission or not in the center
    LO being at the center was typical in 11ac with some exceptions
  In 11ax, it is expected that the LO is not at the center of the transmission in many scenarios
    Typically the case when RUs of different sizes are assigned to a group of STAs
    Reasonable to unify the LO leakage requirement across all cases in 11ax
  We propose that a single LO leakage requirement is defined in 11ax and is specified as follows:
    Power measured at the location of the RF LO using resolution BW 78.125 kHz is max(P-32,-20)
      P is the transmit power per antenna in dBm

## Slide 18: Sampling Frequency Offset
Essential to synchronize the sample clock timing and the frequency clock
  Many implementations use estimated CFO to derive the sample clock timing drift
  Pre-correction of the CFO and the sample time need to be coupled together
To avoid any EVM impact due to any timing drift, we propose to adopt the following statement in the specification (as in 11ac):
  “Transmit center frequency and the symbol clock frequency for all transmit antennas and frequency segments shall be derived from the same reference oscillator”

## Slide 19: Straw Poll #1
Do you agree to add the following text in SFD?
  There are two STA classes that support HE trigger-based PPDU with information exchanged as part of the device capability
    Class A: STAs that are high capability devices and
    Class B: STAs that are low capability devices

## Slide 20: Straw Poll #2
Do you agree to add the following text in SFD?
  STAs that participate in HE trigger-based PPDU shall support per chain max(P-32,-10dBm) as the min Tx power, with P the max power the STA can transmit at the antenna connector of that chain using MCS0 while meeting the TX EVM and spectral mask requirements. A STA transmitting at and above the min power shall support the EVM requirements for TBD MCS (but at least MCS7)

## Slide 21: Straw Poll #3
Do you agree to add the following text in SFD?
  STAs that participate in HE trigger-based PPDU shall support the following absolute Tx power requirements and the RSSI measurement accuracy requirements for the two device classes
Parameter | 11ax Minimum Requirements |  | Comments
 | Class A devices | Class B devices | 
Absolute Transmit Power accuracy | +/-3dB | +/-9dB | Accuracy of achieving a specified transmit power level
RSSI Measurement Accuracy | +/- 2 dB | +/- 5 dB | Difference between the actual RSSI and the measured RSSI Requirements are valid from minimum RX to maximum RX input power

## Slide 22: Straw Poll #4
Do you agree to add the following text in SFD?
  STAs that participate in HE trigger-based PPDU shall pre-compensate for carrier frequency offset (CFO) error and timing drift. After compensation, the absolute value of residual CFO error with respect to the corresponding Trigger frame shall not exceed 350Hz for data subcarriers when measured as the 10% point of CCDF of CFO errors in AWGN at a received power of -60dBm in the primary 20MHz. The residual CFO error measurement shall be made on the HE trigger-based PPDU packet after HE-SIGA.

## Slide 23: Straw Poll #5
Do you agree to add the following text in SFD?
  STA that participate in HE Trigger based PPDU transmission shall have timing accuracy of +/-0.4µs relative to the Trigger frame. This requirement does not include round trip delay.

## Slide 24: Straw Poll #6
Do you agree to add the following text in SFD?
  The following TX LO leakage requirements are supported for all transmission modes in 11ax:
    The power measured at the location of the RF LO using resolution BW 78.125 kHz shall not exceed the maximum of –32 dB relative to the total transmit power and -20 dBm, or equivalently max(P-32,-20), where P is the transmit power per antenna in dBm. The transmit center frequency leakage is specified per antenna.

## Slide 25: Straw Poll #7
Do you agree to add the following text in SFD?
  Transmit center frequency and the symbol clock frequency for all transmit antennas and frequency segments shall be derived from the same reference oscillator