## Slide 1: Channel Access in A-BFT over Multiple Channels
Date: 2016-01-21
Authors:

## Slide 2: A-BFT in 802.11ad [1]
11ad channel access
A-BFT in 11ad
•••
A-BFT
BTI
MBIFS
SSW
Frame(s)
SSW-
Feedback
MBIFS
SSW
Frame(s)
SSW-
Feedback
MBIFS
MBIFS
SSW
SSW
SSW
SSW
SSW
SSW
SSW
SBIFS
SSW
FSS=8
SSW slot
#A-BFT Length-1
SSW slot
#0
PCP/AP
STA
PCP/AP announces the number of SSW slots (the size of A-BFT) and the number of SSW frames per SSW slot indicated, respectively, in A-BFT Length subfield (3-bit) and FSS subfield (4-bit) of Beacon Interval Control field in DMG Beacon.

## Slide 3: Channel Access of SSW slots in 11ad A-BFT [1]
Random backoff procedure: An A-BFT starts as: a STA randomly selects SSW slot # based on a uniform distribution [0, A-BFT Length-1] .
One example, in BTI, three DMG STAs receive the DMG Beacon frames including Beacon Interval Control field with “isResponderTXSS=1”, “A-BFT Length=8” and “FSS=8”.
SSW(s)
SSW-
Feedback
PCP/AP
STA
STA A
STA B
STA C

## Slide 4: Collision Probability of SSW slot in A-BFT
SSW slot collision probability
where L is the number of SSW slots at A-BFT and m is the number of STAs that compete channel access.
Assume that the number of SSW slots L = 8.

## Slide 5: 11ay Channel Access in A-BFT over multiple channels
In 802.11ad, the A-BFT is performed over a single channel.
In an EDMG BSS in 802.11ay, SSW and SSW Feedback frame in A-BFT can be transmitted on either the primary channel or a secondary channel with a bandwidth of 2.16 GHz.
A DMG STA shall operate A-BFT only on the primary channel.
- Case 1: when STA B and STA C are not covered by the selected PCP/AP TX antenna sector and a single antenna is used
PCP/AP
STA
SSW
SSW-
Feedback
STA A
STA B
STA B
PCP/AP
STA
STA C
STA C
Primary
channel
Secondary
channel
- Case 2: otherwise when both STA B and STA C can be covered by the same PCP/AP TX antenna sector or the PCP/AP is capable to transmit SSW-Feedback frames simultaneously to STA B and STA C via respective antennas
PCP/AP
STA
SSW
SSW-
Feedback
STA A
STA B
STA B
PCP/AP
STA
STA C
STA C
Primary
channel
Secondary
channel

## Slide 6: Evaluation of 11ay A-BFT over multiple channels
Assume that A-BFT_Length = 8.
The random backoff procedure for selection of an SSW slot in 11ay A-BFT is the same as it in 11ad.
In 11ay A-BFT, an 11ay STA can select one of available channels randomly.

## Slide 7: Summary
Proposed an efficient A-BFT procedure for RSS BF in 802.11ay. The new A-BFT procedure allows transmission of SSW frames sent from different STAs simultaneously over multiple channels for a dense deployment environment in 11ay.

## Slide 8: Straw Poll/Motion
Would you agree to include the following in the SFD: “11ay BF training should support simultaneous multi-STA RSS over multiple channels during A-BFT”?
Yes:
No:
Abstain:

## Slide 9: Reference
[1] IEEE Std 802.11ad - 2012: Amendment 3: Enhancements for Very High Throughput in the 60 GHz Band.