## Slide 1: Rate Matching for HE-SIG-B
Date: 2016-01-18
Authors:

## Slide 2: HE SIG-B Encoding/Decoding Structure
The common field, per-STA information field is encoded and potentially separately decoded.
Common Field
RU alloc.
unit
Padding
RU alloc.
unit
bits
CRC/Tail
STA info
STA info
CRC/Tail
STA info
STA info
CRC/Tail
Per-STA information Field
STA info
CRC/Tail
SIG-B Padding
Decode Block #1
Decode Block #2
Decode Block #3
Decode Block #4

## Slide 3: Example of SIG-B with ¾ Code-Rate
b0
b1
b2
b3
b4
b5
b24
b25
b26
b27
b28
b29
b30
b31
b32
b33
b34
b35
a0
a1
a2
a3
a4
a5
a24
a25
a26
a27
a28
a29
a30
a31
a32
a33
a34
a35
x0
x1
x2
x3
x4
x5
x24
x25
x26
x27
x28
x29
x30
x31
x32
x33
x34
x35
…
…
Common (or STA specific) Info. Field
Rate-matching Unit
Rate-matching Unit
Input Bits
…
…
BCC output
Bits
Tail Bits
b0
b2
b3
b5
b27
b29
b30
b32
b33
b35
a0
a1
a3
a4
a27
a28
a30
a31
a33
a34
…
Rate
Matching
Output
Bits
Common (or STA specific) Info. Field
Common (or STA specific) Info. Field
Common (or STA specific) Info. Field
Common (or STA specific) Info. Field
Common (or STA specific) Info. Field
…

## Slide 4: MCS Table & Rate Matching Unit
MCS Index | Code-Rate | Modulation
0 | 1/2 | BPSK
1 | 1/2 | QPSK
2 | 3/4 | QPSK
3 | 1/2 | 16 QAM
4 | 3/4 | 16 QAM
5 | 2/3 | 64 QAM
6 | 3/4 | 64 QAM
7 | 5/6 | 64 QAM
8 | 3/4 | 256 QAM
9 | 5/6 | 256 QAM
Potentially Problematic
Not Used in SIG-B
No Issue

## Slide 5: Propose Encoding Method for HE SIG-B
Common Field
Encoding
Interleaving
Modulation
iFFT
STA specific Field
(may contain information for1 or 2 STA)
Common Field
Rate Matching Padding
+
Encoding
STA specific Field
(may contain information for1 or 2 STA)
Rate Matching Padding
+
…
SIG-B Contents
Rate-Matching
Rate-Matching
…
Interleaving performed in units of OFDM symbol (i.e. Ncbps)

## Slide 6: Proposed HE-SIG-B Structure
Filler Bits are added to each encoding/decoding block
Filler Bits are added only if needed
In case of encoding block is not multiple of 3 for MCS 2, 4, 6
In case of encoding block is not multiple of 2 for MCS 5
Common Field
RU alloc.
unit
Padding
RU alloc.
unit
bits
8
8
CRC/Tail
STA info
N
STA info
N
CRC/Tail
STA info
N
STA info
N
CRC/Tail
M
Per-STA information Field
Per-STA information Field
STA info
N
CRC/Tail
Per-STA information Field
SIG-B Padding
P
P
P
Rate-Match Padding
P

## Slide 7: Example of the Solution with ¾ Code-Rate
b0
b1
b2
b3
b4
b5
b24
b25
b26
b27
b28
b29
b30
b31
b32
b33
b34
b35
a0
a1
a2
a3
a4
a5
a24
a25
a26
a27
a28
a29
a30
a31
a32
a33
a34
a35
x0
x1
x2
x3
x4
x5
x24
x25
x26
x27
x28
x29
x30
x31
x32
x33
x34
x35
…
…
Common (or STA specific) Info. Field
Rate-matching Unit
Rate-matching Unit
Input Bits
…
…
BCC
output
Bits
Tail Bits
b0
b2
b3
b5
b27
b29
b30
b32
b33
b35
a0
a1
a3
a4
a27
a28
a30
a31
a33
a34
…
…
Rate
-Matching
Output
Bits
Common (or STA specific) Info. Field
Common (or STA specific) Info. Field
Common (or STA specific) Info. Field
Common (or STA specific) Info. Field
Common (or STA specific) Info. Field
Filler Bits
Info. Field is boundary aligned with rate-matching unit

## Slide 8: Conclusion
Filler bits for HE-SIG-B allow completely separate decoding of each STA-specific information field and common field.
  Without filler bits, the receiver will have to take into account bit position of the decoding block and implement a different rate-matching pattern for each decoding block.
  Rate-matching implementation is a integral part of BCC decoding, therefore changes in rate-matching may result in additional change in receiver implementation.

## Slide 9: Strawpoll #1
Do you agree to added the following text to SFD
When MCS 2, 4, or 6 is configured for HE-SIGB, up to 2 (zero valued) filler bits are added after each tail bits of HE-SIG-B encoding block (i.e. common field and STA-specific information field) such that length of an encoding block (including the filler bits) is multiple of 3.
When MCS 5 is configured for HE-SIGB, up to 1 (zero valued) filler bits are added after each tail bits of HE-SIG-B encoding block (i.e. common field and STA-specific information field) such that length of an encoding block (including the filler bits) is multiple of 2.
Y/N/A
Y/N/A

## Slide 10: References
[1] 11-15-0132-13-00ax-spec-framework