## Slide 1: Low Complexity Beamtraining for Hybrid MIMO
Date: 2016-03-13
Authors:

## Slide 2: Abstract
Beam training for Hybrid MIMO in 11ay can be expensive as number of possible beam combinations grows exponentially with number of antenna arrays.
This contribution proposes a low complexity beam training method for 11ay.
The proposed method can be supported with minimal changes in protocols and frame structures of sector level sweep (SLS) and beam refinement phase (BRP) of 11ad.
Results show significant reduction in complexity and negligible losses in resulting MIMO capacity compared to exhaustive search.

## Slide 3: Introduction
Hybrid Beamforming consists of [1]:
analog beamforming find PAA setup to enable communication
digital beamforming find finer precoders for fixed to enable simultaneous transmission of multiple streams
  For , digital beamformers can be found in closed form as in .11n/ac
We focus on 1):
Assume a MIMO case, but easy to generalize
Our goal is to find beam indices:
beam index for 1st TX PAA
beam index for 2nd TX PAA
beam index for 1st RX PAA
beam index for 2nd RX PAA
such that we obtain:

## Slide 4: Motivation
Analog beamforming:
  find beams which can achieve largest MIMO capacity without prior CSI
  minimize amount of necessary training phases / channel estimations
Exhaustive search complexity of 2×2 MIMO:
  HPBW: 90°→ 7 Beams → = 2401
  HPBW: 60°→ 19 Beams → = 1.3
  HPBW: 30°→ 49 Beams → = 5.8∙
Pairwise Search [2] requires several rounds of (reduced) exhaustive searches
Minimize amount of necessary training phases / channel estimations
  Reuse as much as possible 11.ad frame structures and protocols
capacity landscape [6] with 90°HPBW

## Slide 5: Two stage approach in 11ad [3]
Sector level sweep (SLS)
  train transmit beamformers by sector sweeps (SSW) vs quasi-omni receive beamformers
Beam refinement phase (BRP)
    improve receive beamformers (optional MID subphase)
    improve transmit-receive beam combinations (optional BC phase)

## Slide 6: Overview of proposed approach
SLS stage (assuming MIMO case)
  Two independent SISO trainings
  During the training sequence a score vector for each PAA is measured
  Scores indicate the quality of every beam index at each PAA
  Values can be based on SNR or RSSI
Improved BRP
  Combination of best scored beams from SLS does not necessarily give best MIMO capacity but provides a good starting point Second training phase considering and in addition to and
  Make use of a priori information from SLS stage
  2 methods to consider MIMO channel capacity
    Evolutionary beamtraining
    K-Best beamtraining

## Slide 7: SLS stage for Hybrid MIMO
Example for MIMO:
four SSW procedures needed
beam score vector for each PAA created during SSW
feedback of beam scores (subset) necessary
best joint beam combination candidates can be determined from sorted beam score vectors:

## Slide 8: Beam refinement methods
Evolutionary beamtraining
  non-deterministic approach based on random guesses
  probability distribution function (PDF) derived from previously collected beam scores
  ensures convergence by crossover operation
-best beamtraining
  deterministic approach based on beam scores
  tests K best beam score combinations

## Slide 9: Evolutionary beamtraining
  Procedure (iterative):
      Best combination so far: (, ) = (1 1 , 1 1)
      Get random guess (“mutation”) from beam-score-based PDF: () = (2 2 , 2 2)
      Test metric e.g. MIMO capacity for cross-over permutations: () = (1 1, 2 2) and () = (2 2, 1 1)
      Select best combination seen so far Proceed with step 1.
      Termination:
      after iterations or
      iterations without metric improvement
procedure can be used in different stages of beam training procedure
  within pairwise search (PS) [2]
  on top of 11ad-like SLS
  Drawback: Instant feedback needed after each iteration to determine “best combination”
  Potential benefit in rich scattering environments

## Slide 10: -best beamtraining
  Procedure:
      calculate best candidates , from joint score combinations of SLS stage in descending fashion
      sequentially test best candidates and measure respective capacity:
      select beam combination from tested candidates that maximizes MIMO capacity
      decide if further training required according to e.g., progress or MCS

## Slide 11: Simulation parameters
Channel model
  scenario: Conference Room [5], NLOS
  MIMO
  SU-MIMO Configuration #2 [4]: single array, dual polarization, 2 streams
  half power beamwidth 60° 19 Beams
  basic steerable directional antenna model
  50 channel realizations
Evaluated algorithms
  exhaustive search
  pairwise search
  11ad-like (2 SLS)
  Evolutionary algorithm
  K-Best
Conference room scenario [5]

## Slide 12: Complexity and performance comparison
significant reduction in complexity
negligible or no loss in performance

## Slide 13: Protocol and frame structure (K-Best)
SLS:
  if performed sequentially no changes needed
  if performed in parallel EDMG-CEF must contain 2 orthogonal CE sequences
SLS Feedback: the scores must be acquired at either responder or initiator
  Option 1: using TxSSListRequest
  Option 2: extension of SSW-FBACK frames to support best (tbd) sectors rather than first best
  Option 3: feedback on link 1 , while training on link 2

## Slide 14: Protocol and frame structure (K-Best)
Required feedback:
  if further training required (e.g. improvement in obtained capacity)
    indices of next best beams to be set at initiator based on scores
  if no further training required (e.g. obtained capacity saturates or is enough for highest MCS level)
    best beam combination
    digital beamformer (full or reduced) or full channel measurement (for digital beamformer)
BRP:
  responder requests initiator to transmit with best (tbd) beams
  initiator transmits with requested beams, responder listens with corresponding beams
  responder estimates channels and computes the metric (MIMO capacity)
  frame structure with orthogonal TRNs [3] can be employed

## Slide 15: Conclusions
Complexity of beamtraining for hybrid MIMO configurations can be significantly reduced by using the proposed 2 stage approach
  1st stage (SLS) in beam-to-omni configuration, measuring SISO metric as in 11ad
  2nd stage (BRP) in beam-to-beam configuration, measuring MIMO metric
The a-priori knowledge from two SISO-SLS provides useful information for MIMO-BRP phase
  Comparison of -best () w.r.t. Pairwise Search shows
  complexity reduction of approx.
  same performance as Pairwise Search
  The proposed approach requires only small changes to the 802.11ad frame structures and beamtraining procedures

## Slide 16: References
C. Cordeiro et al, “Next Generation 802.11ad”, doc. 11-14-0606r0.
C. Capar et al, “Efficient Beam Selection for Hybrid Beamforming”, IEEE doc. 11-15/1131r0.
A. Kasher, “Beamforming Training proposals”, doc. 11-16-0103r0.
A. Maltsev et al, “Extension of Legacy IEEE 802.11ad Channel Models for MIMO and Channel Bonding”, IEEE doc. 11-15/1356r1.
A. Maltsev et al, “Channel Models for IEEE 802.11ay”, IEEE doc. 802.11-15/1150r2.
F. Fellhauer et al, “Modelling of Spatial Separation in the 11ay Channel Model”, IEEE doc. 802.11-16/0073r1.

## Slide 17: Appendix

## Slide 18: Complexity Analysis MIMO
Complexity:
  K-Best:
  Pairwise Search:
as in slide 12

## Slide 19: Performance comparison (continued)