## Slide 1: I-Q Decoupled OFDM Modulation
Date: 2016-03-14
Authors:
Name | Affiliations | Address | Phone | Email
Shouxing Simon Qu | BlackBerry, Ltd. | 1001 Farrar Rd., Ottawa, ON, Canada | 1-613-595-4205 | squ@blackberry.com

## Slide 2: Abstract
OFDM has been adopted by various communications systems including IEEE 802.11.
I-Q Imbalance (IQI) has significant adverse impact on OFDM performance, as pointed out in [1]-[2].
A new OFDM modulation scheme, called I-Q Decoupled OFDM (DC-OFDM), is proposed in this submission.
In DC-OFDM, the real (I) and the imaginary (Q) time-domain signals are generated using independent input data sets.
DC-OFDM is robust to I-Q Imbalance.
DC-OFDM provides frequency diversity gain.
DC-OFDM provides same data rate as regular OFDM

## Slide 3: OFDM Basics
In regular OFDM, N subcarriers are independently modulated by N complex numbers.
A set of N complex symbols, , is transformed to a set of time-domain complex numbers, , through IDFT,
IDFT: , (1)
DFT: . (2)
k & n: 0, 1, …, N-1.
: specifies the signal magnitude and phase of the k-th subcarrier at frequency Hz.

## Slide 4: General Expressions for DFT/IDFT with Frequency Offset
IDFT: (3)
DFT: . (4)
  with a frequency offset equal to half of subcarrier space.
  .

## Slide 5
Fig. 1
Sequences are cyclically periodic in discrete signal processing.
k
0
1
2
3
4
5
6
7
0
PSD
Subcarriers
(a) N=8, d = 0
k
0
1
2
3
4
5
6
7
0
PSD
Subcarriers
(b) N=8, d = 0.5

## Slide 6: Impact of I-Q Imbalance on OFDM (1)
Transmitted symbol in time-domain : .
Due to IQI, received time-domain symbol:
and .
Thus,
= conjugate of , is interference (in time-domain).
In frequency Domain, ,
where, .

## Slide 7: Impact of I-Q Imbalance on OFDM (2)
Image leaking from ()-th tone to k-th tone.
Image Leakage Ratio (ILR): (dB).
Example 1:
Assuming , then
.
That is, , . dB.

## Slide 8: Impact of I-Q Imbalance on OFDM (3)
Image leaking from ()-th tone to k-th tone.
Example 2: Value of () with N=8:
See Fig. 1: Tones of same color interfere each other
k | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | 0 | 7 | 6 | 5 | 4 | 3 | 2 | 1
k | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | 0 | 7 | 6 | 5 | 4 | 3 | 2 | 1

## Slide 9: Impact of I-Q Imbalance on MU OFDM [1]
Image
Interference
Fig. 2

## Slide 10: OFDM Signal Robust To I-Q Imbalance
Due to IQI, the interference to is .
Solution to IQI: intentionally set
(5)
Then the interference becomes
.
The received signal becomes
.  without interference.
Eq.(5): The sequence of {} is of Conjugate Symmetry in frequency domain.

## Slide 11: Conjugate Symmetry in Frequency Domain
Example: for N=8,
For d = 0.5:
=
.
For d = 0:
= = = = =
and should be real.
.

## Slide 12
Frequency Conjugate Symmetry for d = 0.5
Fig. 3

## Slide 13
Frequency Conjugate Symmetry for d = 0
Fig. 4

## Slide 14
Fig. 5
Power Spectrum with Conjugate Symmetry

## Slide 15: I-Q Decoupled OFDM Signal (1)
The OFDM signals with (frequency) conjugate symmetry are robust to IQI.
Problem:
  with N subcarriers, it only carries information of N/2 complex numbers.
  Compared to regular OFDM, data rate is reduced by half.

## Slide 16: I-Q Decoupled OFDM Signal (2)
Property of Fourier Transform:
  A signal being conjugate symmetrical in frequency domain is a real signal in time domain.
Solution:
Generate two independent real OFDM signals, combined into a complex signal, carrying information of N complex numbers with N subcarriers.

## Slide 17: I-Q Decoupled OFDM Signal (2)
Fig. 6
B1 and B2 can be any box in Fig.3 and Fig. 4.

## Slide 18: Generation of DC-OFDM Signal with Precoding
Fig. 7 ((d = 0.5)
When B0 is bypassed, it becomes a regular OFDM generator.

## Slide 19: DC-OFDM for MU Applications
DC-OFDM can be used for single user or multi-user (MU) applications.
For MU applications: For each pair of symmetric tones,
  The two tones of each symmetric pair are allocated to a same user;
  Two tones of each symmetric pair are modulated by a data symbol and its conjugate respectively.

## Slide 20
Example: Two Users, N=8, d = 0.5
Fig. 8

## Slide 21
Example: Two Users, N=8, d = 0.5
Fig. 9

## Slide 22
Example: Four Users, N=8, d = 0.5
Fig. 10

## Slide 23: DC-OFDM with I-Q Imbalance
Fig. 11

## Slide 24: Simulation Results: I-Q Imbalance Impact
Fig. 12

## Slide 25: Conclusions
IQI has adverse impact on regular OFDM systems.
Real OFDM (time-domain) signal is robust to IQI.
Real time-domain = Conjugate-symmetric in frequency domain.
DC-OFDM signal:
  A complex OFDM signal formed by two independently generated real time-domain OFDM signals.
  Robust to IQI.
  Same data rate as regular OFDM.
  Providing frequency diversity gain.
  SU & MU.

## Slide 26: References
[1] Rui Yang et al., “I/Q Imbalance Impact to TGax OFDMA Uplink Reception”, IEEE 802.11-15/1314r1, Nov. 9, 2015.
[2] Marcus Windisch, and Gerhard Fettweis, “On the impact of I/Q imbalance in multi-carrier systems for different channel scenarios”, IEEE International Symposium on Circuits and Systems 2007 (ISCAS2007), New Orleans, LA, USA, May 27-30, 2007.

## Slide 27: Straw Poll
1) Do you agree that I-Q decoupled OFDM is more robust to I-Q imbalance than the regular OFDM ?
2) Would you consider accepting I-Q decoupled OFDM, or a modified version of this proposal, in 802.11ay draft ?