## Slide 1
Multi-TID Aggregation Limit
Date: 2016-03-14
Authors:
Name | Affiliation | Address | Phone | Email
Chittabrata Ghosh | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-415-244-8904 | chittabrata.ghosh@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Avi Mansour |  |  |  | avi.mansour@intel.com
Chittabrata Ghosh, Intel

## Slide 2: Authors (continued)
Chittabrata Ghosh, Intel
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 3: Authors (continued)
Chittabrata Ghosh, Intel
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4: Authors (continued)
Chittabrata Ghosh, Intel
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 5: Authors (continued)
Chittabrata Ghosh, Intel
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 6: Authors (continued)
Chittabrata Ghosh, Intel
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 7: Authors (continued)
Chittabrata Ghosh, Intel
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 8: Authors (continued)
Chittabrata Ghosh, Intel
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Tomoko Adachi | Toshiba |  |  | tomo.adachi@toshiba.co.jp
Narendar Madhavan |  |  |  | narendar.madhavan@toshiba.co.jp
Kentaro Taniguchi |  |  |  | kentaro.taniguchi@toshiba.co.jp
Toshihisa Nabetani |  |  |  | toshihisa.nabetani@toshiba.co.jp
Tsuguhide Aoki |  |  |  | tsuguhide.aoki@toshiba.co.jp
Koji Horisaki |  |  |  | kouji.horisaki@toshiba.co.jp
David Halls |  |  |  | david.halls@toshiba-trel.com
Filippo Tosato |  |  |  | filippo.tosato@toshiba-trel.com
Zubeir Bocus |  |  |  | zubeir.bocus@toshiba-trel.com
Fengming Cao |  |  |  | fengming.cao@toshiba-trel.com
Parag Kulkarni |  |  |  | parag.kulkarni@toshiba-trel.com
March 2016
Chittabrata Ghosh, Intel

## Slide 10: Authors (continued)
Minho Cheong | Newracom, Inc. | 9008 Research Dr, Irvine, CA 92618 | +1-949-390-7146 | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com
Sigurd Schelstraete | Quantenna | 3450 W. Warren Ave, Fremont, CA 94538 |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quanetnna.com
March 2016
Chittabrata Ghosh, Intel

## Slide 11: Abstract
In this contribution, we discuss the impact of multi-TID aggregation per STA on the Multi-STA BA length
In order to alleviate the large variance in Multi-STA BA length, we propose to limit the number of TIDs from which MPDUs are aggregated in a multi-TID A-MPDU per STA
Chittabrata Ghosh, Intel

## Slide 12: UL MU Transmission Background
802.11ax standard supports aggregation of UL MPDUs from 8 TIDs in an A-MPDU per STA
Without knowledge of MPDU aggregation of different TIDs, the length of the MU-BA frame may vary significantly
  With variations in the number of TIDs sent among all STAs, we will provide results showing significant difference in MU BA frame transmission duration
Trigger frame
UL OFDMA
MU BA/Ack frame
UL AMPDU
STA#1,TID 1
UL AMPDU
STA#1,TID 2 2
UL AMPDU
STA#1,TID 5
UL AMPDU
STA#1,TID 7
UL AMPDU
STA#2,TID 0
UL AMPDU
STA#2,TID 3
UL AMPDU
STA#2,TID 6
UL AMPDU
STA#3,TID 5
UL AMPDU
STA#2,TID 5
UL AMPDU STA#n,TID i
UL AMPDU STA#n,TID j
UL AMPDU
STA#n,TID k
UL AMPDU
STA#n,TID p
TXOP
00
00
00
00
00
00
00
00
00
00
00
00
00
ACK Policy
Chittabrata Ghosh, Intel

## Slide 13: Background - Multi-STA BA for UL MU
Current proposed MU-BA supports BA for multiple TIDs per STA
  Same STA AID in B0-B10 with separate values in TID Value subfield
However, each STA may aggregate MPDUs of different TIDs, resulting in varying size of the BA Information field for each STA
  Absence of the number of TIDs per STA will lead to problem with parsing the BA Information field
    B11 set to 1 even to signal acknowledgment of all MPDUs leading to further ambiguity of BA length
  Moreover , STA can aggregate DATA and management MPDUs

## Slide 14: Computations of MU-BA Duration at the AP - Assumptions
20 octets of FC, Duration, RA, TA, and FCS fields
BA Control field of length 2 octets with proposed solution
BA Information field is of length 12 octets per STA per TID
  For an ACK indication to an STA, only 2 octets
  For a BA indication to an STA, requires 12 octets
  Total length is variable
Chittabrata Ghosh, Intel
March 2016

## Slide 15: Transmission Duration of Multi-STA BA
Final Conclusions (32STAs) :
MU BA frame duration varies between 41us (1TID, ACK) to 1467us (8TIDs, BA )
Chittabrata Ghosh, Intel
Transmission duration of MU-BA with all ACK
Chart: 

1 TID 2 TIDs 3 TIDs 8 TIDs
41us
70us
101us
253us
Chart: 

1 TID 2 TIDs 3 TIDs 8 TIDs
193us
374us
557us
1467us
Transmission duration of MU-BA with all BA
March 2016

## Slide 16: Multi-TID Aggregation with Partial-state Operation
For multi-TID aggregation, AP needs to maintain temporary BA record for MPDUs in each of the aggregated TIDs per STA
  For a single TID per STA, the record consists of a Bitmap indexed by SSN, 12-bit WinStartR, 12-bit WinEndR, STA address, TID, and WinSizeR
  Size of cache memory storing these BA records grows significantly with increasing number of STAs and TIDs in UL MU operation with partial-states (these records are per <RA,TA,TID>)
A limit on the number of TIDs aggregated or acknowledged immediately in an UL MU PPDU would allow the AP to control the size of temporary BA record per STA operating with partial-states
  The duration of the Multi-STA BA is also limited on the basis of above restriction
  Solves the issue discussed in Slide 13
Therefore, we propose to limit the number of TIDs from which MPDUs are aggregated within an HT immediate BA agreement
Chittabrata Ghosh, Intel

## Slide 17: Proposal for Restricted Duration of MU-BA
We propose to define a maximum number of TIDs aggregated in a multi-TID A-MPDU per STA in order to limit duration of the Multi-STA BA
    AP indicates the maximum number of TIDs of MPDUs that a STA can aggregate in a multi-TID A-MPDU
  An HE STA may indicate ACK policy = 00 in an UL MPDU of a specific TID within an A-MPDU
    Number of TIDs with MPDUs indicating ACK policy = 00 shall never exceed the limit indicated by AP

## Slide 18: MSDUs of Single TID in Multiple A-MPDU Sub-frames
Trigger frame
UL OFDMA
MU BA/Ack frame
UL AMPDU
STA#1,TID 1
UL AMPDU
STA#1,TID 2 2
UL AMPDU
STA#1,TID 1
UL AMPDU
STA#1,TID 7
UL AMPDU
STA#2,TID 0
UL AMPDU
STA#2,TID 3
UL AMPDU
STA#2,TID 3
UL AMPDU
STA#3,TID 5
UL AMPDU
STA#2,TID 0
UL AMPDU STA#n,TID i
UL AMPDU STA#n,TID j
UL AMPDU
STA#n,TID i
UL AMPDU
STA#n,TID i
TXOP
00
00
00
00
00
00
00
00
00
00
00
00
00
An STA may aggregate MPDUs with same TID in multiple A-MPDU sub-frames
  For instance, STA # 1 aggregates MPDUs with TID 1 in first and third A-MPDU sub-frame with MPDUs with TID 2 in the second A-MPDU sub-frame
An STA shall assign the same value “00” in the ACK Policy field for all MPDUs carried in the HE trigger-based PPDU [1]
Chittabrata Ghosh, Intel
[1] Jeongki Kim, “ACK Policy of UL MU frame,” doc.: IEEE 802.11-16/0361r0, March 2016

## Slide 19: Conclusions
We have presented the numerical results about the impact of multi-TID aggregation on the Multi-STA BA length
We have proposed to limit the number of TIDs that are aggregated by a STA in a multi-TID A-MPDU
We have also proposed that within a single A-MPDU containing MPDUs with different value of TIDs, the MPDUs with the same TID value are not required to be in contiguous A-MPDU subframes
Chittabrata Ghosh, Intel

## Slide 20: Straw-poll 1
  Do you support to add to the 11ax SFD that the recipient indicates the maximum number of TIDs of the MPDUs that the originator can aggregate in a multi-TID A-MPDU in MU PPDU?
Chittabrata Ghosh, Intel

## Slide 21: Straw-poll 2
  Do you support to add to the 11ax SFD that within a single A-MPDU containing MPDUs with different value of TIDs, the MPDUs with the same TID value are not required to be in contiguous A-MPDU subframes?
Chittabrata Ghosh, Intel

## Slide 22: Appendix
Chittabrata Ghosh, Intel

## Slide 23: Computations of MU-BA Duration at the AP (illustration with 1 TID)
For 32 STAs with 1 TID, signaling overhead for all ACK indication: 20+2+(1*2)*32 = 86 octets
For 32 STAs with 1 TID, signaling overhead for all BA indication: 20+2+(1*12)*32 = 406 octets
Considering 27 octets/symbol (20MHz, MCS 1), transmission time for ACK with proposed MU-BA: 4*3.2us*3.18 = 40.7us (≈ 0.041ms)
Considering 27 octets/symbol, transmission time for BA with proposed MU-BA: 4*3.2us*15.04 = 192.5us (≈ 0.2ms)
Conclusion:
MU BA frame duration for this case varies between 41us to 193us
Chittabrata Ghosh, Intel
March 2016

## Slide 24: Computations of MU-BA Duration at the AP (illustration with 2 TIDs)
For 32 STAs with 2 TIDs, signaling overhead for all ACK indication: 20+2+(2*2)*32 = 150 octets
For 32 STAs with 2 TIDs, signaling overhead for all BA indication: 20+2+(2*12)*32 = 790 octets
Considering 27 octets/symbol (20MHz, MCS 1), transmission time for ACK with proposed MU-BA: 4*3.2us*5.5 = 70.4us (≈ 0.074ms)
Considering 27 octets/symbol, transmission time for BA with proposed MU-BA: 4*3.2us*29.2 = 373.76us (≈ 0.37ms)
Conclusion:
MU BA frame duration for this case varies between 70us to 374us
Chittabrata Ghosh, Intel
March 2016

## Slide 25: Computations of MU-BA Duration at the AP (illustration with 3 TIDs)
For 32 STAs with 3 TIDs, signaling overhead for all ACK indication: 20+2+(3*2)*32 = 214 octets
For 32 STAs with 3 TIDs, signaling overhead for all BA indication: 20+2+(3*12)*32 = 1174 octets
Considering 27 octets/symbol (20MHz, MCS 1), transmission time for ACK with proposed MU-BA: 4*3.2us*7.9 = 101.12us (≈ 0.1ms)
Considering 27 octets/symbol, transmission time for BA with proposed MU-BA: 4*3.2us*43.5 = 556.8us (≈ 0.56ms)
Conclusion:
MU BA frame duration for this case varies between 101us to 557us
Chittabrata Ghosh, Intel
March 2016

## Slide 26: Computations of MU-BA Duration at the AP (illustration with 8 TIDs)
For 32 STAs with 8 TIDs, signaling overhead for all ACK indication: 20+2+(8*2)*32 = 534 octets
For 32 STAs with 8 TIDs, signaling overhead for all BA indication: 20+2+(8*12)*32 = 3094 octets
Considering 27 octets/symbol (20MHz, MCS 1), transmission time for ACK with proposed MU-BA: 4*3.2us*19.77 = 253.05us (≈ 0.25ms)
Considering 27 octets/symbol, transmission time for BA with proposed MU-BA: 4*3.2us*114.59 = 1466.75us (≈ 1.5ms)
Conclusion:
MU BA frame duration for this case varies between 253us to 1467us
Chittabrata Ghosh, Intel
March 2016