## Slide 1: BlockAck Bitmap
Date: 2016-03-12
Authors:
Name | Affiliation | Address | Phone | Email
Dengyu Qiao | Huawei | Bldg1,Tian An Yun Gu, Bian Tian, Shenzhen China | +86-13530774730 | qiaodengyu@huawei.com
Zhenguo Du |  | Bldg1,Tian An Yun Gu, Bian Tian, Shenzhen China |  | Zhenguo.du@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 |  | Zhigang.rong@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 |  | yangyunsong@huawei.com
Zhiming Ding |  | Bldg1,Tian An Yun Gu, Bian Tian, Shenzhen China |  | Dzm.dingzhiming@huawei.com
Qiang Xiao |  | Bldg1,Tian An Yun Gu, Bian Tian, Shenzhen China |  | xiaoqiang797@huawei.com
Miaomiao He |  | Bldg1,Tian An Yun Gu, Bian Tian, Shenzhen China |  | hemiaomiao@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | Roy.luoyi@huawei.com
Jiayin Zhang |  | No 200 Jinsu Road, Shanghai China |  | zhangjiayin@huawei.com

## Slide 2: Authors (continued)
Jun Luo | Huawei | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 3: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 7: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Tomoko Adachi | Toshiba |  |  | tomo.adachi@toshiba.co.jp
Narendar Madhavan |  |  |  | narendar.madhavan@toshiba.co.jp
Kentaro Taniguchi |  |  |  | kentaro.taniguchi@toshiba.co.jp
Toshihisa Nabetani |  |  |  | toshihisa.nabetani@toshiba.co.jp
Tsuguhide Aoki |  |  |  | tsuguhide.aoki@toshiba.co.jp
Koji Horisaki |  |  |  | kouji.horisaki@toshiba.co.jp
David Halls |  |  |  | david.halls@toshiba-trel.com
Filippo Tosato |  |  |  | filippo.tosato@toshiba-trel.com
Zubeir Bocus |  |  |  | zubeir.bocus@toshiba-trel.com
Fengming Cao |  |  |  | fengming.cao@toshiba-trel.com
Parag Kulkarni |  |  |  | parag.kulkarni@toshiba-trel.com

## Slide 11: Authors (continued)
Minho Cheong | Newracom, Inc. | 9008 Research Dr, Irvine, CA 92618 | +1-949-390-7146 | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com

## Slide 12: Background
Multi-STA BA frame has been defined.
  Passed Motion 1: The spec shall define a multi-STA BA frame by using the multi-TID BlockAck frame format with the following changes
    Add an indication that the frame is a multi-STA BA (TBD)
    Each BA information field can be address to different STAs
    B0-B10 of the Per TID Info field carry a (Partial) AID identifying the intended receiver of the BA Information field

## Slide 13: Background
BlockAck bitmap in the BA Info field is carrying the acknowledgement of MPDUs in one A-MPDU.
For Multi-STA BA, the length of Block Ack Bitmap subfield includes two fixed values, 0 or 64 bits (8 bytes).
  Passed Motion 2: The spec shall define a signaling in the multi-STA BA frame that indicates an ACK, as follows
    If B11 in the per-TID info field is set, then the BlockAck bitmap and the SC subfields in the BA Info field are not present and this BA Info field indicates an ACK of either single MPDU or all MPDUs carried in the eliciting PPDU that was transmitted by the STA whose AID is indicated in the per-TID info field.

## Slide 14: Motivation
  Sometime 64-bit Block Ack bitmap may lead to a waste.
    For 11ac, the number of MPDUs included in one A-MPDU is sometimes far less than 64 in experimental scenarios. This is because it is hard for A-MPDU to aggregate enough number of MPDUs, with regard to some of scenarios with real-time requirement, such as VOIP, Online Video.
    See Appendix 1
  For 11ax, UL/DL OFDMA operation may reduce the number of aggregated MPDUs per STA
  For Multi-STA BA, the waste caused by the redundancy of BlockAck bitmap becomes more serious.
    There are more than one BA Info fields included in one Multi-STA BA frame, which means multiple BlockAck bitmaps shall be present.

## Slide 15: Motivation
  Sometime 64-bit Block Ack bitmap may be insufficient [1].
  Bitmap limited to 64 bit implies one BA per each 64 MPDUs
    At high rates, Data PPDUs are short and overhead increases
      A-MPDU without A-MSDU in practice only carries 64x1500 = 96KB = 96us @ 1Gbps
      A-MPDU + A-MSDU can at most packet ~750KB, but heavy use of A-MSDU causes less reliable MPDUs, increased PER

## Slide 16: Proposed scheme (1/2)
If Block Ack Bitmap has variable length, BA will be more efficient.
Some bits of Fragment Number subfield in Block Ack Starting Sequence Control field can be used to carry an indicator of Bitmap Length to indicate the length of the subsequent Block Ack Bitmap subfield.
Bitmap Length
Multi-STA BlockAck

## Slide 17: Proposed scheme (2/2)
Fragment Number subfield can be used to carry the Bitmap Length, e.g. using bit 0 and 1
  00: 8 bytes
  01: 4 bytes
  10: 32 bytes
  11: TBD

## Slide 18: Summary
In order to improve flexibility of BlockAck Bitmap, an indicator of Bitmap Length is introduced
  The Fragment Number subfield in the Block Ack Starting Sequence Control field is used to carry the Bitmap Length
The proposed scheme can be used in Multi-STA BA.
  For example, the BA frame in the SU exchange sequence between two HEW devices

## Slide 19: Straw Poll
Do you agree to add the following text into the SFD?
  The spec shall define a length indication of Block Ack Bitmap subfield included in Fragment Number subfield of the Block Ack Starting Sequence Control field for a multi-STA BA frame, if the Block Ack Bitmap and the Block Ack Starting Sequence Control subfields are present.

## Slide 20: Reference
[1] 11-16/0378r0 Extended BA Bitmap

## Slide 21: Appendix 1
We observe the number of MPDUs included in an A-MPDU in a VHT BSS for different services
  N_MPDU: the number of MPDUs included in an A-MPDU
  Max(N_MPDU): the maximum of N_MPDUs for a specific service
4 types of services are tested
  Web browsing
  VOIP
  Uploading
  Video

## Slide 22
Observations
  Because of real-time requirement, it is hard for A-MPDU to aggregate enough number of MPDUs, with regard to some of scenarios, such as VOIP, Video.
Chart: Max(N_MPDU)
| Web Browsing | VOIP | Uploading | Video
 | 11 | 20 | 27 | 32

## Slide 23
Observations (Web browsing and VOIP)
  More than 70% of the VHT frames include a single VHT MPDU
  The N_MPDU is larger, the probability is smaller
Chart: N_MPDU
 | 0.807 | 0.079 | 0.054 | 0.024 | 0.012 | 0.008 | 0.005 | 0.006 | 0.002 | 0.002 | 0.001
Chart: N_MPDU
 | 0.777 | 0.085 | 0.05 | 0.036 | 0.008 | 0.01 | 0.005 | 0.015 | 0.004 | 0.003 | 0 | 0 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0 | 0.001
Chart: N_MPDU
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
 | 0.079 | 0.054 | 0.024 | 0.012 | 0.008 | 0.005 | 0.006 | 0.002 | 0.002 | 0.001
Chart: N_MPDU
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 0.085 | 0.05 | 0.036 | 0.008 | 0.01 | 0.005 | 0.015 | 0.004 | 0.003 | 0 | 0 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0 | 0.001
Web browsing
VOIP