## Slide 1: Functional requirements for 802.11az
Date: 2016-05-11
Authors:

## Slide 2: Objectives and background
This document proposes a set of functional requirements on scalability for the 802.11az measurement protocol to support a large number of STAs (> 200) in performing positioning concurrently for IoT devices as presented in the use case document [1].
Accuracy and coverage
  Requirements for accuracy and coverage are presented in [2] and already included in the functional requirement document [3] .
Scalability
  Scalability is critical for IoT scenarios, which should support increased number of devices without loss of accuracy or coverage. Typical “Smart building” use cases have been discussed in [4]. Currently no requirements are defined for supporting scalability.

## Slide 3: Requirements for scalability (2.1.3)
The 11.az capable APs shall:
Support locating and tracking at least 200 STAs (e.g. IoT devices) simultaneously
Support a medium usage of maximum 5% and ~50% in case of dedicated 802.11az AP
Support tracking of devices with a refresh rate from 0.1 Hz to 0.5 Hz. A higher refreshing rate can be considered for dedicated APs.
Support user speed between 0 km/h - 3km/h, typical speed for IoT devices
Support latency up to 500 ms (as described in use case document)
Support for unassociated STAs
Notes: Medium usage should be low for legacy devices and it could be reduced by including dedicated az-nodes (APs and STAs). The usage could be higher for the dedicated nodes.
We need a low refresh rate for these devices  also generating low medium usage.
If unassociated devices are supported, the overhead due to handshake will be reduced.

## Slide 4: Motion
Move to adopt the set of functional requirements listed in this document and include them in the TGaz Functional Requirements Document under a sub-section focused on Scalability for the .11az protocol.
  Moved:
  Seconded:
  Result:

## Slide 5: References
[1] https://mentor.ieee.org/802.11/dcn/16/11-16-0137-04-00az-ngp-use-case-document.pptx
[2] Functional requirements for scalability operation 11-16-0134-03-00az-accuracy-and-coverage-functional-requirements
[3] https://mentor.ieee.org/802.11/dcn/16/11-16-0424-01-00az-proposed-802-11az-functional-requirements.docx
[4] https://mentor.ieee.org/802.11/dcn/16/11-16-0315-02-00az-smart-buildings-use-cases.ppt