## Slide 1: Functional requirements for 802.11az
Date: 2016-05-11
Authors:

## Slide 2: Measurement Requirements (2.1.1)
Append the following text as an additional requirement to the end of section 2.1.1:
The 802.11az amendment shall support at least one mode of operation that enables AoA/AoD measurements in the 2.4GHz and 5GHz bands, alone or in conjunction with range measurements.
Notes: Medium usage should be low for legacy devices and it could be reduced by including dedicated az-nodes (APs and STAs). The usage could be higher for the dedicated nodes.
We need a low refresh rate for these devices  also generating low medium usage.
If unassociated devices are supported, the overhead due to handshake will be reduced.

## Slide 3: Requirements for Scalability (2.1.3)
Replace section 2.1.3 R18 as follows:
Current text: Support at least 200 unassociated and associated STAs, per AP performing locationing operation concurrently.
Proposed text: Support locating and tracking all associated and at least 200 unassociated STAs per AP concurrently
Replace section 2.1.3 R20 as follows:
Current text: Utilize less than 10% of the channel capacity of an AP
Proposed text: Support configuration by the network user to modify performance parameters such as the frequency and number of STAs tracked to achieve network resource usage over a range from less than 5% or to greater than 50% in cases were a dedicated AP is present.
Notes: Medium usage should be low for legacy devices and it could be reduced by including dedicated az-nodes (APs and STAs). The usage could be higher for the dedicated nodes.
We need a low refresh rate for these devices  also generating low medium usage.
If unassociated devices are supported, the overhead due to handshake will be reduced.

## Slide 4: Requirements for Scalability (2.1.3) cont.
Replace section 2.1.3 R21 as follows:
Current text: Operate with a maximum refresh rate of .5Hz.
Proposed text: Operate with tracking refresh rates ranging from 0.1 to 0.5Hz with higher refresh rates available in APs dedicated to providing location.
Append the following text as additional requirements to the end of section 2.1.3:
Detect and report STA speeds ranging from 0 to 3km/h.
Report initial STA location within 2sec
Support continuous tracking of STAs with a latency of <= 500ms
Notes: Medium usage should be low for legacy devices and it could be reduced by including dedicated az-nodes (APs and STAs). The usage could be higher for the dedicated nodes.
We need a low refresh rate for these devices  also generating low medium usage.
If unassociated devices are supported, the overhead due to handshake will be reduced.

## Slide 5: Motion
Motion
To adopt the functional requirements listed in slides 2 through 4 of submission 11-16/0579r1 and include them in the TGaz Functional Requirements Document 11-16/0424
  Moved:
  Seconded:
  Result:

## Slide 6: References
[1] https://mentor.ieee.org/802.11/dcn/16/11-16-0137-04-00az-ngp-use-case-document.pptx
[2] Functional requirements for scalability operation 11-16-0134-03-00az-accuracy-and-coverage-functional-requirements
[3] https://mentor.ieee.org/802.11/dcn/16/11-16-0424-01-00az-proposed-802-11az-functional-requirements.docx
[4] https://mentor.ieee.org/802.11/dcn/16/11-16-0315-02-00az-smart-buildings-use-cases.ppt
[5] https://mentor,ieee.org/802.1+/dcn/16/11-16-595-00-00az-proposed-functional-requirements-for-network-based-positioning.pptx