## Slide 1: Left over Issues in RA Signaling for HE-SIGB
Date: 2016-05-16
Authors:
Name | Affiliation | Address | Phone | Email
Yan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | yzhang@marvell.com
Hongyuan Zhang |  |  |  | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 5: Authors (continued)

## Slide 6: Authors (continued)

## Slide 7: Authors (continued)
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com
Minho Cheong | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com

## Slide 11: Overview
The RA signaling table has been agreed in [1] to cover all full allocations.
  There are 16+32+32 = 80 “Definition TBD” entries in the table.
  Those entries can represent some most frequently used partial bandwidth allocations.
Additionally, center 26-tone RU for 80/160MHz BW is not included in the 8-bit table.
  Center 26-tone RU for each 80MHz is not included in any 242-tone RU.
  Need to signal whether the center 26-tone RU has been allocated or not.
8 bits indices | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Num of entries
000 00000 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 00001 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 00010 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 00011 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 00100 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 00101 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 00110 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 00111 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
000 01000 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 01001 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 01010 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 01011 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 01100 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 01101 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 01110 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 01111 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
000 1xxxx | Definition TBD |  |  |  |  |  |  |  |  | 16
001 00yyy | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 8
001 01yyy | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 8
001 10yyy | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 8
001 11yyy | 52 |  | 52 |  | 26 | 106 |  |  |  | 8
010 00yyy | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 8
010 01yyy | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 8
010 10yyy | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 8
010 11yyy | 106 |  |  |  | 26 | 52 |  | 52 |  | 8
011 xxxxx | Definition TBD |  |  |  |  |  |  |  |  | 32
10 yyy yyy | 106 |  |  |  | 26 | 106 |  |  |  | 64
11 0 00yyy | 242 |  |  |  |  |  |  |  |  | 8
11 0 01yyy | 484 |  |  |  |  |  |  |  |  | 8
11 0 10yyy | 996 |  |  |  |  |  |  |  |  | 8
11 0 11yyy | 2*996 |  |  |  |  |  |  |  |  | 8
11 1xxxxx | Definition TBD |  |  |  |  |  |  |  |  | 32
Table 4 - Arrangement and number of MU-MIMO allocations

## Slide 12: Partial Bandwidth Allocation
Partial bandwidth allocation includes both empty allocation (no user is scheduled for a 242-tone RU), or partially allocated BW per 20MHz channel.
It is impossible to cover all partial allocated RU combinations by 8bit table (need at least 11bit table).
Focus on only 1 unallocated RU in the discussion.
  If there are more than 1 unallocated RUs, we can always use “dummy STA ID” for user info signaling in HESIGB user fields.

## Slide 13: Case 1: Empty Allocation
Non-contiguous channel bonding,
  There is no user to signal in a punctured 242-tone RU.
  It is essential to add an entry corresponding to zero users in this 242-tone RU, instead of using a “dummy STA ID” in user field to save some overhead.

## Slide 14: Case 2: Partial Allocations with Only Large RUs Allocated
There is no 26-tone RU allocated within each 20MHz channel
  Most frequent partial allocations cases are the ones where center 26-tone RU is not allocated.
There are total “1 (52+52) + 64 (106+106) + 8 (52+52+106) + 8 (106+52+52) = 81” combinations.
  Given the number of available entries in the table, we can limit the number of spatially multiplexed users to 4 in each 106-tone RU for the 106+106 case.
  Still some entries are left for other purposes.
52
52
52
52
52
52
52
52
106
106
106
106

## Slide 15: Center 26-tone RU for 80/160MHz
Use 1 bit to indicate if the center 26-tone RU is allocated for each 80MHz. (2 bits if 160MHz or 80+80MHz).
  Negligible overhead added, save “dummy STA” user info overhead in user fields
For full BW 80MHz, add 1 bit indication of the same value in the common block fields of both SIGB content channels.
For full BW160MHz, add 1 bit indication, corresponding to one individual 80MHz, in common block fields of both SIGB content channels.

## Slide 16: Proposed Changes to RA Signaling
Propose to replace 36 “Definition TBD” entries with the highlighted entries highlighted in Table 4 in 11ax SFD 3.2.5 HE-SIG-B sub-clause to indicate most frequently used partial bandwidth allocations.
‘zz’ = 00~11 indicates number of spatially multiplexed STAs for 106-tone RU in partial bandwidth allocations.
8 bits indices | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Num of entries
000 0 0000 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 0 0001 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 0 0010 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 0 0011 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 0 0100 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 0 0101 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 0 0110 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 0 0111 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
000 0 1000 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
000 0 1001 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
000 0 1010 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
000 0 1011 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
000 0 1100 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
000 0 1101 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
000 0 1110 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
000 0 1111 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
000 1 0yyy | 52 |  | 52 |  | - | 106 |  |  |  | 8
0001 1yyy | 106 |  |  |  | - | 52 |  | 52 |  | 8
00100 yyy | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 8
00101 yyy | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 8
00110 yyy | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 8
00111 yyy | 52 |  | 52 |  | 26 | 106 |  |  |  | 8
01000 yyy | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 8
01001 yyy | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 8
01010 yyy | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 8
01011 yyy | 106 |  |  |  | 26 | 52 |  | 52 |  | 8
0110 zzzz | 106 |  |  |  | - | 106 |  |  |  | 16
0111 0000 | 52 |  | 52 |  | - | 52 |  | 52 |  | 1
0111 0001 | 242-tone RU empty |  |  |  |  |  |  |  |  | 1
0111 0010 | 484-tone RU empty |  |  |  |  |  |  |  |  | 1
0111 0011 | 996-tone RU empty |  |  |  |  |  |  |  |  | 1
0111 01xx | Definition TBD |  |  |  |  |  |  |  |  | 4
0111 1xxx | Definition TBD |  |  |  |  |  |  |  |  | 8
10 yyy yyy | 106 |  |  |  | 26 | 106 |  |  |  | 64
11 0 00yyy | 242 |  |  |  |  |  |  |  |  | 8
11 0 01yyy | 484 |  |  |  |  |  |  |  |  | 8
11 0 10yyy | 996 |  |  |  |  |  |  |  |  | 8
11 0 11yyy | 2*996 |  |  |  |  |  |  |  |  | 8
11 1 xxxxx | Definition TBD |  |  |  |  |  |  |  |  | 32
Table 4 - Arrangement and number of MU-MIMO allocations

## Slide 17: Reference
[1] IEEE 802.11-15/1335r0 HE-SIG-B Contents

## Slide 18: SP1
Do you support to add the following to the current SFD:
  For full BW 80MHz, add 1 bit to indicate if center 26-tone RU is allocated in the common block fields of both SIGB content channels with same value.
  For full BW160MHz, add 1 bit to indicate if center 26-tone RU is allocated for one individual 80MHz in common block fields of both SIGB content channels.

## Slide 19: SP2
Do you support to use 36 “Definition TBD” entries in Table 4 in the current SFD 3.2.5 HE-SIG-B sub-clause to indicate most frequently used partial bandwidth allocations, as shown in slide 15?