## Slide 1: Open Loop vs Closed Loop SU-MIMO for 11ay
Date: 2016-05-16
Authors:

## Slide 2: Abstract
In this contribution we demonstrate potential benefit from using closed loop (or channel-dependent precoding) SU-MIMO via system level simulations with different antenna configurations and deployment scenarios.

## Slide 3: Background
Open loop (OL) SU-MIMO is a viable MIMO scheme for communication in mmW if the analog beam width is very narrow and LoS link is available
The performance of open loop SU-MIMO may be degrade by strong inter-stream interference. This may be caused by mutual coupling between the antennas, near field interference, antenna distances, and channel conditions [2].
Questions for a given antenna configuration
  In which scenario will the inter-stream interference be strong?
  If closed-loop (CL) SU-MIMO is used, e.g. channel-dependent precoding, can SU-MIMO improve the performance in the presence of strong inter-stream interference?

## Slide 4: Analysis based on Idealized Channel
LoS channel model [2]
  are random variables, uniformly distributed between 0 and
Receiver: LMMSE
CL SU-MIMO is achieved by precoding the Tx signal with the “V” matrix generated from SVD of the channel matrix (
Performance metric
  Achievable sum rate of two streams based on per stream SINR at the output of the LMMSE
    , where is the per-stream SINR at the MMSE output) [5]
Observation
  CL SU-MIMO outperforms OL SU-MIMO when the inter-stream interference is strong.

## Slide 5: Analysis based on 11ad Channel Models
Consider antenna configuration #3 [3]
  Each PAA has 4x4 antenna elements
  Include Right (R) and Left (L) hand circular polarization cases.
  Assume the distance (d) between two antennas is 5cm
Back lobes are assumed blocked
R
or
L
R
or
L
Polarization cases
  Linear Polarization
  Tx(V, V) – Rx(V, V)
  Tx(V, H) – Rx(V, H)
  Circular Polarization
  Tx(L, L) – Rx(L, L)
  Tx(L, L) – Rx (R, R)
The relative orientation of the Tx and Rx is included when generating the channel matrices [4].

## Slide 6: Simulation Setup
Consider five different models described in [1]
  Case 1: Cubicle Laptop Far (NLoS only)
  Case 2: Cubicle Laptop Near (LoS + NLoS)
  Case 3: Conference Room STA-STA (LoS + NLoS)
  Case 4: Conference Room STA-AP (LoS + NLoS)
  Case 5: Living Room (LoS + NLoS)
Stations are randomly placed with one degree freedom in orientation
Analog Tx and Rx beams are assumed perfectly aligned in cases with LoS
.
Top view of case 3 and 5
.
Top view of case 1,2 and 4
AP

## Slide 7: Distribution of Inter-stream Interference Power
Measure the distribution of
measures the orthogonality of the channel matrix
Observation: The distribution of p value depends antenna configuration and deployment scenarios
(Results with circular polarized antennas are available in Appendix)

## Slide 8: Achievable Sum Rate of LMMSE
Achievable sum rate = , where is the per-stream SINR at the MMSE output.
Observation: The sum rate gain of CL SU-MIMO over OL SU-MIMO depends on polarization of the antennas, deployment scenarios and SNR
(Results with circular polarized antennas are available in Appendix)

## Slide 9: Conclusion
Although the OL SU-MIMO is an important MIMO mode for 11ay due to its simplicity, its performance may suffer from strong inter-stream interference which depends on many different factors, such as antenna configuration, polarization, environment, accuracy of analog beamforming, etc..
The 11ay system throughput may benefit from CL SU-MIMO, especially when the inter-stream interference is strong.
The cost-benefit of using CL SU-MIMO may need to be studied further with consideration of more antenna configurations and usage cases generated in TGay.

## Slide 10: References
Alexander Maltsev, et. al., ”Channel Models for 60 GHz WLAN Systems”, 11-09-0334-08-11ad
Artyom Lomayev, et. al., “Performance Analysis of Open Loop SU-MIMO Receivers for IEEE 802.11ay”, IEEE 802.11-16/0388r0
Alexander Maltsev, et. al. “Channel models for ieee 802 11ay”, IEEE 802.11-15/1150r3
Rui Yang, et. al. “Channel Modeling with PAA Orientations”, IEEE 802.11-16/0339r1
Matthew R. McKay, et. al., “Achievable Sum Rate of MIMO MMSE Receivers: A General Analytic Framework”, IEEE Transaction on information theory, Vol. 56, No. 1, Jan 2010

## Slide 11: Appendix
Inter-stream interference power distribution and CL gain over OL SU-MIMO for Configuration #3 with polarized antennas

## Slide 12: SP (for survey)
Do you agree that closed-loop SU-MIMO based on channel-dependent precoding should be considered for 802.11ay?
Y:
N:
A: