## Slide 1: LiFi: Concept, Use-cases and Progress
Date: 2016-05-10
Authors:

## Slide 2: Abstract
The exponential demand for wireless communications, estimated at over 70% CAGR, is set to continue. The electromagnetic spectrum is becoming increasingly crowded and alternative, unlicensed mediums are being explored.
Light offers a completely unlicensed and very well understood medium for wireless communications. The use of light to provide high speed, bidirectional and networked wireless communications is named LiFi.

## Slide 3: What is LiFi?

## Slide 4: LiFi: Competitive Advantages
Security
Safety
Localization
Data density
No Regulatory Constraints – Globally Unlicensed

## Slide 5: Capacity
There are capacity bounds defined by Shannon’s Theory
OWC Channel not a Gaussian (non-negative, real-valued signal with an Average Power Constraint), but can be modeled to be similar
There is an upper bound (You/Kahn 2002)
  DCO-OFDM + Good Coding
  Improved waveform
    U-OFDM
    ACO-OFDM

## Slide 6: Capacity
There are capacity bounds defined by Shannon’s Theory
OWC Channel not a Gaussian (non-negative, real-valued signal with an Average Power Constraint), but can be modeled to be similar
There is an upper bound (You/Kahn 2002)
  DCO-OFDM + Good Coding
  Improved waveform
    U-OFDM
    ACO-OFDM

## Slide 7: Optical OFDM
TIA
Sym. Map
Sym. DE-Map
No Up-conversion

## Slide 8: No Up-Conversion = Baseband Modulation
Incoherent Modulation
The Baseband signal is modulated by changing the Intensity of the Light
The Baseband signal is detected by measuring Directly Detecting the light intensity
“Morris Code” 2.0
Wavelength Division Multiplexing to utilize the entire Light Spectrum

## Slide 9: DC-biased Optical-OFDM
.
is the DC biased

## Slide 10: DC-biased Optical-OFDM

## Slide 11: Unipolar Optical-OFDM

## Slide 12: Unipolar Optical-OFDM

## Slide 13: The Architecture
Switch
Gateway DHCP Server
Power & Data

## Slide 14: Energy Efficiency
Computational Efficiency
  Proposed protocols have similar computational complexity to existing communication protocols such as 802.11 g/n/ac PHYs
  Detailed specifications for a proposal can be found:
    https://mentor.ieee.org/802.15/dcn/16/15-16-0363-00-007a-text-input-lifi-low-bandwidth-phy-and-mac-d0.docx
    https://mentor.ieee.org/802.15/dcn/16/15-16-0356-01-007a-text-input-for-high-bandwidth-phy.zip
Availability of Energy
  Lighting is already present and consuming power
Electromagnetic Radiated power
  Smaller wavelength of light means it requires more energy to achieve the same distance

## Slide 15: IR vs. VLC
Time has changed the key factors for this technology:
  Components
  Constraints
  Use-cases
Technology
  High power devices can be produced with VL (regulation/health&safety)
  IR receiver technology is more developed today
  Optical OFDM
  Networking (Handover & Multiple Access)

## Slide 16: Security
Cyber
  Use of existing 802.1x capabilities
Physical
  Light signals power degrades quicker than any other RF signal.
  Confined, clearly visible coverage area
  Intuitive

## Slide 17: Emitter Technology

## Slide 18: Receiver Technology
PIN Photo-Diode (PD)
Avalanche PD (APD)
Single-photon APD
(SPAD)
Data Rate / Gbps
100
10
1
0.1
Research
Solar-cells

## Slide 19: Impact of LiFi on CRI & Lifetime of LEDs
“Provided adequate thermal management is used, the average drive current dictates the emitted light quality (CRI, CCT and chromaticity) but not the instantaneous drive current. Hence to preserve the expected light quality of LEDs used for LiFi, the modulating signal must be balanced.”
  W. O. Popoola, “Impact of VLC on Light Emission Quality of White LEDs,” Journal of Lightwave Technology, Vol. 34, No. 10, May15, 2016.

## Slide 20: 802.11 vs. LiFi
 | 802.11 | LiFi
Medium | RF | Light
Signal Modulation | Coherent | IM/DD
Duplex | Half (Full ?) | Full
Hidden Node | Rarely Occurs | By Design CSMA/CA does not work

## Slide 21: Co-existence

## Slide 22: Co-existence
Network
Cell 1
Cell 2
User 1
Handover
Router and WiFi AP
RF
Optical
VLC offloading WLAN and/or cellular traffic in a 3-tier HetNet
RF for uplink
Data aggregation in RF and/or optical
Seamless connectivity in a mobile multiuser access scenario
Gigabit applications while supporting:
Illumination functionality
  Color tunable
  Dimmable
High quality lighting
  CCR
  CRI

## Slide 23: Co-existence

## Slide 24: The LiFi Optical Atto-cell Network
Cellular network in a room: optical atto-cell network.
Each light functions as a base station covering a very small area (typically 1-10 m2).
Inherent properties of light reduce interference:
  No signals outside the room
  Easy beamforming with optics
  Enhanced security

## Slide 25: Het. Nets = Small Cells
I. Stefan, H. Burchardt, and H. Haas, “Area spectral efficiency performance comparison between VLC and RF femtocell networks,” ICC, 2013.

## Slide 26: Interference Coordination in VLC
Spectrum reuse leads to co-channel interference (CCI).
Interference coordination techniques in OW:
  Traditional static resource partitioning [2]
  Busy-burst-signalling-based interference-aware resource allocation [3]
  Fractional frequency reuse [4].
[2] G. W. Marsh, J. M. Kahn, “Channel Reuse Strategies for Indoor Infrared Wireless Communications,” IEEE Trans. on Commun., 1997.
[3] B. Ghimire and H. Haas, “Self Organising Interference Coordination in Optical Wireless Networks,” in EURASIP Journal on Wireless Communications and Networking, 2012.
[4] C. Chen, et. al., “ Fractional frequency reuse in optical wireless networks,” in PIMRC, 2013.

## Slide 27: Joint Transmission in VLC
LED array design:
VLC Downlink network:
Transmission region division:
Frequency plan:

## Slide 28: Simulation Results
Signal to Interference plus Noise Ratio (SINR):

## Slide 29: References
I. Stefan, H. Burchardt, and H. Haas, “Area spectral efficiency performance comparison between VLC and RF femtocell networks,” ICC, 2013.
G. W. Marsh, J. M. Kahn, “Channel Reuse Strategies for Indoor Infrared Wireless Communications,” IEEE Trans. on Commun., 1997.
B. Ghimire and H. Haas, “Self Organising Interference Coordination in Optical Wireless Networks,” in EURASIP Journal on Wireless Communications and Networking, 2012.
C. Chen, et. al., “ Fractional frequency reuse in optical wireless networks,” in PIMRC, 2013.
H. Haas, L. Yin, Y. Wang, and C. Chen, "What is LiFi?," in Journal of Lightwave Technology , vol.PP, no.99, 2016
C. Chen, D. A. Basnayaka, and H. Haas, "Downlink Perormance of Optical Attocell Networks," in IEEE Journal of Lightwave Technologies, vol. 34, no. 1, pp. 137-156, Jan. 2016.
Dobroslav Tsonev, Stefan Videv, and Harald Haas, "Towards a 100 Gb/s visible light wireless access network," Opt. Express 23, 1627-1637 (2015)
M. Ayyash, H. Elgala, A. Khreishah, V. Jungnickel, T. Little, S. Shao, M. Rahaim, D. Schulz, Coexistence of WiFi and LiFi towards 5G: Concepts, Opportunities, and Challenges, IEEE Communiations Magazine, Optical Communications Series, vol. 54, no. 2, pp. 64-71, February 2016.
Yunlu Wang and Harald Haas, “Dynamic Load Balancing with Handover in Hybrid Li-Fi and RF Networks”, Journal of Lightwave Technology, vol. 33, no. 22, pp.4671-4682, 2015.