## Slide 1: Clarification of SR Fields in HE Trigger Based PPDU
Date: 2016-07-25
Authors:
Name | Affiliation | Address | Phone | Email
Daewon Lee | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Minho Cheong |  |  |  | minho.cheong@newracom.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Thomas Derham |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Feng Jiang |  |  |  | feng1.jiang@intel.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Lochan Verma |  | 5775 Morehouse Dr. San Diego, CA USA |  | lverma@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 6: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com
Narendar Madhavan | Toshiba |  |  | narendar.madhavan@toshiba.co.jp
Masahiro Sekiya |  |  |  | 
Toshihisa Nabetani |  |  |  | 
Tsuguhide Aoki |  |  |  | 
Tomoko Adachi |  |  |  | 
Kentaro Taniguchi |  |  |  | 
Daisuke Taki |  |  |  | 
Koji Horisaki |  |  |  | 
David Halls |  |  |  | 
Filippo Tosato |  |  |  | 
Zubeir Bocus |  |  |  | 
Fengming Cao |  |  |  | 

## Slide 11: Re-Cap of SR Motion #8
Add the following 4 bit SR field (in SIG A) for HE Trigger-Based PPDU
  One TBD value for SR Disallow Flag, (under TBD restrictions)
  One TBD value is reserved
  Remaining 14 values for SRP
    SRP = TX PWRAP + Acceptable Receiver Interference Level at AP
    SR STA shall back-off its TX power based on
    TX PWRSR STA < SRP – RSSI trigger frame @ SR STA”
For HE trigger-based PPDU, in HE SIG-A, 4 SR fields are signaled:
  For 20MHz one SR field corresponding to entire 20MHz (other 3 fields indicate identical values)
  For 40MHz two SR fields for each 20MHz (other 2 fields indicate identical values)
  For 80MHz four SR fields for each 20MHz
  For 160MHz four SR fields for each 40MHz
  The exact location of each 20MHz for 80MHz BW is TBD”

## Slide 12: Background
For HE trigger-based PPDU, four SR fields are signalled in Trigger frame:
  For 20MHz, one SR field corresponding to entire 20MHz (other 3 fields indicate identical values)
  For 40MHz, two SR fields for each 20MHz (other 2 fields indicate identical values)
  For 80MHz, four SR fields for each 20MHz
  For 160MHz, four SR fields for each 40MHz
  The exact location of each 20MHz for 80MHz BW is TBD
SR field 1
SR field 2
SR field 3
SR field 3
SR field 1
SR field 2
SR field 3
SR field 4
SR field 1
SR field 2
SR field 3
SR field 4
For 20MHz
Four SR fields in Trigger frame
SR field 1
SR field 2
SR field 3
SR field 4
For 40MHz
For 80MHz
For 160MHz
Note- Different colors of the SR field indicate that values may be different

## Slide 13: SR Field Interpretation Ambiguity
We assume that each of the SR fields in HE trigger-based PPDU correspond to 20 (or 40) MHz bands starting from lowest frequency to highest frequency.
However, There are few cases where the interpretation the SR field in the HE trigger based PPDU is ambiguous.
  40MHz HE Trigger-based PPDU in 2.4GHz band
  80+80MHz HE Trigger-based PPDU in 5GHz band
We provide some examples of ambiguity in the next two slides.

## Slide 14: Issue on SR Field Interpretation in 2.4 GHz
OBSS STAs receiving a HE Trigger-based PPDU cannot distinguish whether received HE PPDU is from Candidate 1 or 2.
Field Interpretation ambiguity exists
SR1
SR2
SR1
SR2
Candidate 1
Candidate 2
40MHz
40MHz
Freq.
Freq.
OBSS - STA
Freq.
Receives This 20MHz
HE PPDU
HE PPDU
SR1
SR2
SR1
SR2
…
HE-SIG-A
…
OBSS - STA
Which One?

## Slide 15: Issue on SR Field Interpretation in 5 GHz
OBSS STAs receiving a HE Trigger-based PPDU cannot distinguish whether received HE PPDU is from Candidate 1, 2, or 3.
Field Interpretation ambiguity exists
HE PPDU
SR1
SR2
SR3
SR4
…
HE-SIG-A
…
OBSS - STA
Which One?
SR1/SR2
SR3/SR4
SR1/SR2
SR3/SR4
Candidate 1
Candidate 2
160MHz
80 + 80 MHz
Freq.
Freq.
Freq.
OBSS - STA
Freq.
Receives This 80MHz
HE PPDU
Candidate 3
SR1/SR2
SR3/SR4
80 + 80 MHz

## Slide 16: Potential Solutions
Option 1) For the problematic cases, AP shall set the same SR fields between ambiguous bands.
  For 40MHz in 2.4GHz, same SR field value in each 20MHz
  For 80+80MHz in 5GHz, same SR field value in each 80MHz band (which consists of two 40MHz)
Option 2) For the problematic cases, STA chooses worst case SR field between ambiguous bands.
  For 40MHz in 2.4GHz, choose the worst case SR field among 20MHz
  For 160MHz and 80+80MHz in 5GHz, choose the worst case SR field value between the two 80MHz band (which consists of two 40MHz)
Option 3) Provide extra signaling to HE-SIG-A to allow resolution of SR fields

## Slide 17: Example of Option 1
OBSS STA uses the SR values corresponding to 80MHz SR band.
It is up to AP to configure 80+80MHz (to have same value between 80MHz segments) to avoid ambiguity.
If different values are set for SR1/2/3/4, STA can implicitly find out that this is from a 160MHz HE PPDU (i.e. candidate 1)
HE PPDU
SR1
SR2
SR3
SR4
…
HE-SIG-A
…
OBSS - STA
Uses this SR fields (based on 80MHz location)
SR1/SR2
SR3/SR4
SR1/SR2
SR1/SR2
Candidate 1
Candidate 2
160MHz
80 + 80 MHz
Freq.
Freq.
Freq.
OBSS - STA
Freq.
Receives This 80MHz
HE PPDU
Candidate 3
SR1/SR2
SR1/SR2
80 + 80 MHz

## Slide 18: Discussion & Conclusion
Option 1 is the preferred solution to resolve SR field ambiguity.
  Simpler receiver behavior & logic
  No changes to bit field design of HE-SIG-A
 | Pros | Cons
Option 1 | Simple STA behavior and logic | AP is mandated to operation conservatively in 80+80MHz in 5GHz band.
Option 2 | If STA is aware of exact channelization, STA is able to utilize all band specific SR field | STAs has to operate conservatively when receiving both 160MHz and 80+80MHz. Requires STAs to perform additional logic and inconsistent behavior depending on situation
Option 3 | Full resolutions of SR field ambiguity | Requires either changes to the HE-SIG-A signaling structure or additional bit fields to be included in HE-SIG-A

## Slide 19: Strawpoll #1
Do you agree to accept the proposed text changes in document “11-16/0902r1, Proposed Text Changes for SR Fields in HE Trigger-Based PPDU”?
  Note: the proposed text changes are based on option 1 of this document.
Y/N/A

## Slide 20: References
[1] 11-16/XXXXr0, Proposed Text Changes for SR Fields in HE Trigger-Based PPDU