## Slide 1: EDMG-CEF Design for Control and SC PHY in MIMO Modes
Date: 2016-07-25
Authors:

## Slide 2: Abstract
In this contribution we propose two EDMG-CEF design options for control and single carrier PHY to support 11ay SU and MU MIMO.

## Slide 3: Background
TGay has agreed that 11ay will support SU-MIMO and MU-MIMO [1]
To support those MIMO schemes, it has also been agreed that the EDMG PPDU will have the following format [1]
“EDMG-CEF” needs to be designed to enable MIMO schemes.
It is desirable to design a set of orthogonal CE sequences, one for each spatial stream
  Analog beamforming may not be effective to completely separate spatial streams [3] [4]
L-STF | L-CEF | L-Header | EDMG-Header-A | EDMG-STF | EDMG-CEF | EDMG-Header-B | Data | AGC | TRN

## Slide 4: Properties of CEF in 11ad (1/2)
CEF for Control and SC PHY [2]
  Constructed using Golay complementary pair
  “Circulant Property”: Having both cyclic prefix and cyclic suffix
Waveform (p/2 BPSK)

## Slide 5: Properties of CEF in 11ad (2/2)
Cyclic Auto-Correlation of
  is orthogonal to its up-to +/- 256-sample cyclic shifts
Using , the estimated channel impulse responses will not suffer from interference due to channel multipaths and sampling time offset up to +/- 256 samples
+/- 256 Samples

## Slide 6: Variants of 11ad CEF
The length of 11ad CEF could be reduced by including only Gu512 or Gv512 (Reduced CEF)
  Reduces latency, but also reduces SNR and zero-correlation range
The length of 11ad CEF could also be extended by including multiple Gu512 and/or Gv512 (Extended CEF)
  Increases SNR and zero-correlation range, but also increases latency
In both cases, the circulant property is preserved.
Gu512 or Gv512
-Gb128
-Ga128
…
STF
Reduced CEF
Gu512 | Gv512
-Gb128
-Ga128
…
STF
Extended CEF
Gu512 | Gv512
+/- 128 Samples

## Slide 7: Proposals of EDMG-CEF for MIMO
We recommend that
  The sequences in EDMG-CEF will be based on a Golay complementary pair used in L-CEF
  The basic building block could be or its variants, e.g. for reduced CEF, and for extended CEF, depending on the need.
  The basic building block should be modulated based on rotated modulation, such as pi/2-BPSK
  EDMG-CEF should include CE sequences , one for each space-time stream, where is the number of space-time streams.
  and should provide zero cyclic cross-correlation within certain range. For example
  , where and

## Slide 8: EDMG-CEF Options for Two-Stream MIMO (1/2)
Option 1: Using “P matrix” concept
  P matrix is an orthogonal matrix, e.g.,
Stream 1
…
…
EDMG-CEF
Stream 2
Note: The length of EDMG-CEF can be reduced by using or only
in and
This could be put at the end of EDMG-STF

## Slide 9: EDMG-CEF Options for Two-Stream MIMO (2/2)
Option 2: = Conjugate()
Stream 1
…
…
EDMG-CEF
Stream 2
Cyclic auto correlation
of
Cyclic auto correlation
of
Cyclic cross correlation
of and
Note: The length of EDMG-CEF can be extended by using multiple or/and in .
This could be put at the end of EDMG-STF

## Slide 10: Simulation Results
Assume CIR:
h1(1)=1-j2; h1(20)=3-j4; h2(1)=-1+j2; h2(64)=-3+j4
Channel Estimation Using P-Matrix
Channel Estimation Using Conjugation

## Slide 11: Further Design Considerations
In case of four-space-time-stream transmission, one can use either 4x4 P orthogonal matrix or combination of 2x2 P matrix and conjugation methods.
Reduced CEF and Extended CEF mechanisms can be used with trade-off between the latency and SNR, which may depend on the existence of LoS, antenna configurations, environment, etc.

## Slide 12: References
[1] Carlos Cordeiro, “Specification Framework for TGay”, IEEE 802.11-15/01358r4
[2] Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications, Amendment 3: Enhancements for Very High Throughput in the 60 GHz Band
[3] Rui Yang, et. al., “Open Loop vs Closed Loop SU-MIMO for 11ay”, IEEE 802.11-16/0642r1
[4] Li-Hsiang Sun, et. al. “Link Level Performance Comparisons of Open Loop, Closed Loop and Antenna Selection for SU-MIMO”, IEEE 802.11-16/0911r0

## Slide 13: SP
Do you agree that the SFD will include the following
EDMG-CEF shall be built based on a Golay complementary pair, e.g., defined in 11ad
  Y/N/A:
The basic building block of EDMG-CEF shall include a combination of the sequences in the L-CEF, i.e., , with the circulant property.
    Y/N/A:
The basic building block of EDMG-CEF may be extended or reduced.
    Y/N/A:
  The basic building block shall be modulated using rotated BPSK, e.g., pi/2-BPSK as L-CEF.
  Y/N/A: