## Slide 1: TID value of ALL ACK signaling
Date: 2016-07-27
Authors:

## Slide 2: Recap. Multi-STA BA format
9.3.1.9.7 Multi-STA BlockAck variant[1]
  … The TID subfield(#2581) contains the TID for which the acknowledgment or block acknowledgment applies. If the Ack Type(#1408) field is 0, then the Block Ack Starting Sequence Control and Block Ack Bitmap subfields(#1274) are not present and the Per STA Info subfield(#1141) indicates the acknowledgment of successful reception of either a single MPDU or of all the MPDUs carried in the eliciting (A-)MPDU(#1276). If the Ack Type(#1408) subfield is 1, then the Block Ack Starting Sequence Control and Block Ack Bitmap subfields(#1141) are present.

## Slide 3: Motivation
In all ACK situation, one BA information may inform acknowledgement for multiple TIDs
  ACK type is set to 0
TID setting rule for All ACK case is not defined
The originator STA may confuse All ACK with single ACK in certain situations
  MPDUs with no BA agreement are also allowed to be aggregated in Multiple TID A-MPDUs
    Acknowledged by M-BA as well
    ACK type will be set to 0
  Currently all 16 TID values are assigned for specific purposes
    E.g., EDCA and HCCA

## Slide 4: Ambiguity in All ACK signaling
TID0
MMPDU
No BA agreement
TID3
A-MPDU (AID:1)
TID2
AID:1
ACK type:0
TID:0-15
TID2
…
All MPDUs are decoded correctly
TID0
MMPDU
No BA agreement
TID3
TID2
AID:1
ACK type:0
TID:0
TID2
…
Only one MPDU is decoded
BA information for AID:1
TID value for All ACK may be set to one of TIDs aggregated in the A-MPDU
The originator may not distinguish All ACK and single ACK upon the reception of M-BA
  In case TIDs without BA agreement are aggregated
Setting rule for TID subfield in case of All ACK needs to be specified

## Slide 5: Proposed methods for TID indication in All ACK (1)
Option 1 - Setting TID value for All ACK to one of TIDs sent in the current A-MPDU under BA agreement
  Ambiguity occurs when TIDs without BA agreement are aggregated
Pros.:
  No additional TID value is necessary
  No change on current TID value setting method
Cons.:
  In case there is no TIDs with BA agreement, separate BA info. for each TID must be provided
TID0
MMPDU
No BA agreement
TID3
A-MPDU (AID:1)
TID2
AID:1
ACK type:0
TID:2 or 3
TID2
…
BA information for AID:1
BA info. for All ACK
TID2
AID:1
ACK type:0
TID:2
TID2
…

## Slide 6: Proposed methods for TID indication in All ACK (2)
Option 2 - Setting TID subfield to one of 1000-1110
  TID 1000-1111 is assigned for connection oriented service
    e.g., HCCA – not likely to be used for 11ax
    TID 1111 is already assigned for MMPDU ACK in 11ax
  Pros.
    Upon the reception of BA information with TID 1110, the originator doesn’t have to decode the rest of BA information fields
  Cons.
    Additional TID must be reserved for indicating all ACK
    May be awkward when A-MPDU consists of single TID
We prefer option 2
  Option 2 seems more definite and more efficient
TID0
MMPDU
No BA agreement
TID3
A-MPDU (AID:1)
TID2
AID:1
ACK type:0
TID:1110
TID2
…
BA information for AID:1
TID2
AID:1
ACK type:0
TID:1110
TID2
…

## Slide 7: Conclusion
In this contribution, we have discussed TID value for BA information in case of all ACK
Without proper TID value setting rule, originator may not distinguish single MPDU ACK and all ACK upon reception of M-BA
We propose to Set TID value of All ACK to one of values between 1000-1110

## Slide 8: Strawpoll
Do you agree to to adopt the spec text change as shown in doc 11/16-0917r1?

## Slide 9: Reference
[1] Draft P802.11ax_D0.2