## Slide 1: WUR-based Power Save Operations of AP
Date: 2016-07-25
Authors:

## Slide 2: Introduction
Power save modes of the IEEE 802.11 standard have focused on power save operations of non-AP STAs
AP is not allowed to enter power save mode to provide immediate network availability to STAs
However, power save operation of AP is getting important
  Mobile AP (Wi-Fi tethering) scenario [2][3]
  Standby power regulations of always-on network equipment [4][5]
Wake-up receiver-based power save operations would enable AP to efficiently minimize its standby power consumption while providing prompt network accessibility to STAs.

## Slide 3: Need for AP’s Power Saving: Mobile AP Scenario
Smartphone Wi-Fi tethering
  Smartphone connected to a cellular network while providing Wi-Fi connectivity to nearby Wi-Fi clients
  Measurements show excessive energy consumptions during Wi-Fi tethering
    Additional 260~820mW power consumed compared to Wi-Fi client mode [3]
Enable WUR-based power save operations on Mobile AP without no additional H/W cost
  Mobile AP (smartphone) may already have Wake-up receiver H/W since it usually operates as a STA

## Slide 4: Need for AP’s Power Saving: Energy Efficiency Requirements
Regulations/Incentive Programs for energy efficient AP
  Small network equipment like modems, routers, and access points present an huge opportunity for reducing nation-wide energy usages due to the large installed base of products and their always-on nature
  Governments are establishing standby power regulations of AP and certification programs to promote energy efficient AP [4~6]
Enable WUR-based power save operations on Static AP with addition of low-cost WUR
  The allowance power for energy efficient AP regulation/certification is hard to met by high performance APs without additional breakthrough

## Slide 5: Various Scenarios according to WUR capabilities
Power save operation scenarios according to WUR on STA/AP
  1: Wakeup Receiver on STA only (Main Scenario for initial WUR deployment)
    STA can enter WUR-based power save mode
  2: Wakeup Receiver on AP only (Mobile AP scenario)
    AP can enter WUR-based power save mode
  3: Wakeup Receiver on both AP and STA (General scenario when WUR becomes common)
    AP and STA can enter WUR-based power save mode
WUR’s scope should not be limited to the scenario 1
Flexible protocol design would enable widespread adoption of the technology in various scenarios
AP
STA
WUR ?
802.11 TR
802.11 TR
WUR ?
wakeup
packet
wakeup
packet
802.11 Transceiver
(can send wake-up packet)
Wake-up Receiver
or

## Slide 6: WUR-based Power Save Operations of both AP and STA
AP and STA may enter power save mode while its WUR on
Each AP/STA wakes up its 802.11 TR when
  its WUR receives Wake-up packet
  there is buffered traffic to send
wakeup delay
802.11
WUR
802.11
sleep
sleep
wake up signal
Backoff
Wake-up packet
WUR
802.11
Uplink
Data Exchange
Backoff
Wake-up packet
wakeup delay
sleep
sleep
802.11
Downlink
Data Exchange
sleep
sleep
AP
STA
WUR
802.11 TR
802.11 TR
WUR
wakeup
packet
wakeup
packet
or

## Slide 7: Conclusions
WUR would enable non-AP STAs to remain low-power state without sacrificing reachability
WUR would also enable AP to minimize its standby power while providing always-on network services in various scenarios:
  Mobile AP tethering scenario
  Meeting standby power regulations of network equipment
  IoT scenarios (e.g. Battery operated mobile gateway collecting IoT/Sensor data [7])
We propose that the scope of WUR should allow flexible protocol design that enables WUR-based power save operations of STA and/or AP.

## Slide 8: References
  [1] 11-16/0605r3, Proposal for LP-WUR Study Group
  [2] H. Han et al., “DozyAP: Power-Efficient Wi-Fi Tethering” ACM MobiSys ‘12
  [3] K.-H. Jung, et al., “Energy Efficient Wifi Tethering on a Smartphone” IEEE Infocom ‘14
  [4] US EPA Energy Star Small Network Equipment
  https://www.energystar.gov/products/office_equipment/small_network_equipment
  [5] EC Code of Conduct on Energy Consumption of Broadband Equipment
  http://iet.jrc.ec.europa.eu/energyefficiency/ict-codes-conduct/energy-consumption-broadband-communication-equipment
  [6] (EU) No 801/2013 amending Regulation (EC) No 1275/2008 with regard to ecodesign requirements for standby, off mode electric power consumption of electrical and electronic household and office equipment
  https://ec.europa.eu/energy/sites/ener/files/documents/Guidance%20document_Lot%2026_Networked%20Standby_clean%20FIN.pdf
  [7] 11-16/0974r0, WUR Usage Scenarios and Applications

## Slide 9: Appendix: ENERGY STAR SNE Program [4]
The US EPA ENERGY STAR program is defined for Small Network Equipment (SNE) like modems, routers, and access points.
For an Access Point product, to obtain Energy Star certification, it should limit its power to PBASE = PBASE +∑ PADD
  Base power allowance of (PBASE) to 2W.
  Each additionally implemented function would add power allowance (PADD).

## Slide 10: Appendix: EC CoC on Energy Consumption of Broadband Equipment [5]
The Code of Conduct sets out the basic principles to be followed by all parties involved in broadband equipment, operating in the European Community, in respect of energy efficient equipment.
  Idle state to reach max 2~3Watts power consumption targets