## Slide 1: Open Loop Spatial Multiplexing with Phase Hopping for 11ay
Date: 2016-07-25
Authors:

## Slide 2: Introduction
Several MIMO scenarios for 11ay have been proposed [1], and the contribution of [2] proposed open loop spatial multiplexing (OLSM) + PH(Phase Hopping) as OLSM and showed PER(Packet Error Rate) performance.
This presentation shows new simulation results in OLSM + PH with precoding and discusses benefit of precoding.

## Slide 3: SU-MIMO Scenario: Open Loop Spatial Multiplexing (OLSM) (1/2)
2-stream
Encoder
Spatial Multiplexing
or Pre-coder
RF
RF
2-stream
Decoder
Spatial De-Multiplexing
or Pre-coder decoding
RF
RF
    Two or more streams are transmitted by using spatial multiplexing to increase data throughput.
    2x2 OLSM MIMO system has 2 TX array antennas and 2 RX array/quasi-omni
    antennas.
    Introduction of interference cancellation in RX is possible.
    OLSM can operate with long range by including basic beamforming (BF) training.

## Slide 4: SU-MIMO Scenario: OLSM (2/2)
    Definition of OLSM:
    No Sounding except for BF
    - OLSM is one of suitable SU-MIMO scenarios at a mobile case.
    → In MIMO scenarios with sounding, performance becomes worse
    by feedback delay of sounding.
    OLSM uses predetermined or no precoding matrices.

## Slide 5: OLSM + PH [2]
Precoding + PH
Precoding
No precoding
Mapper
Pre-coder
Bit
-
inter
-
leaver
LDPC
Constellation in Precoding + PH
symbol
(Changes the phase in one of the antennas to randomize information and avoid destructive interference along a codeword)
(Linear combination of streams to increase diversity)
QPSK
After Precoding
PH
Precoding + PH
No Precoding + PH
PH
Precoding
-> This presentation focuses on Precoding + PH.

## Slide 6
LOS Model #1 [3]
    LOS model #1 is a line of sight which has a cross-link power attenuation[3]. Channel matrix of 2x2 MIMO systems in LOS (line-of-sight) model #1 is expressed as:
    where is phase of channel component between transmit antenna v and receive antenna u, and a is a power attenuation coefficient of cross-link terms.
    The LOS model #1 supposes that phases of channel components are independent random variables and uniformly distributed from 0 to 2p and phases of channel components are quasi-static parameters (i.e. Block fading (constant for each PPDU (PPDU length=8192 bytes))).
    The cross-link power attenuation coefficient a depends on the coupling between transmit antennas and the distance between transmit and receive antennas. The coefficient a has a range from 0 to 1.

## Slide 7
Benefits of PH (1/2)
s1(i)
s2(i)
Rx1(i)
Rx2(i)
In this case, received state of signal points falls into destructive interference (constellation degeneracy).
Transmitter
Receiver
symbol
symbol
#0
#1
#2
#0
#1
#2
r=2p*1/7
r=2p*2/7
r=2p*1/7
r=2p*2/7
Received state is static
*Note that this assumption is an example to help easy understanding of PH operation.
constellation degeneracy (9=16-7 signal points)
    The LOS model #1 supposes that phases of channel components are independent random variables and uniformly distributed from 0 to 2p and phases of channel components are quasi-static parameters (i.e. Block fading (constant for each PPDU (PPDU length=8192 bytes))).
    Ex.) Block fading with a=1 and = = = = 0 radian of
    channel matrix is assumed*.
    No precoding without PH:
S1(i) and S2(i) : QPSK

## Slide 8
Benefits of PH (2/2)
    No precoding with PH:
The receiver avoids falling into destructive interference (constellation degeneracy) in LOS environment by PH (scattering the channel phase).
    Circuit cost is negligible, because transmitter and receiver need to add only the phase changer.
s1(i)
s2(i)
Rx1(i)
Rx2(i)
Transmitter
Receiver
symbol
symbol
#0
#1
#2
#0
#1
#2
r=2p*1/7
r=2p*2/7
Received state is varying
PH
S1(i) and S2(i) : QPSK

## Slide 9: Performance in LOS model #1
Performance of precoding + PH in LOS model #1 are shown in Appendix, and it can be confirmed that:
Precoding+ PH has large gain, compared with no PH.
This presentation focuses on discussing effectiveness by introducing precoding.

## Slide 10: Vertical and Horizontal MIMO Architecture
The contribution of [3] discussed vertical and horizontal mapping.
    Vertical encoding
    Horizontal encoding
    - One encoder and one mapper
    => Setting one MCS is necessary
    - High speed encoder/decoder
    - Multiple encoder and multiple mapper
    => Setting multiple MCS is possible
    - Encoder/decoder has large complexity
-> Performances with vertical encoding are evaluated.

## Slide 11
UEP(unequal power) Environment
Two assumptions are considered.
A#1:
Considering individual difference of transmitter difference of antenna gain between 2 transmit antennas exists.
A#2:
Gain difference of two transmission beams exists.
Therefore, when employing MIMO+PH, transmission signals Tx1(i) and Tx2(i) are expressed as:
Precoding + PH
No Precoding + PH
PH
Precoding
Gain difference
Performance with vertical encoding when employing MIMO+PH is evaluated by simulation.

## Slide 12
LOS Model #2
    In LOS model #1, we add following scenarios (UEP: unequal power) [1]:
    Scenario 1:
    Considering individual difference of transmitter and so on, difference of antenna gain between 2 transmit antennas exists.
    Scenario 2:
    Considering individual difference of receiver and so on, difference of antenna gain between 2 receive antennas exists.
    Considering Scenarios 1 and 2, channel matrix of 2x2 MIMO systems in LOS model #2 is expressed as:
    where b is a coefficient of gain difference.
    The UEP coefficient b has a range from 0 to 1.
    Note that :
    For simplification of UEP performance evaluation, a is set to 0.

## Slide 13
Simulation Conditions
    MIMO : 2x2 OLSM precoding with PH/no precoding with PH
    Period of PH is 7.
    Modulation set : (BPSK, BPSK), (QPSK,QPSK),
    (16QAM,16QAM),(64QAM,64QAM)
    Channel model : LOS model #2
    a=0
    b=0dB, -5dB, -10dB (Coefficient of gain difference in transmitter and receiver)
    FEC : 11ad LDPC codes (Codeword size=672 bits)
    Detection : ML (Maximum Likelihood)
    ZF (Zero Forcing)
    MMSE (Minimum Mean Square Error)
    *Equation for precoding with PH is expressed as
    In UEP case, it is suitable to set to q to p/4 radian, because receivers can obtain equal power s1(i) and s2(i).

## Slide 14
Comparison between Precoding and no precoding (b=0dB)
  b=0dB => No gain difference (Equal power environment)
(BPSK, BPSK)
(QPSK, QPSK)
ML
MMSE
ZF

## Slide 15
Comparison between Precoding and no precoding (b=0dB)
ML
MMSE
ZF
(16QAM, 16QAM)
(64QAM, 64QAM)
    - In equal power case (b=0dB), performances with precoding (+PH) and with no precoding (+ PH) are close.

## Slide 16
Comparison between Precoding and no precoding (b=-5dB)
(BPSK, BPSK)
(QPSK, QPSK)
ML
MMSE
ZF

## Slide 17
Comparison between Precoding and no precoding (b=-5dB)
ML
MMSE
ZF
(64QAM, 64QAM)
(16QAM, 16QAM)

## Slide 18
Comparison between Precoding and no precoding (b=-10dB)
(BPSK, BPSK)
(QPSK, QPSK)
ML
MMSE
ZF

## Slide 19
Comparison between Precoding and no precoding (b=-10dB)
ML
MMSE
ZF
(16QAM, 16QAM)
(64QAM, 64QAM)

## Slide 20
Remark
In unequal power case:
When using MMSE and ZF, performance with precoding (+PH) is better than that with no precoding.
When using ML, performance with precoding (+PH) is better than that with no precoding except for low coding rate in (16QAM,16QAM) and (64QAM,64QAM)
When using vertical encoding, precoding + PH has advantage in unequal power case except for specific case as mentioned above.
Regarding simulation results, when using horizontal encoding, in order to employ 1 MCS for all spatial streams, introducing precoding is worthy.

## Slide 21
Summary
Precoding + PH has advantage at unequal power case, compared with no precoding with PH. Therefore, introducing precoding is worthy.

## Slide 22
Straw poll
  Do you agree to modify the following in clause 6.1 of the SFD:
  “For EDMG OFDM mode, the 11ay specification shall define SU EDMG PPDU transmission with and without phase hopping. An EDMG STA may support transmission and reception of SU EDMG PPDU with phase hopping. In this mechanism, the following apply:
  - Precoding may be used
  - The period of phase hopping is TBD.”

## Slide 23
References
11-15-0334-01-ng60-mimo-framework
11-16-0669-01-00ay-open-loop-spatial-multiplexing-with-phase-hopping-for-11ay
11-16-0388-00-00ay-performance-analysis-of-open-loop-su-mimo-receivers-for-ieee-802-11ay

## Slide 24
Appendix

## Slide 25
Simulation Conditions
    MIMO : 2x2 OLSM + precoding with PH/without PH
    Period of PH is 7*.
    Modulation set : (BPSK,BPSK),(QPSK,QPSK),
    (16QAM,16QAM)(64QAM,64QAM)
    Channel model : LOS model #1
    a=-3dB, -5dB, -10dB
    (Power attenuation coefficient of cross-link terms)
    FEC : 11ad LDPC codes (Codeword size=672 bits)
    Detection : ML (Maximum Likelihood)
    ZF (Zero Forcing)
    MMSE (Minimum Mean Square Error)
    *Equation for precoding with PH is expressed as

## Slide 26
(BPSK,BPSK),(QPSK,QPSK)

## Slide 27
(QPSK, QPSK)
Comparison between PH and no PH (R=1/2)
(BPSK, BPSK)
a=-5dB
a=-10dB
- In (BPSK,BPSK), PH has gain, compared with no PH when using ML and MMSE.

## Slide 28
Comparison between PH and no PH (R=5/8)
(BPSK, BPSK)
(QPSK, QPSK)
a=-5dB
a=-10dB

## Slide 29
Comparison between PH and no PH (R=3/4)
(BPSK, BPSK)
(QPSK, QPSK)
a=-5dB
a=-10dB

## Slide 30
Comparison between PH and no PH (R=13/16)
(BPSK, BPSK)
(QPSK, QPSK)
a=-5dB
a=-10dB
- PH has gain, compared with no PH when using ZF and MMSE and ML.

## Slide 31
(16QAM,16QAM),(64QAM,64QAM)

## Slide 32
Comparison between PH and no PH (R=1/2)
(16QAM, 16QAM)
(64QAM, 64QAM)
a=-5dB
a=-10dB

## Slide 33
Comparison between PH and no PH (R=5/8)
(16QAM, 16QAM)
(64QAM, 64QAM)
a=-5dB
a=-10dB

## Slide 34
(16QAM, 16QAM)
a=-5dB
a=-10dB
Comparison between PH and no PH (R=3/4)
(64QAM, 64QAM)

## Slide 35
Comparison between PH and no PH (R=13/16)
(16QAM, 16QAM)
(64QAM, 64QAM)
a=-5dB
a=-10dB
- PH has gain, compared with no PH.

## Slide 36
a=-3dB

## Slide 37
Comparison between PH and no PH (a=-3dB, R=1/2)
(BPSK,BPSK)
(QPSK,QPSK)
(16QAM,16QAM)
(64QAM,64QAM)

## Slide 38
Comparison between PH and no PH (a=-3dB, R=5/8)
(64QAM,64QAM)
(BPSK,BPSK)
(QPSK,QPSK)
(16QAM,16QAM)

## Slide 39
Comparison between PH and no PH (a=-3dB, R=3/4)
(BPSK,BPSK)
(QPSK,QPSK)
(16QAM,16QAM)
(64QAM, 64QAM)

## Slide 40
Comparison between PH and no PH (a=-3dB, R=13/16)
- In a=-3dB, PH has large gain, compared with no PH.
(BPSK,BPSK)
(16QAM,16QAM)
(64QAM,64QAM)
(QPSK,QPSK)