## Slide 1: Input on WUR PAR Scope
Date: 2016-07-25
Authors:

## Slide 2: Abstract
The purpose of this presentation is to provide some thoughts on the Scope of the PAR for the wake-up receiver (WUR) project

## Slide 3: New PHY
We will need to develop a new PHY
The PHY has to be compatible with an ultra-low power wake-up Receiver (WUR)
We will not specify the exact receiver but the active receive power consumption must be in the range of hundreds of microwatts not in the range of tens or hundreds of milliwatts
Proposed Text
Specifies a PHY, which is compatible with an ultra-low power wake-up receiver with active receiver power consumption of several hundred microwatts.

## Slide 4: Payload
The WUR is intended to provide control function like waking up a STA or a group of STAs
This WUR is not intended to carry data
Keep the scope of it functionality simple and clean
Proposed Test
Specifies MAC frames that carry paging and related control information

## Slide 5: Frequency Band
We do not want to have to add an antenna to a low-power IoT device
Hence the WUR should operate in the same band as the primary 802.11 STA with which it is paired, so it can share the same antenna
Most popular frequency bands are 2.4 GHz and 5 GHz
  Focus on most popular bands: 2.4 GHz and 5 GHz
  Design can be expanded in the future to other bands like sub-1 GHz
Proposed Text
Operates in the 2.4 GHz and 5 GHz frequency bands.

## Slide 6: Range
It is important that the WUR supports the same range as the primary 802.11 STA with which it is paired
Low-power IoT devices use a variety of 802.11 technologies including 802.11n and for low data rate applications 802.11b
Need to match the range of these 802.11 technologies
Proposed Text
Provided similar or better range compared to legacy 802.11 stations

## Slide 7: Coexistence
The WUR must coexist with the 802.11 devices operating in the bands that they share
Proposed Text
Supports coexistence mechanisms with legacy 802.11 stations

## Slide 8: Summary
Specifies a PHY, which is compatible with an ultra-low power wake-up receiver with active receiver power consumption of several hundred microwatts.
Specifies MAC frames that carry paging and related control information
Operates in the 2.4 GHz and 5 GHz frequency bands.
Provided similar or better range compared to legacy 802.11 stations
Supports coexistence mechanisms with legacy 802.11 stations