## Slide 1: Wake-Up Receiver Usage Scenarios and Applications
Date: 2016-07-25
Authors:
July 2016
Shahrnaz Azizi, etc., Intel Corporation

## Slide 2: Abstract
This presentation summarizes applications and usage scenarios for consideration in the development of requirements in WUR SG.
July 2016
Shahrnaz Azizi, etc., Intel Corporation

## Slide 3: Background
With duty-cycled operation, low power consumption and low latency are conflicting goals
  To increase battery life, a device needs to sleep more  increased latency
  To receive data with low latency, a device needs to sleep less  shorter battery life
Low latency
(but short battery life)
Long battery life
(but long latency)
Sleep less
Sleep more
Goal
latency
battery
life
July 2016
Shahrnaz Azizi, etc., Intel Corporation

## Slide 4: Problem: Internet-of-Things (IoT) Use Case
Today without Low Power Wake-up Receiver (WUR)
  User cannot access the IoT device while the IoT device is off to save power
IoT device
Access Point
Access Point
Configuration change command
(e.g. collect data every 10 min)
Internet
User
command
Waits until IoT device wakes up
(worst case = 1 hour)
OFF
(wakes up every 1 hour)
ON
July 2016
Shahrnaz Azizi, etc., Intel Corporation

## Slide 5: WUR Solution: IoT Use Case
Proposed scheme using WUR
  User can access the IoT device with low latency and the IoT device can have long battery life
WUR has very low power consumption (<100 µW). It is a companion radio for 802.11, but not used for user data.
IoT Device
Access Point
Access Point
Configuration change command
(e.g. collect data every 10 min)
Internet
User
command
Wake-up Packet
OFF
ON
(wakes up every 1 hour)
July 2016
Shahrnaz Azizi, etc., Intel Corporation

## Slide 6: Usage Model 1: Quick Message/Incoming Call Notification Scenario
(1) Without WUR
or
Sleep/wake periodically
Internet
message
AP buffers data until the client wakes up
Main radio needs to wake up periodically to receive a notification within a latency requirement
or
message
802.11
(2) With WUR
Internet
message
message
Wake-up packet
+
or
Sleep until wake-up packet is received
Wake-up upon reception of wake-up packet and receive message
802.11+LP-WUR
July 2016
Shahrnaz Azizi, etc., Intel Corporation

## Slide 7: Usage Model 2: Quick Status Query/Report, Configuration Change Scenario
(1) Without WUR
(2) With WUR
AP
Sleep/wake periodically
Internet
Status query command
Status query command
IOT device
802.11
AP buffers data until the IOT device wakes up
Configuration change command
or
IOT device
802.11+LP-WUR
AP
Sleep
Internet
Wake-up packet
Status query command
Status query command
+
Status report
Configuration change command
or
July 2016
Shahrnaz Azizi, etc., Intel Corporation

## Slide 8: Usage Model 3: Quick Emergency/Critical Event Report Scenario
(1) Without LP-WUR
(2) With LP-WUR
Mobile gateway
(battery operated)
Internet
IOT/sensor device
802.11
Mobile gateway sleeps for a long period of time to save power
Emergency event happens but cannot report until the mobile gateway wakes up from the sleep state
or
Mobile gateway
(battery operated)
Internet
IOT/sensor device
802.11
Mobile gateway sleeps for a long period of time until it receives a wakeup packet from the sensor device
Emergency event happens and reports the event to the mobile gateway with low-latency
or
Event report
Wakeup packet
+
Event report
Sleep
Sleep/wake periodically
802.11
802.11 + LP-WUR
Shahrnaz Azizi, etc., Intel Corporation

## Slide 9: Summary and the Next Step
We presented a few use cases for WUR where low power consumption and low latency at the same time are enabled.
Translate these into requirements that can be captured in the PAR and CSD.
July 2016
Shahrnaz Azizi, etc., Intel Corporation