## Slide 1: EDMG Header Encoding and Modulation
Date: 2016-07-26
Authors:

## Slide 2: Abstract
This submission is about EDMG Header-A modulation
We present the details of the modulation
We will present some initial simulation results

## Slide 3: Introduction
The EDMG Header-A carries the information about EDMG PPDU.
This contribution proposes an EDMG Header-A modulation and presents preliminary results

## Slide 4: 11ay Frame Format
L-STF | L-CEF | L-Header | EDMG-Header-A | EDMG-STF | EDMG-CEF | EDMG-Header-B | Data | AGC | TRN
Field | Description
L-STF | Non-EDMG Short Training field
L-CEF | Non-EDMG Channel Estimation field
L-Header | Non-EDMG Header field
EDMG-Header-A | EDMG Header A field
EDMG-STF | EDMG Short Training field
EDMG-CEF | EDMG Channel Estimation field
EDMG-Header-B | EDMG Header B field
Data | The Data field carries the PSDU(s)
AGC | Automatic Gain Control field
TRN | Training sequences field
Table 1—Fields of the EDMG PPDU

## Slide 5: EDMG Header-A Content (SU)
Field | # of bits | Start bit | Description
BW | 6 | 0 | Set to the indexing value corresponding to a specific bandwidth type (2.16, 4.32, 6.48. 8,64, 2.16+2.16GHz) and a specific primary channel allocation
EDMG-MCS-SS1 | 6 | 6 | Contains an EDMG MCS index used for SS1
EDMG-MCS-SS2 | 6 | 12 | Contains an EDMG MCS index used for SS2
EDMG-MCS-SS3 | 6 | 18 | Contains an EDMG MCS index used for SS3
EDMG-MCS-SS4 | 6 | 24 | Contains an EDMG MCS index used for SS4
EDMG-MCS-SS5 | 6 | 30 | Contains an EDMG MCS index used for SS5
EDMG-MCS-SS6 | 6 | 36 | Contains an EDMG MCS index used for SS6
EDMG-MCS-SS7 | 6 | 42 | Contains an EDMG MCS index used for SS7
EDMG-MCS-SS8 | 6 | 48 | Contains an EDMG MCS index used for SS8
GI/CP Length | 2 | 54 | Normal/Short/Long/Reserved GI/CP
PSDU Length | 22 | 56 | Indicates the length of the EDMG PSDU in octets.
Beamformed | 1 | 78 | If set to 1, indicates that per-carrier beamforming is used.
TxEVM | 3 | 79 | Indicates how much the Tx EVM is better than the minimum required.
Reserved | 30 | 82 | Set to 0
CRC | 16 | 112 | 

## Slide 6: EDMG Header-A Modulation options
EDMG Header-A is transmitted in CB1 mode, following L-Header and duplicated over all bonded channels.
It was suggested by to use same encoding and modulation as L-Header, but without the repetition.
  Such a method, reuses the existing HW and supports 112bits in two FDE symbols.
  Efficiency is improved if we limit to one symbol, but 48bits are not enough.
  Using MCS1 doesn’t provide enough coding gain for the header compared to data.

## Slide 7: Encoding and Modulation

## Slide 8: Performance
Floating point simulation, AWGN, no analog impairments

## Slide 9: Summary
In this presentation we presented the design of EDMG Header-A encoding and modulation
Suggested designs benefits
  Supports 112 payload bits + 16 CRC bits
  Full reuse of L-Header LDPC encoder and decoder
  Full reuse of L-Header modulation and demapping (except the duplication used for L-Header)
Performance results for EDMG Header-A show expected performance (3dB less than L-Header), with about 3dB margin relative to MCS1

## Slide 10: Strawpoll
Insert in the SFD: “EDMG-Header-A is two DMG SC symbols long comprising of 112 data bits followed by a 16 bit CRC. The EDMG-Header-A is transmitted as follows:
- The CRC is the same CRC as that of the header of the DMG SC mode
- First 64 bits and second 64 bits are each encoded and modulated as specified in steps 1-5 in section 20.6.3.1.4 (Header encoding and modulation). Restricting to steps 1-5 means that the symbol is not duplicated to the second symbol as in DMG.
- GI is added after each SC block (same as for DMG SC mode)
Processing is illustrated in Slide 7

## Slide 11: References
11-15-1358-04-00ay-specification-framework-for-tgay